## Slide 1: BCS Level 4 Certificate in Network Systems and Architecture
NSaA-QAN_60305472
2 – Storage Protocol Failures

## Slide 2: 2. Storage Protocol Failures

## Slide 3: What is a storage protocol?
A protocol specific to a technology
Mainly used in cloud applications
Most storage networks use the SCSI protocol for communication between servers and disk drive devices

## Slide 4: Small Computer System Interface (SCSI)
In use since the early 1980’s and was originally used to move data within a single server
Dominant block level access method for disk in the data centre
Still widely used in its native format but it has also been encapsulated into other protocols for use within storage networks for consolidated storage

## Slide 5: Fibre Channel (FC)
Designed to extend the functionality of SCSI into point-to-point, loop, and switched topologies
FC encapsulates SCSI data and Command Descriptor Blocks (CDB) into the payload of Fibre Channel frames
Fibre Channel networks provided the addressing, routing, and flow-control required to support SCSI data
Designed to meet the needs of SCSI by providing ‘lossless’ in order delivery
  This means that in a stable network FC frames will not be dropped
  Delivered in order ensuring that the Upper Layer Protocols (ULP) will not be forced to reorder or resend frames
Typically carried over fiber-optic links on dedicated infrastructures
Traditionally built-in pairs as exact mirrors of one another
FC networks come in 1/2/4/8 Gbps speeds with 16/32 Gbps in the works

## Slide 6: internet/IP Small Computer System Interface (iSCSI)
Typically uses TCP ports 860 and 3260
iSCSI takes SCSI data and CDBs and places it in the payload of IP packets
Allows the SCSI protocol to be extended across existing IP infrastructure
Has not gained the required market share
The problem with iSCSI from a protocol standpoint is that it takes the SCSI protocol which expects lossless, in-order delivery, and places it in TCP/IP packets which are designed to support heterogeneous WAN networks and experience packet loss and out-of-order delivery frequently

## Slide 7: Fibre Channel over Ethernet (FCoE)
Ratified in 2009 and provides the functionality for moving native Fibre Channel across consolidated Ethernet networks
FCoE encapsulates full Fibre Channel frames inside Ethernet Jumbo Frame payloads
FCoE does not modify the existing Fibre Channel protocol suite

## Slide 8: Common Internet File System (CIFS)
CIFS is a file based storage system based on Server Message Block (SMB)
This is a shared storage protocol typically used in Microsoft environments for file sharing
Windows-based file shares rely on CIFS as the transfer protocol of the file level data
File based storage relies on an underlying files system such as FAT32, XFS, NTFS
  block based storage does not

## Slide 9: Network File System (NFS)
File based storage protocol
NFS is traditionally used in Linux and Unix environments
NFS is also a widely used protocol for VMware environments and can offer several benefits for virtual machine storage
As a file based storage protocol NFS experiences many of the same limitations as stated for CIFS

## Slide 10: Hyper Text Transfer Protocol (HTTP) and others
When the cloud discussion leaves the data centre (private/internal cloud) and moves up to the service provider level such as Google, Amazon, or the TelCos, the protocols listed above may not have the necessary scalability
Protocols such as HTTP based storage are being used to simplify storage configuration and increase its scalability

## Slide 11: Failures
Disk failure
  This type of failure is triggered by failure mechanisms of disks
  Imperfect media, media scratches caused by loose particles, rotational vibration, and many other factors internal to a disk can lead to this type of failures
  Sometimes, the storage layer proactively fails disks based on statistics collected by on-disk health monitoring mechanisms - e.g., a disk has experienced too many sector errors
Physical interconnect failure
  This type of failure is triggered by errors in the networks connecting disks and storage heads
  It can be caused by host adapter failures, broken cables, shelf enclosure power outage, shelf backplanes errors, and/or errors in shelf FC drivers
  When physical interconnect failures happen, affected disks appear to be missing from the system

## Slide 12: Failures
Protocol failure
  This type of failure is caused by incompatibility between protocols in disk drivers or shelf enclosures and storage heads and software bugs in the disk drivers
  When this type of failure happens, disks are visible to the storage layer but I/O requests are not correctly responded by disks
Performance failure
  This type of failure happens when the storage layer detects that a disk cannot serve I/O requests in a timely manner while none of previous three types of failures are detected
  It is mainly caused by partial failures, such as unstable connectivity or when disks are heavily loaded with disk-level recovery (e.g., broken sector remapping)

## Slide 13: Locally Attached Storage Protocol Failures
Storage protocol failures
  SATA
  SCSI
  SAS
hardware failure - loss of access to local disk(s) and / or corruption of data

## Slide 14: Causes and Impact of Failures of RAID
Raid 0
  Uses striping
  Maximise parallelism
  No redundancy
  No error correction
  No fault tolerance
  Only use 50%
  NO drive can fail
RAID 1
  Uses mirroring
  Redundant data
  Fault tolerant
  Most common form
  One drive can fail
Raid 5
  Uses block-level striping
  Rotating parity array
  Error correction takes place in same disks as data storage
  Parallelism, better performance than RAID 4
  Single drive failure
RAID 10
  Mirroring AND striping at same time
  Minimum of 4 disks (have to be even amount)
  Fault tolerance
  Very high performance
  Only use 50%
  2 drives can fail (one in each mirrored pair)

## Slide 15: Causes and Impact of Failures of RAID
Loss of single / multiple disks
  reduced throughput
  loss of data depending on RAID
Level and number of disk failures
  See previous slide
Loss of RAID controller
  permanent / temporary loss of access to data

## Slide 16: Failures of network shares
Usually caused by network card drivers
  Use proprietary driver, not windows version
Anti-virus programs
ACL issues
DNS issues in AD
Misconfigured firewall or protocols (NFS, SMB, TCP/IP, AFS)
  complete loss of access to NAS
Misconfigured NFS
  loss of access for Linux / NAS network shares
Misconfigured SMB
  loss of access to Windows network shares
Misconfigured AFS
  loss of access for Apple systems shares
Misconfigured authentication and/or authorisation
  loss of access to some / all NAS / network shares

## Slide 17: Storage Area Network (SAN) failures
A Storage Area Network (SAN) is a specialized, high-speed network that provides block-level network access to storage
SANs are typically composed of hosts, switches, storage elements, and storage devices that are interconnected using a variety of technologies, topologies, and protocols
SANs may also span multiple sites
SANs are often used to:
  Improve application availability (e.g., multiple data paths)
  Enhance application performance (e.g., off-load storage functions, segregate networks, etc.)
  Increase storage utilization and effectiveness (e.g., consolidate storage resources, provide tiered storage, etc.), and improve data protection and security
  SANs also typically play an important role in an organization's Business Continuity Management (BCM) activities

## Slide 18: Storage Area Network (SAN) failures
SANs are commonly based on Fibre Channel (FC) technology that utilizes the Fibre Channel Protocol (FCP) for open systems and proprietary variants for mainframes
The use of Fibre Channel over Ethernet (FCoE) makes it possible to move FC traffic across existing high speed Ethernet infrastructures and converge storage and IP protocols onto a single cable
Single misconfigured or failed Fibre switch
  Increased load on remaining switches and possible reduced throughput and/or storage outage
  The standard data network is unaffected;
Loss of all Fibre switches
  Complete loss of access to storage
  The standard data network is unaffected
Failure of a single host bus adapter (HBA)
  Increased load on remaining HBA on a single node and possible reduced throughput for this node or complete outage if this is the only on-board HBA

## Slide 19: Failures of network shares
2.4 Explain causes and consequences of storage area network (SAN) failures over the Fibre Channel protocol and summarise the appropriate response for each.
    single misconfigured or failed Fibre switch - increased load on remaining switches and possible reduced throughput and/or storage outage. The standard data network is unaffected;
    loss of all Fibre switches - complete loss of access to storage. The standard data network is unaffected;
    failure of a single host bus adapter (HBA) - increased load on remaining HBA on a single node and possible reduced throughput for this node or complete outage if this is the only onboard HBA.

## Slide 20: Fibre Channel

## Slide 21: Fibre Channel over Ethernet (FCoE)
The FC SAN physical components such as network cables network adapters and hubs or switches can be used to design a Fibre channel Storage Area Network
The different types of FC architecture which can be designed are:
  Point-to-point
    two nodes are connected directly to each other
  Fibre channel arbitrated loop (FC-AL)
    the devices are attached to a shared loop
  Fibre channel switched fabric (FC-SW)
    a single FC switch or a network of FC switches (including FC directors) to interconnect the nodes

## Slide 22: Basic troubleshooting tips for Fibre Channel (FC) SAN issues
Always take backup of Switch Configurations
Troubleshooting Connectivity Issues
  Fcping - an FC version of the popular IP ping tool
  Fctrace - traces a route/path to an N_Port
Things to check while troubleshooting Zoning
  Are your aliases correct ?
  If using port zoning, have your switch domain IDs changed ?
  If using WWPN zoning, have any of the HBA/WWPNs been changed ?
  Is your zone in the active zone set?
Rescan the SCSI Bus if required
Understanding Switch Configuration Dumps
Use Port Error Counters

## Slide 23: SAN failures over Fibre Channel over Ethernet (FCoE)
Single misconfiguration or failed standard switch
  Increased load on remaining switches and possible reduced throughput or storage outage
  The standard data network may also be impacted
TCP/IP misconfiguration
  Inability for some / all nodes to access storage
Failure of a single network interface controller (NIC)
  Increased load on remaining NIC on a single node and possible reduced throughput for this node or complete outage if this is the only on-board NIC
Incorrect / invalid logical unit number (LUN)
  Inability to access logical storage device
Loss of network
  Total outage

## Slide 24: SAN failures over the iSCSI
Single misconfiguration or failed standard switch
  Increased load on remaining switches and possible reduced throughput or storage outage
  Standard data network may also be impacted
TCP/IP misconfiguration
  Inability for some / all nodes to access storage
Failure of a single NIC
  Increased load on remaining NIC on a single node and possible reduced throughput for this node or complete outage if this is the only on-board NIC
Incorrect / invalid iSCSI qualified name (IQN) address
  Inability to access logical storage device

## Slide 25: Cloud Storage Failures
Router / ISP failure
  Complete loss of access
TCP/IP misconfiguration
  Inability for some / all nodes to access storage
Misconfigured authentication / authorisation
  Loss of access to some / all cloud storage
Cloud service provider failure
  Loss of access to data and / or loss of data
Data read, disk, or server failures
  Basically corrupt data or failing hardware