## Slide 1: Operating Systems and Architecture
(UFCFCU-30-1)
<digital logic>

## Slide 2
After completing this section of the module you will be able to:
  Describe and explain computer architecture, digital logic and machine level representation of data (number systems)
  digital logic
  static and dynamic digital systems
<outcomes>

## Slide 3
  At the end of the last session we looked at logic functions
  In this session we see how these are implemented in hardware and used for arithmetic and logic
<logic>
OR |  | 
A | B | Output
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
AND |  | 
A | B | Output
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
NOT | 
A | Output
0 | 1
1 | 0
XOR |  | 
A | B | Output
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 4
  The components are called gates, their output value depends on the input values
  This is a one transistor NOT gate
<not gate>
NOT | 
A | Output Q
0 | 1
1 | 0
Notes: We forget about transistors now (this isn’t an electronics course) and introduce our first example of abstraction – the logic gate diagram. Abstraction – making a model that can be reused without having to rewrite all the detail.

## Slide 5
  This is an AND gate
<and gate>
AND |  | 
A | B | Output Q
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1

## Slide 6
  This is an OR gate
<or gate>
OR |  | 
A | B | Output Q
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1

## Slide 7
  This is an XOR (exclusive or) gate
<xor gate>
XOR |  | 
A | B | Output Q
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 8
Rule of addition
0+0 = 0
1+0 = 1
1 +1 = 0 and carry 1 The XOR gate handles the addition
The AND gate handles the carry
This is only a half adder as it does not handle a carry in
<half adder>

## Slide 9
Rule of addition
0+0 = 0
1+0 = 1
1 +1 = 0 and carry 1
<full adder>
Notes: Get the students to come up to the board and draw the inputs and outputs to each gate to show how it works.

## Slide 10
Simplify the diagram
<full adder>
Full adder
Cin
Carry out
A
B
S

## Slide 11
<4 bit adder>
Chain 4 full adders to make a 4 bit adder
Similarly, chain 32 full adders to make a 32 bit adder
If the last adder produces a carry out of 1, then we have run out of bits!
Full adder
Cin
A0
B0
S0
Full adder
A1
B1
S1
Full adder
A2
B2
S2
Full adder
A3
B3
S3
Cout
Notes: Ask them what do we do when we get a final carry out bit?

## Slide 12
<4 bit subtraction>
For subtraction we need to flip the bits and add 1
We could build a separate unit for subtraction
But there is a way to use the full adder
To add 1 we can just force the first Cin to be 1
To flip the bits we could use a NOT gate
But we need to control whether we are adding or subtracting
Full adder
Cin
A0
B0
S0
Full adder
A1
B1
S1
Full adder
A2
B2
S2
Full adder
A3
B3
S3
Cout

## Slide 13
Use an XOR gate and a control signal
The XOR gate is added to all B inputs on a multibit adder
This is the first stage
<1 bit subtraction>
Full adder
Control
0 = +
1 = -
Carry out
A
B
Result
Notes: Again, get them to come to the white board and show how this works with the combination of inputs

## Slide 14
So far:
We have a unit that can add and subtract
We have introduced the concept of control
Where do the inputs come from and where does the output go?
We need to store data
<progress>

## Slide 15
Gates can be connected to form flip flops
  Devices which retain a state until flipped into another state
The D type flip flop
  Data appears on input D
  CK is a clock input
  The value on D will only change when the clock value is 1
  Therefore the value of D is stored until there is a clock signal
<flip flop>
Notes: Another white board challenge!

## Slide 16
Series of D type flip flops can form registers
  The fastest form of storage
  Integrated into the CPU
Used to:
  Hold data values
  Hold addresses
  Hold status
  Hold instructions
<registers>

## Slide 17
<registers>
Full adder
Full adder
Two bit adder
  Both numbers to be added appear on D0 - D3
  When CP is 1, the data is clocked into the adders and the result is available at the output
  The clock is required to time and control all the functions

## Slide 18
Arrays of D type flip flops are called SRAM
RAM for Random Access Memory
S for static
  So long as power is applied, SRAM will retain its value, it does not need to be refreshed
  This means all accesses are for required functions, and are not overhead
<sRAM>

## Slide 19
A bitwise AND takes two equal-length binary values and performs the logical AND operation on each pair of the corresponding bits
A bitwise OR takes two equal-length binary values and performs the logical OR operation on each pair of the corresponding bits
<bitwise AND OR>
 | 0 | 0 | 1 | 1
AND | 0 | 0 | 1 | 0
 | 0 | 0 | 1 | 0
 | 0 | 0 | 1 | 0
OR | 1 | 0 | 0 | 0
 | 1 | 0 | 1 | 0

## Slide 20
Bitwise operations are very common and implemented in hardware
  A collection of AND and OR gates
  These examples are for 32 bits
<bitwise AND OR hardware>

## Slide 21
These units are combined with the adder to form a 32 bit ALU Arithmetic Logic Unit
<ALU>

## Slide 22
We need one more component – the multiplexor
  Selects an input to go to the output depending on the value of the control
<multiplexor>

## Slide 23
We use two multiplexors to select the outputs from the 3 units
  When c0=0, the AND OR result is A AND B, and the ADDSUB result is A + B.
  When c0=1, the AND OR result is A OR B, and the ADDSUB result is A - B.
<ALU>
Notes: Last whiteboard challenge

## Slide 24
The 32 bit ALU has 32 wires in parallel coming from the registers and leaving the unit.
This is shown in shorthand as:
These wires are called a bus, as they transport data
<bus>
32

## Slide 25
The values in the registers are constantly changing as operations occur
Inputs and results have to be stored
  A data bus connects the registers to DRAM
  A special register, the program counter, holds the address of the next value to be retrieved from memory and transfers it on the address bus
<DRAM>
ALU
Registers
RAM
32
32
32
PC
16
32

## Slide 26
DRAM - dynamic random access memory
SRAM - static random access memory
Refresh needs the stored values to be read and rewritten frequently
<DRAM v SRAM>
Characteristic | SRAM | DRAM
Speed | Faster | Slower
Size | Small | Large
Cost | Expensive | Cheap
Use | Registers, cache | Main memory
Density | Less dense | Highly dense
Construction | Complex | Simple
Transistors per bit | 6 | 1
Charge leakage | None | Exists, requires refresh
Power consumption | Low | High
Notes: More on this on day 4.

## Slide 27
Transistors can be used to form gates
AND, OR, XOR and multiplexors can be used to form units capable of mathematical and logical operations on bits
Date can be moved around units on buses
A clock signal can control operations
Data can be stored in SRAM and DRAM
<Conclusion>