## Slide 1: Operating Systems and Architecture
(UFCFCU-30-1)
<computer architecture>

## Slide 2
After completing this section of the module you will be able to:
  Explain the relationships between hardware components and the subsystems used in a computer system.
  This section will examine hardware. Operating system I/O will be covered on day 11
  Programmed I/O
  Interrupt driven I/O
  Direct Memory Access (DMA)
  Serial and parallel buses
  PCIe
  Adapters
  GPUs
<outcomes>

## Slide 3
Trends in I/O systems
  Improving processing efficiency
  Moving functions into the CPU, ultimately SOC
  Moving processing power into the adapters, offloading the CPU
  Replacing parallel buses with serial
  Point to point replacing sharing
  Continuous performance improvements
<trends>

## Slide 4
Methods of programming I/O
  Programmed I/O
    CPU controls all activities
  Interrupt driven I/O
    CPU initiates all activities
  Direct memory access
    Activities offloaded to adapters
<programming I/O>
Notes: This is part of the trend to improve processing efficiency

## Slide 5
Programmed I/O
    Already seen in the RISC simulator
    INP R0,2
    INP R1,2
    ADD R2,R1,R0
    OUT R2,4
    HLT
    Each I/O data transfer requires a CPU instruction
    Used for PS/2 keyboard and mouse
    Still in use where high data rates not required, such as embedded systems
<programmed I/O>
PIO instructions
PIO instruction

## Slide 6
Raspberry Pi GPIO (general purpose input/output)
Example Python program for LED on pin 18
import RPi.GPIO as GPIO import time GPIO.setmode(GPIO.BCM) GPIO.setwarnings(False) GPIO.setup(18,GPIO.OUT) print "LED on" GPIO.output(18,GPIO.HIGH) time.sleep(1) print "LED off" GPIO.output(18,GPIO.LOW)
<programmed I/O>

## Slide 7
Code to detect button push – no interrupt
Polls the button status every 0.1 second
Why is this bad?
pressed = False
while True:
# button is pressed when pin is LOW
if not GPIO.input(BUTTON_GPIO):
if not pressed:
print("Button pressed!")
pressed = True
# button not pressed (or released)
else:
pressed = False
time.sleep(0.1)
<polling>
Notes: Nobody uses this if they can avoid it.

## Slide 8
Code to add an interrupt and handler
Why is this better?
def button_callback(channel):
if not GPIO.input(BUTTON_GPIO):
print("Button pressed!")
else:
print("Button released!")
GPIO.add_event_detect(BUTTON_GPIO, GPIO.BOTH,
callback=button_callback, bouncetime=50)
<interrupt>
Notes: What is that bounce time about? Debounce in keyboards? Or is that done in hardware?
Bouncetime is the minimum time between interrupts – anything less than this e.g. a key bounce will be ignored, avoids multiple key presses when there was only one.

## Slide 9
PIO is not efficient for large or high rate data transfers
DMA (Direct Memory Access) offloads the CPU from reading and writing between devices and memory
Typically the CPU will issue
  a count of the data to be transferred
  the memory address
  the address of the I/O device
  if it is a read or a write
The DMA controller will then carry out the transfer and interrupt the CPU when it is complete, of if it needs another block of data
Used in disk controllers, network, graphics and sound adapters
<DMA>

## Slide 10
DMA takes control of the bus during transfer
  If the CPU requires the bus, it has to wait for 1 data block (word)
  This is not an interrupt
  Effect is CPU executing more slowly during DMA transfers, but not much
<DMA>
Bridge
Memory
I/O
CPU
DMA read
What is the purpose of the bridge?
What is a word?
Notes: This should lead to a discussion about bus speeds
Direct Memory Access
Smallest accessible unit in memory is called a word

## Slide 11
PC architecture (c 2000)
Why are there 2 bridges?
Why are the I/O devices organised this way?
What does each bus do?
Which buses are serial and which are parallel?
<Computer architecture>
Notes: More discussion about speeds and data rates.

## Slide 12
Parallel bus
If run at the same clock speed, it is 8 times as fast as a serial bus
Issues:
  Clock skew
  Crosstalk
  What are these?
<parallel bus>
Transmitter
Receiver
D0
D1
D2
D4
D3
D5
D6
D7
1-byte parallel bus
8 bits transferred at once
Notes: Also issues with reflections. Crosstalk and skew get worse with length. On motherboards if the bus has a bend, the outside path is longer than the inner path creating skew.

## Slide 13
Serial bus
If run at the same clock speed, it is 8 times slower than a parallel bus
Advantage:
  Smaller
  Less crosstalk
  Cheaper
  Longer
<serial bus>
Transmitter
Receiver
D0
D1
D2
D4
D3
D5
D6
D7
1-bit serial bus
1 bit transferred at a time

## Slide 14
Ethernet, HDMI, USB, PCIe, DMI serial buses use differential signalling
  Uses 2 wires (e.g. twisted pair)
  Receiver only detects difference between signals, therefore eliminating noise on both wires
  Low voltage more susceptible to noise
  In single ended
    Vsupply – Vground = Vsupply
  In differential
    The low state is not ground, but – Vsupply
    So difference is Vsupply – (-Vsupply) = 2Vsupply
    Giving double the noise immunity
<differential signalling>
Notes: Very important on motherboards where Vsupply less than 2V

## Slide 15
Serial has become cheaper over time
Serial can be clocked faster than parallel
What has replaced these parallel interfaces?
  IEEE 1284
  PATA
  SCSI
  PCI
Why, specifically?
<serial >

## Slide 16
<current PC>
Northbridge now in CPU
Southbridge now the PCH (platform controller hub)
DMI 3.0 (direct media interface) serial CPU – PCH bus
SATA serial disk bus
M.2 PCIe/SATA serial bus
PCIe serial bus
2.5 G Gigabit Ethernet
USB serial bus
Legacy PS/2 port (really)

## Slide 17
<PCIe>
PCIe – express
Whereas PCI was a shared bus system, PCIe is a point to point system
Why is this better?
Notes: PCI parallel, only one use of bus at a time and in one direction, speed limited to slowest device. PCIe full duplex between any 2 endpoints, no limit on concurrent access across multiple endpoints

## Slide 18
<lanes>
PCIe – lanes
A lane consists of 2 differential signaling pairs, one for transmitting and one for receiving
A link can contain:
  1
  4
  8
  16
  32 lanes
PCIe 3.0 8GT/s per lane
What is GT/s and what does this mean in bytes/s?
Notes: Discuss how clocking is embedded in the signal, so no extra wires required.

## Slide 19
<lanes>
Lane usage
1 lane
  Low cost, low performance
16 lane
  Graphics adapters
  10 gigabit Ethernet
  SAS or Fibre Channel
Using PCIe 3.0 what are the transfer rates achievable for 16 lanes?
Do CPUs and PCHs limit the number of concurrent lanes in use?
From the top:
4 lane
16 lane
1 lane
16 lane
Legacy PCI
Notes: What are SAS and Fibre Channel? Slides coming later.

## Slide 20
As well as DMA transfers from device to memory it is possible for:
  Peer to peer DMA transfers between devices
  No involvement of CPU or main memory
<PCIe and DMA>
Notes: Simplifies multi GPU programming – SLI and Crossfire use this. You can talk about these

## Slide 21
SATA – serial ATA
  Used to connect disks and SSDs
  Two pairs using differential signalling
  3 grounds
  SATA revision 3.0
    6 Gbit/s, 600 MB/s
SATA express
  Supports SATA and 2 PCIe 3.0 lanes
  UP to 2 GB/s
  Supports NVMe for SSDs
M.2
  Implementation of SATA Express in small form factor
<SATA>
Notes: Get them to find out NVMe is. Non-Volatile Memory Express – specific interface to take advantage of SSDs

## Slide 22
SAS – Serial attached SCSI
Used in servers
Complete a comparison of SATA with SAS
<SAS>
Notes: Get them to do the work – speeds, reliability, up time, seek times, cost, usage

## Slide 23
Storage area network
Like Ethernet, but uses Fibre Channel
  SCSI over fibre
  Up to 128 Gb/s
Allows multiple servers to share storage
Not accessible to LAN
Can automate backups
<SAN>
Notes: Ask then if they think hubs and bridges are still in use

## Slide 24
USB – Universal Serial Bus
Firewire
Thunderbolt
All are used to attach a variety of hardware
They all use differential signalling and carry power
Construct a table showing their key characteristics and usage (only compare the latest and current versions)
<USB firewire thunderbolt>
Notes: Full duplex or not, speeds, length, PCIe or not, but split into two groups and let them decide what the key characteristics are. Mention DMA cyber attack vumerability

## Slide 25
DMI – direct media interface (Intel. AMD use PCIe)
DMI 3.0
  Interface between CPU and PCH
  Similar to PCIe
  4 lanes
  8 GT/s, 3.93 GB/s
<DMI>

## Slide 26
GPUs
Significant processing power
Offload OpenGL DirectX
Can be used for non graphical purposes
What are common non-graphical uses?
<graphics>
Notes: You can probably talk about these for hours

## Slide 27
Video can be:
  On an adapter card
  Integrated into the CPU
Compare the two approaches
<graphics>
Notes: Dedicated v shared RAM, cost, size, energy consumption, offload, performance

## Slide 28
Network interface controller
  Integrated on motherboard or into SOC (system on chip)
  Serial connections for slower speeds 10/100/1000
  PCIe connection for performance Gigabit and 10 Gigabit Ethernet
  Interrupt driven to request transfer of data
  DMA for transfer of data to buffers in main memory (more on this in operating systems)
  Transmit and receive queues handle packets
  High performance adapters can offload the complete TCP/IP stack from the CPU (more on this in module 2)
  RJ45, fibre optic and wireless
<NIC>

## Slide 29
Server platform
How many PCIe lanes?
  Direct to CPU
  Other
Why?
How is this optimised for the required use?
What is a BMC?
<servers>

## Slide 30
CPU + PCH in one package
What are the advantages of this?
<Integration>
Intel EVO September 2020
Notes: Matched system, shorter bus lengths, Intel EVO announced this September. Has PCIe 4.0. Get them to say what the improvements are – double the bandwidth.

## Slide 31
System on a chip
All I/O integrated
What are the advantages of this?
<soc>
Broadcom

## Slide 32
<phone SOC>
Notes: Some fun discussion points here. How many cores?

## Slide 33
Construct – for your own notes – a bus speed hierarchy
Fastest at the top
Slowest at the bottom
Current versions only
Quote the performance
Include typical usage
<final task>

## Slide 34
We have covered:
All the I/O buses in current use
How signalling is performed
How the CPU is offloaded for data transfers and graphics
How the operating system handles I/O will be covered on day 11
<conclusion>