## Slide 1: Operating Systems and Architecture
(UFCFCU-30-1)
<computer architecture>

## Slide 2
After completing this section of the module you will be able to:
  Describe and explain computer architecture, digital logic and machine level representation of data (number systems)
    Fetch – execute
    ALU
    Registers
    Buses
    Control unit
<outcomes>

## Slide 3
von Neumann architecture (1945)
A stored program computer has:
  A processing unit with registers and an ALU
  A control unit with an instruction register and program counter
  Memory that stores data and instructions
  External mass storage
  Input and output mechanisms
This architecture is still used today for general purpose computing
<stored program computer>
Notes: Nothing new in computer architecture.
The ALU and memory are connected by buses

## Slide 4
So far we have described how the ALU and memory are connected by a bus
We now need to see how this is implemented in practice and how the operation is controlled
All CPU operations begin with:
  Fetch an instruction from memory
Then
  Decode the instruction in the control unit
Then
  Execute the instruction in the ALU
Then repeat or halt
<fetch – decode -execute>

## Slide 5
There are 2 internal registers which:
Contain the address in memory to be read or written to, the memory address register (MAR)
Store the data to be written, or the data read, from memory, the memory data register (MDR)
There are two buses connecting the registers to memory
  The address bus
  The data bus
<MAR and MDR>

## Slide 6
Register 0
Register 1
Register n
Memory address register
Memory data register
<MAR and MDR>
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
etc |  |  |  |  |  |  |  | 
Address bus
Data bus
Memory
Notes: MAR – Memory address register
MDR – Memory data register

## Slide 7
Where does the MAR get its value from?
The program counter (PC) – another internal register
This register holds the address in memory of the next instruction
Where does the first value in the program counter come from when a CPU is first powered up?
<program counter>
Notes: ROM chip that is accessed by the BIOS.

## Slide 8
Program counter
Register 0
Register 1
Register n
Memory address register
Memory data register
<program counter>
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
etc |  |  |  |  |  |  |  | 

## Slide 9
Breakdown of the fetch phase
  T1 a valid address from the MAR is on the address bus
  T2 the contents of the memory location are put on the data bus
  T3 the data is transferred to the MDR
  T4 the instruction in the MDR is loaded into the instruction register (IR)
  The program counter (PC) is incremented by 1
  The fetch takes 4 clock cycles
<fetch>

## Slide 10
Program counter
Register 0
Register 1
Register n
Memory address register
Memory data register
<instruction register>
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
etc |  |  |  |  |  |  |  | 
Instruction register
Control unit

## Slide 11
The decode phase
  T1 (of the execute cycle in the diagram) - the instruction is decoded in the control unit
  Either in hardware or microcode, the control unit sends appropriate signals to the ALU (e.g. the Control 0 and control 1 lines from our ALU logic diagram)
<decode>

## Slide 12
The execute phase
  T2 and T3 (of the execute cycle in the diagram) - the ALU performs the instruction
  The complete cycle for a simple instruction takes 7 clock cycles
  If a CPU clocked at 3GHz takes 7 cycles to perform an instruction, how long is that in nanoseconds?
<execute>

## Slide 13
  We will illustrate the CPU and its operation using a RISC simulator (based on an ARM processor) http://www.peterhigginson.co.uk/RISC/
<simulation>
Program counter
Instruction register
Notes: We are going to use this a lot. Probably a good idea to demo how you can load a program, step it or run it at various speeds, stop, before they try it themselves on the next slide.
LR is the link register used to hold the return address for a function cell
SP Stack pointer is used to hold “automatic” variables context/parameters across function calls.
Conceptually you can think of the "stack" as a place where you "pile" your data.
You keep "stacking" one piece of data over the other and the stack pointer tells you how "high" your "stack" of data is. You can remove data from the "top" of the "stack" and make it shorter.

## Slide 14
  Select hex
  Select the add program
  The memory is populated
  Press STEP once for 1 instruction cycle
  What has happened?
  Decode the instruction x7102
  What are the addresses of the I/O devices?
  Modify the program to write the result back to location 090 instead of register 2.
<add>
http://www.peterhigginson.co.uk/RISC/instruction_set.pdf
Notes: You can edit the program by clicking in the Assembly Language window, making the changes and then pressing submit. You may want to show them around the instruction set before the tackle the decode and rewrite tasks.

## Slide 15
Step though the remainder of the program
This is an example of the programming construct – sequence
There are two other programming constructs:
  Selection
  Iteration
The next example contains both
<sequence>

## Slide 16
  What does this program do?
  (A paper exercise – do not use the simulator)
  Where does selection occur?
  Where does iteration occur?
  What operations occur in the ALU?
<loop>
 | 0 | 1 | 2 | 3 | 4 | 6 | 6 | 7
000 | x2a20 | x71a7 | x1201 | x227f | x9801 | x2a0a | x71a7 | x0000
Notes: Take them away from the screens!

## Slide 17
A stack is an area of memory for storing items on a last in – first out basis (LIFO)
A data item is pushed onto the stack (PSH)
A data item is popped from the stack (POP)
The address of the top of the stack is held in the stack pointer
<stack>
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Stack pointer
PSH 65
0 | 0 | 0 | 0 | 0 | 0 | 0 | 65
Stack pointer
Notes: You could get them to use the whiteboard on this slide to show what happens when you PSH and POP more than one thing.

## Slide 18
Click in the Assembly Language window
Enter the program shown
Click Submit
Run the program
Why does the stack pointer start at 400?
When does the stack pointer get decremented and incremented?
Modify the program to push 5 items onto the stack, then retrieve them into their original locations
<stack>
Notes: If they are smart, they will see there is an instruction to PSH several registers at once. Get them to copy this code into a txt file as it may be useful later.

## Slide 19
  What use is a stack?
  Saving the position and status of a program when jumping to a subroutine, then restoring them when the subroutine finishes
  Passing values (parameters, variable) from one part of a program to another (e.g. functions)
  What are potential cyber problems with stacks?
<stack>

## Slide 20
  When an operation needs to be repeated in a program, rather than coding it each time it is required, code it as a subroutine
  A JMS instruction will “jump” the program to a new address
  A RET instruction will “return” the program to where it was
<subroutine>
Main program |  | 
JMS |  | Subroutine
Main program continues |  | RET

## Slide 21
Enter the program shown
Run the program
What is the function of LR and what is it?
What is LAB1?
Explain the opcode x9e05
Explain what submit has done
Write a program to save and restore the values of 2 registers before and after a subroutine
<subroutine>
Notes: Could start with the saved txt file

## Slide 22
  A flag is a status bit used to indicate the result of an operation
  The simulator has 4 flags showing the result of the last ALU operation
    N negative
    Z zero
    C carry
    V overflow
  Run this program
  What flag does it set and why?
  Write programs that set the other three flags
<flags>
Notes: They may need help with this.

## Slide 23
  You should now be able to explain the architecture of the RISC simulator
  Address and data buses and registers
  The instruction cycle
  The specialised registers
    Program counter
    Stack pointer
    Instruction register
  PSH and POP
  JMS and RET
  Flags
<summary>

## Slide 24
  Apart from subroutines, the programs have been linear sequences
  The output device (address 4 and 7) was instantaneous
  In real implementations, output devices are not instantaneous
  Suppose a program needs to write to a hard disk
    It rotates at 7,200 rpm. A half track rotation time is 4mS
    Given our 3GHz example earlier, how many instructions could be run while waiting for 4mS?
  In the dark ages (1981) of DOS 1.0, the PC would be unable to do anything else if it was printing
  The solution to these issues are interrupts
<interrupts>

## Slide 25
  Without interrupts
  The preparation, I/O command and completion take a few instructions
  Writing takes the time
<interrupts>
User program |  | I/O Program
Code |  | 
Write |  | 
Wait |  | Preparation
Wait |  | I/O command
Wait |  | Writing
Wait |  | Completion
Code |  | 
Notes: The CPU is hung up for a long time, ss the previous calculation

## Slide 26
  Interrupt mechanism
  The CPU can be interrupted by an interrupt signal that can be sent by a device
  Control is then passed to an interrupt handler which deals with the interrupt request
  The fetch execute cycle is modified
<interrupts>
Start
Fetch
Execute
Check/handle interrupts
Interrupts enabled
Interrupts disabled
Notes: You could ask then to speculate on why you may want to disable interrupts? The answer comes up later on.

## Slide 27
  With interrupts
<interrupts>
User program |  | I/O Program
Code |  | 
Write |  | 
Wait |  | Preparation
Code |  | I/O command
Code |  | Writing
Code |  | Completion
Code |  | Raise interrupt
Service interrupt |  | 
Code |  | Interrupt handler
 |  | Code
 |  | Return
Notes: The wait is now very short

## Slide 28
  The interrupt request can be to indicate completion, or request more data to be read or written
  Interrupts can occur at any point in a program’s execution
  On receiving an execution request:
    The current instruction is completed
    Acknowledge the interrupt (device removes request)
    Push the current status, register contents etc and program counter onto the stack
    Program counter pointed to relevant interrupt service routine
    Process the interrupt
    On completion pop the status, register contents etc and program counter
    Continue execution of interrupted program
<interrupts>
Notes: Now we see why we explained the stack. Key here is that the interrupted program has no need to know anything about what the interrupt is, or do anything about it.

## Slide 29
  What happens if an interrupt occurs during an interrupt?
  Interrupts can be disabled during interrupt handling
    Second or subsequent interrupts held in a pending state
    Serviced in sequence
  What are the problems with this?
  Consider three devices:
    Printer
    Hard disk
    Comms adapter
<multiple interrupts>

## Slide 30
  Consider three devices:
    Printer – very slow
    Hard disk - slow
    Comms adapter - fast
  If interrupts from the comms adapter are disabled while handling the hard disk or printer, then data may be lost or a buffer overflowed
  The solution is to have interrupt priorities
    Comms has highest priority
    Then hard disk
    Then printer
  Then interrupts can be interrupted
<multiple interrupts>

## Slide 31
<multiple interrupts>
User program |  | Printer |  | Comms |  | Disk
User program interrupted by printer
Printer interrupted by comms
Comms returns to printer
Disk interrupts printer
Disk returns to printer
Printer returns to user program

## Slide 32
<8085 8—bit microprocessor>
What are the features of the 8085 that you understand and can explain?
Notes: A task for a couple of groups? Come back and present to this slide .There are items we haven’t covered so brownie points for explaining them.

## Slide 33
  We have covered:
  The essential components of the CPU
  How the CPU is architected
  How the individual components operate
  I/O systems will be covered on day 5
<conclusion>