## Slide 1: Operating Systems and Architecture
(UFCFCU-30-1)
<number systems>

## Slide 2
Module introduction
Number systems
Digital logic
Representation of data
Computer architecture
Memory systems and storage architecture
I/O systems

## Slide 3
After completing this section of the module you will be able to:
  Describe and explain computer architecture, digital logic and machine level representation of data (number systems)
  Binary
  Hexadecimal
  Binary addition and subtraction
  2’s complement
  Floating point
  Logical operators
<outcomes>

## Slide 4
All computers do is manipulate numbers
A computer required to work in decimal would not be impossible, but it would be impractical
Early computers did work in decimal using BCD (binary coded decimal) but even then the basic operation is in binary - a two state numbering system
Why?
Because there are 3 economical physical representations of two states
  Electricity
  Magnetism
  Electromagnetic (light, radio)
<computers don’t do decimal>

## Slide 5
Electricity can be used to represent two states
Presence of a voltage or absence of a voltage
<electricity>

## Slide 6
The orientation of the magnetic particles on a disc or tape (North-South or South-North) represents a 0 or a 1
<magnetism>

## Slide 7
<light>
The surface of an optical disc has pits burnt into it by a laser.
When laser light is shone on the disc a pit will scatter light and the regular surface (land) reflects the light.
In the diagram a reflection is given the value 1, scattering has the value 0

## Slide 8
<wireless>
A radio wave is amplitude modulated by binary data (amplitude shift keying)
A binary value of 1 has a greater amplitude than a binary value of 0

## Slide 9
256
In the first column from the right we multiply by 0 times 10
In the second column we multiply by 1 times 10
In the third column we multiply by 2 times 10
So the value 256 is really (2x10x10) + (5x10) + 6
Another way of saying this is that:
the first column is 10 to the power 0 = 1
the second column is 10 to the power 1 = 10
the third column is 10 to the power 2 = 100
So 256 = (2x102)+(5x101)+(6x100)
This is known as a base 10 numeral system, or decimal
<base 10>

## Slide 10
Decimal (or base 10) had 10 values
Binary (or base 2) has 2 values: 0 and 1
The binary digit is known as a bit
In computing the value 0 = false and the value 1 = true
Compared to base 10 each column is a power of 2
  the first column is 2 to the power 0 = 1
  the second column is 2 to the power 1 = 2
  the third column is 2 to the power 2 = 4
  the fourth column is 2 to the power 3 = 8
<base 2>

## Slide 11
The same value can be represented in base 10 or base 2
Range of 5 columns of binary = 0 - 31
Possible values of 5 columns of binary = 32
<values>
Value | 1 x 101 | 1 x 100 |  | 1 x 24 | 1 x 23 | 1 x 22 | 1 x 21 | 1 x 20
0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0
7 | 0 | 7 |  | 0 | 0 | 1 | 1 | 1
15 | 1 | 5 |  | 0 | 1 | 1 | 1 | 1
17 | 1 | 7 |  | 1 | 0 | 0 | 0 | 1

## Slide 12
In computing we use 8 columns – a byte
Range of 8 columns of binary = 0 - 255
Possible values of 8 columns of binary = 256
<bytes>
Value | 1 x 27 | 1 x 26 | 1 x 25 | 1 x 24 | 1 x 23 | 1 x 22 | 1 x 21 | 1 x 20
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
4 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
16 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
32 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
64 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
128 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 13
  This is a 32 binary number (4 bytes)
  10010010 11100110 01111010 10110101
  It is painfully long to read or write
  For convenience we read and write in hexadecimal
  16 values: 0 – F
  0 1 2 3 4 5 6 7 8 9 A B C D E F
  These represent all the values of 4 bits
  Two hexadecimal digits represent a byte
<hexadecimal>

## Slide 14
  Converting our 32 bit binary number (4 bytes)
  10010010 11100110 01111010 10110101
  Split into groups of four
  1001 0010 1110 0110 0111 1010 1011 0101
  Covert to decimal
  9 2 14 6 7 10 11 5
  Convert to hexadecimal
  9 2 E 6 7 A B 5
  Return to bytes
  92 E6 7A B5
<hexadecimal>

## Slide 15
  92 E6 7A B5 is easy to read and write
  Remember: the computer only works in binary
  Is 92 decimal or hexadecimal?
  Write hex as:
  0x92
<hexadecimal>

## Slide 16
In manipulating numbers the two types of operations are:
Mathematical
  Addition
  Subtraction (done by addition using 2’s complement)
  Multiplication (done by repeated addition)
  Division (done by repeated subtraction)
  Addition is the most efficient in hardware
Logical
  Not
  Or
  And
  Exclusive OR
<operations>

## Slide 17
Rule
0+0 = 0
1+0 = 1
1 +1 = 0 and carry 1
Examples
<binary addition>
 | Binary |  |  |  | Decimal |  | Binary |  |  |  | Decimal
 | 0 | 1 | 0 | 1 | 5 |  | 0 | 1 | 1 | 1 | 7
 | 1 | 0 | 1 | 0 | 10 |  | 0 | 1 | 0 | 1 | 5
Sum | 1 | 1 | 1 | 1 |  |  | 0 | 0 | 1 | 0 | 
Carried | 0 | 0 | 0 | 0 |  |  | 1 | 1 | 1 |  | 
Result | 1 | 1 | 1 | 1 | 15 |  | 1 | 1 | 1 | 0 | 14

## Slide 18
So far all integers have been unsigned
To represent signed integers there are 2 methods
1: Signed-magnitude
  Use the most significant (leftmost) bit to indicate the sign
  0 = positive
  1 = negative
  0001 1011 is +27
  1001 1011 is -27
  Range is -128 to +128
  Problem: 2 values for zero (0000 0000 and 1000 0000)
  Problem: Does not follow rules for addition or subtraction
<negative binary >

## Slide 19
2: Two’s complement
  Use the most significant (leftmost) bit to indicate the sign
  0 = positive
  1 = negative
  0001 1011 is +27 (the same as for signed-magnitude)
  Negative numbers are a pattern that when added to the positive pattern results in zero
  The two’s complement is obtained by flipping the bits and adding 1
  Range is -128 to +127 (zero is treated as an integer)
  Follows rules for addition or subtraction
<negative binary >
3 |  | 0000 0011
 | Flip the bits | 1111 1100
-3 | Add 1 | 1111 1101
0 | Add 3 and -3 | 0000 0000

## Slide 20
Examples
Note: ignore the carry beyond the MSB
<binary subtraction>
7 | 0111
5 | 0101
-5 | 1011
7-5 = 2 | 0010
5 | 0101
7 | 0111
-7 | 1001
5-7 = -2 | 1110

## Slide 21
Real numbers
  + 3.142
  + 1,000,205
  - 0.000475
Floating point (scientific), set by the value of the exponent
  + 3.142 x 10+0
  + 1.000205 x 10+6
  - 4.75 x 10-4
Labels - 4.75 x 10- 4
<real numbers>
Sign
Mantissa
Exponent’s sign
Exponent

## Slide 22
Use the same scheme for binary floating point
IEEE 754 Floating point standard (32 bit)
The most-significant bit, bit 31, is the sign of the number: 0 is positive, -1 is negative
The exponent field holds an 8-bit unsigned value from which we subtract 127 to get the actual power of two. This allows for positive and negative values without needing a sign bit
  This is called biased notation, where the exponent has a bias (in this case, 127) subtracted to get the real power of two.
The mantissa (or fraction) is 23 bits long, which is about 8 decimal places long.
Each bit in the mantissa is a power of two which comes after the "decimal" place, i.e. the "decimal" place is implicitly to the left of bit 22.
<floating point>
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
S | 8 bit exponent |  |  |  |  |  |  |  | 23 bit mantissa |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 23
Examples
The sign bit is 0, so it is a positive number
The exponent is 127, so 127-127 = 0
The mantissa is 11 with an implied 1 = 1.11
  (the leading mantissa bit is always 1, so it is implied rather than stored)
1.11 = 1. 0.12 + 0.14 which is 1.5 + 0.25 = 1.75
The result is 1.75 x 20 = 1.75
<floating point>
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
S | 8 bit exponent |  |  |  |  |  |  |  | 23 bit mantissa |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 24
  Difficulties with floating point
  32 bit corresponds to 8 decimal places
  Rounding errors
  Implementation
    Requires special hardware (FPU) or done in software
<floating point>

## Slide 25
  Logic functions
<logic>
OR |  | 
A | B | Output
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
AND |  | 
A | B | Output
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
NOT | 
A | Output
0 | 1
1 | 0
XOR |  | 
A | B | Output
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1

## Slide 26
Module introduction
Number systems
Digital logic
Representation of data
Computer architecture
Memory systems and storage architecture
I/O systems