## Slide 1
BCS Level 4 Certificate in Network and Digital Communications Theory
QAN 603/0703/1

## Slide 2
Networking Basics

## Slide 3
No Connection
Single user
No connection
Very secure

## Slide 4
Connection
Two users
Crossover cable
Full duplex
  Transmit and receive at the same time
OSI layer 1 – Physical
  Transmission of bits
100010100101010

## Slide 5
Hub
Two or more users
A single network segment
Straight cables
OSI layer 1 – Physical
  Transmission of bits
Hub
  Amplifies signal
  Broadcasts input on all outputs
  Clients reject inputs not for them
  Half duplex – transmit or receive
  Poor performance
101001
101001
101001
101001

## Slide 6
MAC (Media Access Control) Addressing
Uniquely identifies a network interface controller (NIC)
MAC addresses are used as a network address for Ethernet and Wi-Fi
Addresses are assigned by the manufacturer and stored in the NIC’s read-only memory or firmware
It is a 48-bit address for 281,474,976,710,656 possible MAC addresses (normally shown as 6 octets) ether 4a:00:02:00:ca:e0 (from ifconfig)
ipconfig or ifconfig commands show the MAC address

## Slide 7
Packets and frames
A MAC address allows data to be directed to a specific device
The data segment is called a frame
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
FRAME |  |  |  |  |  | 

## Slide 8
Switch
Two or more users
A single network segment
Straight cables
OSI layer 2 – Data Link
  Transmission of packets
Switch
  Amplifies signal
  Directs inputs to correct outputs
  Full duplex
  Best performance
  Error checking
101001
111011
101001
111011

## Slide 9
Switch operation
Works on the Layer 2 Header
  Uses the source and destination MAC addresses to make its forwarding decisions.
MAC Address Table
  maps the switch’s ports to MAC addresses
  the source address and the port a frame was received on are entered in the MAC Address Table.
  as each connected device sends a frame the table gets fully populated
  the table is then used to forward frames to their intended destination

## Slide 10
Local Area Network
When the area covered is small, such as an office, this is known as a Local Area Network (LAN)
Devices connected to the switches are called Hosts
The hosts are typically clients, servers or LAN attached peripherals, such as printers
A LAN can be wired or wireless
Switches can be cascaded to increase the number of hosts

## Slide 11
Increasing the number of hosts
Adding switches is inefficient (inactive hosts are flushed from the MAC address table after 300s)
Adding hosts increases traffic congestion on the LAN (more collisions and failed transmissions)
Adding hosts means increased processing loads
The solution is to create additional physical networks

## Slide 12
IP addresses
A MAC address is physical, it allows packets to be delivered from one NIC to another (hop to hop)
IP addresses are logical and allow delivery of packets across networks (from end to end)
IP addresses work at OSI layer 3 – Network
An address is a 32 bit binary number represented as 4 octets
  E.g. 192.168.1.123 (IP v4)
Destination and source IP addresses are added to the data payload of the ethernet packet

## Slide 13
Packets with IP addresses
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
PACKET |  |  |  |  |  | 
Source IP address | Destination IP address
4 bytes | 4 bytes

## Slide 14
Two networks
192.168.1.12
192.168.2.7
Router
A
B
R1 NIC
R2 NIC
Source MAC | Destination MAC | Source IP | Destination IP
Host A | Router R1 | 192.168.1.12 | 192.168.2.7
Source MAC | Destination MAC | Source IP | Destination IP
Router R2 | Host B | 192.168.1.12 | 192.168.2.7
X
192.168.1.9
Notes: 146

## Slide 15
ARP Address Resolution Protocol
Used to find the MAC address for a given IP
Host A (192.168.1.12) needs to send to Host B (192.168.2.7)
It knows 192.168.2.7 is in a different network
It has a default gateway of 192.168.1.1 (the router)
It sends a broadcast ARP message (MAC ff:ff:ff:ff:ff:ff) for 192.168.1.1 (this goes to all hosts on the network)
Only the router replies with its Mac and IP addresses
Host A updates its ARP table
Sends packet to 192.168.2.7 with router MAC address

## Slide 16
ARP table

## Slide 17
Router Table In Host A (192.168.1.12)
  Contains a 0.0.0.0 entry which points to the default gateway 192.168.1.1
  Contains other IP addresses on its own network and the address of its own NIC
  If sending to Host X it will look in the table and send directly
  If sending to Host B (192.168.2.7) will find 0.0.0.0 as the closest match in the table and send to the gateway
Network Destination | Gateway | Interface | Notes
0.0.0.0 | 192.168.1.1 | 192.168.1.12 | 
127.0.0.1 | On-Link | 127.0.0.1 | Loopback
192.168.1.9 | On-Link | 192.168.1.12 | Host X

## Slide 18
Router’s Table
  Contains a list of IP addresses and interfaces
  If sending to 192.168.1.n will forward via R1 NIC
  If sending to 192.168.2.n will forward via R2 NIC /24 refers indirectly to the number of hosts on the network and is covered in subnetting (not in the BCS Cloud syllabus)
IP address | Interface
192.168.1.0/24 | R1 NIC
192.168.2.0/24 | R2 NIC

## Slide 19
Windows Network Utilities
Ping
  Tests connectivity
  ping 192.168.2.7
ARP
  Shows MAC addresses for IP addresses

## Slide 20
IP addresses
IP address classes
  Class D is used for multicast (224-239)
  Class E is experimental (240-255)
One class A address is worth 16M hosts
Therefore a way is needed to allocate significantly more hosts than are available
Address class | First octet range | Number of hosts
A | 1-126 | 16M
B | 128-191 | 64k
C | 192-223 | 254

## Slide 21
Private IP addresses
  Address ranges allocated as private, therefore not permissible onto the general internet.
  So, an organisation can have one outward facing IP address and up to 16M hosts inside
  This is done using network address translation (explained later)
Address range | Number of hosts
10.0.0.0 – 10.255.255.255 | 16M
172.16.0.0 – 172.31.255.255 | 1M
192.168.0.0 – 192.168.255.255 | 64K

## Slide 22
Setting IP addresses
  Assume a small system with 192.168.1.n addresses
  Static addresses are set on the device
  Dynamic addresses are leased by a DHCP server
IP address | Host | Type
192.168.1.1 | Router | Static
192.168.1.10 | Server | Static
192.168.1.20 | Printer | Static
192.168.1.100 - 200 | Desktops | Dynamic

## Slide 23
DHCP Dynamic Host Configuration Protocol
  Host sends a discovery request (255.255.255.255) for a DHCP server
  Server responds with a lease offer of an IP address, gateway address, duration and DNS server address (see later for DNS)
  Host responds with a request to accept the offered lease
  Server acknowledges the request
  Host configures its network interface with the agreed parameters

## Slide 24
DHCP Windows Configuration
Static Dynamic

## Slide 25
Recap
Hosts have MAC and IP addresses
They can communicate in the same network using switches and MAC addressing
To communicate between networks they use routers and IP addresses
Private IP addresses allow duplicate usage in different organisations, but are not allowed on the internet
IP addresses can be manually configured or obtained by DHCP

## Slide 26
Internet connection
Connection to the ISP
  ADSL
  Cable
  Satellite
  Cellular
  Leased line
ISP supplies:
  IP address via DHCP
  DNS address

## Slide 27
ISP IP addresses
An ISP will allocate an IP address from a range it owns
These IP addresses are unique on the internet
Gloucester College IP address is 212.219.57.69
All internet traffic to and from Gloucester College is via the IP address 212.219.57.69
Internal IP addresses at the college will be from the private IP addresses ranges
How does traffic for a private IP address get to the right host?

## Slide 28
Network and port address translation (NAT and PAT)
Implemented in the router
Allows many hosts on the internal network to connect via one public IP address
Allows many applications on one host to communicate with many services in the cloud
Uses IP and port numbers

## Slide 29
Ports
An IP address and a port address make up a socket
  Eg 212.219.57.69:80 (Gloucester college HTTP port)
An application, service or process uses the socket to send and receive data via the network – OSI Layer 4 Transport
The operating system
  transmits the data from all application ports on to the network
  directs received packets to the matching IP address and port number

## Slide 30
Port allocation
Well known ports 0-1023
  Examples
    21 FTP
    25 SMTP
    80 HTTP
    110 POP3
    443 HTTPS
Registered ports 1024-49151
Dynamic ports 49152-65535

## Slide 31
Packets with IP addresses and port numbers
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
PACKET |  |  |  |  |  | 
Source IP address | Destination IP address | Source port number | Destination port number
4 bytes | 4 bytes | 2 bytes | 2 bytes

## Slide 32
Browser request
Host | Router client side | Router ISP side | Cloud service
S 192.168.1.12:3333 D 216.58.218.206:80 | 192.168.1.12:3333 | 212.219.57.69:7777 | S 212.219.57.69:7777 D 216.58.218.206:80
Host inserts random source port number
Router translates internal network IP address to the external network address and port
Router updates translate table and records port numbers

## Slide 33
Server response
Cloud service | Router ISP side | Router client side | Host
S 216.58.218.206:80 D 212.219.57.69:7777 | 212.219.57.69:7777 | 192.168.1.12:3333 | S 216.58.218.206:80 D 192.168.1.12:3333
Server puts source address from received packet into destination address of outbound packet
Router translates external network IP address to the internal network address and port
Host receives packet and OS directs to correct application

## Slide 34
Domain Name System
Translates domain names to IP addresses
A host will query a domain name server (address from DHCP) with the domain name (eg www.techrepublic.com)
DNS server returns the IP address
Windows command: nslookup

## Slide 35
Recap
Internal networks connect to the internet via ISP
The ISP allocates an IP address
Network address translation (NAT) allows private IP addressing
Port address translation (PAT) allows multiple applications to connect to cloud services
DNS allows memorable names to be used for cloud resources

## Slide 36
1. Network Data and Protocols (20%, K2)
In this key topic, the apprentice will describe and explain the common networks in use and their associated data formats, protocols and related performance issues. Outcomes should include an ability to:
1.1 Describe data formats and protocols in current use
1.2 Explain features of network protocols in widespread use on the Internet
1.3 Identify network failure modes and reasons why networks ‘hang’
1.4 Describe approaches to error control in a network

## Slide 37
1.1 Describe data formats and protocols in current use
A candidate should be able to:
• Explain what is meant by data and protocol.
• Explain the relationship between data and protocol.
• Explain the technical specification of data formats and protocols.
• Describe the main features of data formats and protocols such as syntax, synchronisation, error recovery methods and error detection.
• Identify what data formats and protocols are in current use such as PPP, 802.3 and SLIP.
• Recognise protocol diagrams such as UML and Time-Sequence.

## Slide 38
Data
Data is information that has been translated into a form that is efficient for movement or processing
Relative to today's computers and transmission media, data is information converted into binary digital form
It is acceptable for data to be used as a singular subject or a plural subject
Raw data is a term used to describe data in its most basic digital format
At its most rudimentary level, data is usually in the form of ones and zeros, known as binary data
As all computer data is in binary format, it can be created, processed, saved, and stored digitally
Allows data to be transferred from one computer to another using a network connection or various media devices
Does not deteriorate over time or lose quality after being used multiple times

## Slide 39
Protocol
Network protocols are formal standards and policies comprised of rules, procedures and formats that define communication between two or more devices over a network
Network protocols govern the end-to-end processes of timely, secure and managed data or network communication
These rules include what type of data may be transmitted, what commands are used to send and receive data, and how data transfers are confirmed
Notes: You can think of a protocol as a spoken language. Each language has its own rules and vocabulary. If two people share the same language, they can communicate effectively. Similarly, if two hardware devices support the same protocol, they can communicate with each other, regardless of the manufacturer or type of device. For example, an Apple iPhone can send an email to an Android device using a standard mail protocol.
146

## Slide 40
Protocols
Protocols exist for several different applications
Examples include wired networking (e.g., Ethernet), wireless networking (e.g., 802.11ac), and Internet communication (e.g., IP)
The Internet protocol suite, which is used for transmitting data over the Internet, contains dozens of protocols
May be broken up into four categories:
  Link layer - PPP, DSL, Wi-Fi, etc.
  Internet layer - IPv4, IPv6, etc.
  Transport layer - TCP, UDP, etc.
  Application layer - HTTP, IMAP, FTP, etc

## Slide 41
ISO Model
Application
(Host-to-host) Transport
Internet
Network Interface
(Hardware)
TCP/IP Model Layers
Notes: The TCP/IP architectural model has four layers that approximately match six of the seven layers in the OSI Reference Model. The TCP/IP model does not address the physical layer, which is where hardware devices reside. The next three layers—network interface, internet and (host-to-host) transport—correspond to layers 2, 3 and 4 of the OSI model. The TCP/IP application layer conceptually “blurs” the top three OSI layers. It’s also worth noting that some people consider certain aspects of the OSI session layer to be arguably part of the TCP/IP host-to-host transport layer.
146

## Slide 42
Link Layer Protocols
Establish communication between devices at a hardware level
In order to transmit data from one device to another, each device's hardware must support the same link layer protocol

## Slide 43
Internet Layer Protocols
Used to initiate data transfers and route them over the Internet

## Slide 44
Transport Layer Protocols
Define how packets are sent, received, and confirmed

## Slide 45
Application Layer Protocols
Contain commands for specific applications
For example, a web browser uses HTTPS to securely download the contents of a webpage from a web server
An email client uses SMTP to send email messages through a mail server.

## Slide 46
Data Formats
A data format or file format is the format in which the data is coded
The information is coded in such a way that a program or application can recognize, read and use the data
Data transmission occurs:
  In the form of bits (1’s and 0’s)
  Light
  Radio
  Microwave
Can be analogue or digital
Data can be compressed and decompressed

## Slide 47
Data Formats - Microwave
Uses a beam of radio waves in the microwave frequency range (6GHz to 8.2GHz) to transmit information between two fixed locations on the earth
Beams are unidirectional
Have high loss due to high frequency
Max distance ~40km
Use line of sight

## Slide 48
Data Formats - Light
Can be laser (Light Amplification by Stimulated Emission of Radiation) (ultraviolet) or normal white light
Ultraviolet waves have wavelengths of 400 to 700 nm
Can be transmitted along optic fibre

## Slide 49
Loss of data
Data can become unusable in three different ways:
  Loss of bits The carrier is damaged, is lost of its quality deteriorates in such a way that it effect the bits, popularly called 'bit rot‘
  Loss of documentation It is unclear how one file is tied to another, for instance when different versions of a file or the metadata are no longer available, leaving the meaning of the data unclear
  Loss of display possibilities The operating system, the hardware or the application are no longer present or cannot be used anymore. That can also be caused by external factors such as computer virus, fire or accidental deleting of files.

## Slide 50
1.2 Explain features of network protocols in widespread use on the Internet.
Including, but not limited to:
HTTPS HTTP SMTP SNMP TCP UDP IP

## Slide 51
HTTP
HTTP is a simple but powerful protocol:
  HTTP is connectionless
  HTTP is media independent
  HTTP is stateless
HTTP is not secure as it is not encrypted
HTTP operates at the highest layer of the TCP/IP model, the Application layer

## Slide 52
HTTPS
HTTPS is an extension of the Hypertext Transfer Protocol (HTTP)
It is used for secure communication over a computer network, and is widely used on the Internet
HTTPS is not a separate protocol, but refers to use of ordinary HTTP over an encrypted SSL/TLS connection
Operates at the Application layer, as does the TLS security protocol (operating as a lower sublayer of the same layer)
The TLS protocol performs the encryption
HTTPS connections uses a public key certificate for the web server
This certificate must be signed by a trusted certificate authority for the web browser to accept it without warning

## Slide 53
SMTP
The primary job of the Simple Mail Transfer Protocol (SMTP) is to implement the TCP/IP electronic mail delivery system
SMTP includes a number of other features and capabilities
These allow SMTP to support special requirements and auxiliary needs of the mail system, and are described in detail in RFC 2821
  Mail relaying
  Mail forwarding
  Mail Gatewaying
  Address debugging
  Mailing list expansion
  Turning
Notes: Mail Relaying: As discussed in the SMTP communication overview, the protocol was once widely used in a “relaying mode” where e-mail was routed from one SMTP server to another to reach its destination. Today, the normal method of e-mail transfer on the Internet today is directly from the sender's SMTP server to the recipient's, using DNS MX records to determine the recipient SMTP server address. SMTP still includes the ability to relay mail from one server to another, provided certain conditions are met. Note that in addition to the inefficiency of relaying, many servers won't relay mail because this feature has been abused for spamming and hacking.
Mail Forwarding: Under certain conditions, an SMTP server may agree to accept e-mail for a non-local mailbox and forward it to the appropriate destination. This sounds similar to relaying but is used in a different way. A common example is when a user changes his or her e-mail address. If I have worked at XYZ Industries for years and then retire, the company may no longer wish to let me receive e-mail at the company's SMTP server. As a courtesy, however, they may forward e-mail sent to me there so I still receive it at my new company.
Mail Gatewaying: Certain SMTP servers may be configured as e-mail gateways. These devices “translate” TCP/IP e-mail into a form suitable for another e-mail system, and vice-versa. Gatewaying is a complex topic because e-mail systems can be so different; one of the more important problems is the inconsistency of addressing methods of different e-mail systems.
Address Debugging: SMTP includes a VRFY (verify) command, which can be used to check the validity of an e-mail address without actually sending mail to it.
Mailing List Expansion: The SMTP command EXPN (expand) can be used to determine the individual e-mail addresses associated with a mailing list. (Note however that this has nothing directly to do with mailing list software like Majordomo.)
“Turning”: The original SMTP protocol included a command that allows the SMTP sender and SMTP receiver to change roles. This could be used to allow SMTP server A to send e-mail to server B, and then have B send e-mail it has queued for A in the same session. In practice, this capability was not widely used for a variety of reasons, including security considerations. It is now officially “not recommended”, but may still be implemented in some SMTP software.
<number>

## Slide 54
SMTP
Proxy | Name
SOCKS4 | SOCKS4 proxy.
SOCKS4A | SOCKS4A proxy (capable of resolving domain names).
SOCKS5 | SOCKS5 proxy.
HTTP CONNECT | HTTP proxy using CONNECT method.
The SMTP class supports the following Proxy servers:

## Slide 55
SNMP
Simple Network Management Protocol” is a communications protocol through which an admin, via manager systems and authorized agents, can monitor and even manipulate some aspects of a networks configuration and traffic
SNMP is an open internet standard for managing networked devices (systems)
three versions of SNMP that define approved standards:
  SNMPv1
  SNMPv2 (also known, and referred to in this document, as SNMPv2c)
  SNMPv3

## Slide 56
SMNP
Main features:
  Managers and Agents
    SNMP is a network protocol that allows devices to be managed remotely by a network management station (NMS), also commonly called a manager.
    To be managed, a device must have an SNMP agent associated with it. The purpose of the agent is to:
      Receive requests for data representing the state of the device from the manager, and provide an appropriate response
      Accept data from the manager to enable control of the device state
      Generate SNMP traps, which are unsolicited messages sent to one or more selected mangers to signal significant events relating to the device

## Slide 57
SMNP
Main Features (cont):
  Management Information Base
    To manage and monitor a device, its characteristics must be represented using a format known to both the agent and the manager
    These characteristics can represent physical properties such as fan speeds, or services such as routing tables
    The data structure defining these characteristics is known as a management information base (MIB)
  In response to a get operation, the agent provides data, either maintained locally or directly from the managed device
  In response to a set operation, the agent typically performs some action affecting the state of either itself or the managed device

## Slide 58
SMNP
Main Features (cont):
  MIB Tables
    Much of the data content defined by MIBs is in tabular form, and organized as entries consisting of a sequence of objects, each with its own OIDs. For example, a table of fan characteristics could consist of a number of rows, one per fan, with each row containing columns corresponding to the current speed, the expected speed, and the minimum acceptable speed
    The addressing of the rows within the table can be as follows:
      Simple, single-dimensional index (a row number within the table, for example `6')
      More complex, multidimensional, instance specifier such as an IP address and port number (for instance, 127.0.0.1, 1234)

## Slide 59
SMNP
Main Features (cont):
  Access Control
    All addressable objects defined in the MIB have associated maximum access rights, for instance, read-only or read-write
    These determine the maximum access the agent can support, and can be used by the manager to restrict the operations it will permit the operator to attempt
    The agent is able to apply lower access rights as required, that is, it is able to refuse writes to objects that are considered read-write
    This refusal can be on the basis of:
      How applicable the operation is to the object being addressed (for example, where an object defined by the MIB represents a state machine for which only certain transactions are legal)
      Security restrictions that limit certain operations to restricted sets of managers

## Slide 60
TCP
Transmission Control Protocol (TCP - RFC 793) is considered as a reliable protocol
Transmission Control Protocol (TCP) is responsible for breaking up the message (Data from application layer) into TCP Segments and reassembling them at the receiving side
It is not sure that the data reaching at the receiving device is in the same order as the sending side, because of the problems in network or different paths packets flow to the destination
TCP is responsible for keeping the unordered segments in the right order
TCP assures a reliable delivery by resending anything that gets lost while traveling the network

## Slide 61
TCP - Characteristics
Stream Data transfer:
  Applications working at the Application Layer transfers a contiguous stream of bytes to the bottom layers
  It is the duty of TCP to pack this byte stream to packets, known as TCP segments, which are passed to the IP layer for transmission to the destination device
  The application does not have to bother to chop the byte stream data packets

## Slide 62
TCP - Characteristics
Reliability:
  The most important feature of TCP is reliable data delivery. In order to provide reliability, TCP must recover from data that is damaged, lost, duplicated, or delivered out of order by the Network Layer
  TCP assigns a sequence number to each byte transmitted, and expects a positive acknowledgment (ACK) from the receiving TCP layer
  If the ACK is not received within a timeout interval, the data is retransmitted
  The receiving TCP uses the sequence numbers to rearrange the TCP segments when they arrive out of order, and to eliminate duplicate TCP segments

## Slide 63
TCP - Characteristics
Flow control:
  Network devices operate at different data rates because of various factors like CPU and available bandwidth
  It may happen a sending device to send data at a much faster rate than the receiver can handle
  TCP uses a sliding window mechanism for implementing flow control
  The number assigned to a segment is called the sequence number and this numbering is actually done at the byte level
  The TCP at the receiving device, when sending an ACK back to the sender, also indicates to the TCP at the sending device, the number of bytes it can receive (beyond the last received TCP segment) without causing serious problems in its internal buffers

## Slide 64
TCP - Characteristics
Multiplexing:
  Multitasking achieved through the use of port numbers
Connections:
  Before application processes can send data by using TCP, the devices must establish a connection
  The connections are made between the port numbers of the sender and the receiver devices
  A TCP connection identifies the end points involved in the connection
  A socket number is a combination of IP address and port number, which can uniquely identify a connection
Full duplex:
  TCP provides for concurrent data streams in both directions

## Slide 65
IP
Internet Protocol
Principal communications protocol in the Internet protocol suite for relaying datagrams across network boundaries
Its routing function enables internetworking, and essentially establishes the Internet
Addressing
  IP packet headers contain addresses that identify the sending computer and the receiving computer
  Routers use this information to guide each packet across communication networks and connect the sending and receiving computers

## Slide 66
IP
Reassembly
  Internet Protocol keeps track of the way messages between computers are broken into packets
  Since most messages are too big to fit in one packet, and since packets aren't sent in any organized order, they must be reassembled as they arrive at the recipient
  IP dictates how packets are reassembled into usable messages

## Slide 67
IP – Frame Format

## Slide 68
TCP/IP
TCP/IP is a set of protocols (Protocol Suit) that enable communication between computers
It is a tested and proved protocol suit
Features:
  Multi-vendor support
  Iteroperability
  Logical addressing
  Routability
  Name resolution
  Error control and flow control
  Multiplexing/de-multiplexing
Notes: 1) Multi-Vendor Support. TCP/IP is implemented by many hardware and software vendors. It is an industry standard and not limited to any specific vendor.
2) Interoperability. Today we can work in a heterogeneous network because of TCP/IP. A user who is sitting on a Windows box can download files from a Linux machine, because both Operating Systems support TCP/IP. TCP/IP eliminates the cross-platform boundaries.
3) Logical Addressing. Every network adapter has a globally unique and permanent physical address, which is known as MAC address (or hardware address). The physical address is burnt into the card while manufacturing. Low-lying hardware-conscious protocols on a LAN deliver data packets using the adapter's physical address. The network adapter of each computer listens to every transmission on the local network to determine whether a message is addressed to its own physical address.
For a small LAN, this will work well. But when your computer is connected to a big network like internet, it may need to listen to millions of transmissions per second. This may cause your network connection to stop functioning.
To avoid this, network administrators often segment (divide) big networks into smaller networks using devices such as routers to reduce network traffic, so that the unwanted data traffic from one network may not create problem in another network. A network can be again subdivided into smaller subnets so that a message can travel efficiently from its source to the destination. TCP/IP has a robust subnetting capability achieved using logical addressing. A logical address is an address configured through the network software. The logical addressing system used in TCP/IP protocol suit is known as IP address.
4) Routability. A router is a network infrastructure device which can read logical addressing information and direct data across the network to its destination.TCP/IP is a routable protocol, which means the TCP/IP data packets can be moved from one network segment to another.
5) Name Resolution. IP addresses are designed for the computers and it is difficult for humans to remember many IP addresses. TCP/IP allows us to use human-friendly names, which are very easy to remember (Ex. www.omnisecu.com). Name Resolutions servers (DNS Servers) are used to resolve a human readable name (also known as Fully Qualified Domain Names (FQDN)) to an IP address and vice versa.
6) Error Control and Flow Control.The TCP/IP protocol has features that ensure the reliable delivery of data from source computer to the destination computer. TCP (Transmisssion Control Protocol) defines many of these error-checking, flow-control, and acknowledgement functions.
7) Multiplexing/De-multiplexing. Multiplexing means accepting data from different applications and directing that data to different applications listening on different receiving computers. On the receiving side the data need to be directed to the correct application, for that data was meant for. This is called De-multiplexing. We can run many network applications on the same computer. By using logical channels called ports, TCP/IP provides means for delivering packets to the correct application. In TCP/IP, ports are identified by using TCP or UDP port numbers.
<number>

## Slide 69
TCP – Frame Format

## Slide 70
UDP
User Datagram Protocol
  Provides connectionless, unreliable service
  So UDP faster than TCP
  Adds only checksum and process-to-process addressing to IP
  Used for DNS and NFS
  Used when socket is opened in datagram mode
  It sends bulk quantity of packets
  No acknowledgment
  Good for video streaming: it is an unreliable protocol

## Slide 71
UDP – Frame Format

## Slide 72
1.3 Identify network failure modes and reasons why networks ‘hang’
A candidate should be able to:
• Describe failure modes in protocols.
• Describe the effect on a protocol of data communication errors.
• Describe causes for network failures.
• Explain the causes for system 'hangs'.

## Slide 73
The Effect On A Protocol Of Data Communication Errors
Error control is the technique of detecting and correcting blocks of data during communication
It checks the reliability of characters both at the bit level and packet level
If proper error control is in place, transmitted and received data is ensured to be identical, as in many cases communication channels can be highly unreliable
Data can be corrupted while in transmission
In order to retain reliable communication, errors must be detected and corrected
Forward error control and feedback error control are the two types of error-control mechanisms used in communications

## Slide 74
Causes for Network Failures
Misconfiguration
Security breaches
Old equipment
Human error
Incompatible changes
Hardware failures
Power failures

## Slide 75
Causes for System 'Hangs'
CPU
RAM
NIC failure
Overheating
Software errors
Electrical problems
Environment

## Slide 76
1.4 Describe approaches to error control in a network
A candidate should be able to:
• Describe at least one approach to error control in a network such as; forward error control, feedback error control and block error control.
• Identify methods of error control, such as checksum, parity and redundancy.

## Slide 77
Forward Error Control
In forward error control, additional redundant information is also transmitted along with the data
This helps the receiver to detect and determine the location of the error in the transmitted data
Forward error control is less commonly used due to the amount of additional redundant information which is transmitted.

## Slide 78
Feedback Error Control
In backward or feedback error control, along with each character, a little additional information is provided for the detection of errors
The receiver in this technique performs no error correction
If the received data is found to contain errors, the entire data is retransmitted

## Slide 79
Methods of Error Control
Checksum
Parity
Redundancy

## Slide 80
Checksum
A checksum is an error-detection method in a the transmitter computes a numerical value according to the number of set or unset bits in a message and sends it along with each message frame
At the receiver end, the same checksum function (formula) is applied to the message frame to retrieve the numerical value
A checksum error means there was a problem with the serial communications
A checksum is created based on the data values in the data blocks to be transmitted using some algorithm and appended to the data
When the receiver gets this data, a new checksum is calculated and compared with the existing checksum
A non-match indicates an error

## Slide 81
Parity
Historically the most commonly used data integrity method
Parity can detect - but not correct - single-bit errors
Error Correction Code (ECC) is a more comprehensive method of data integrity checking that can detect and correct single-bit errors

## Slide 82
Redundancy
Cyclic Redundancy Check (CRC):
  CRC is based on binary division.
  A sequence of redundant bits called CRC or the CRC remainder is appended to the end of a data unit, so that the resulting data unit becomes exactly divisible by a second, predetermined binary number
  At its destination, the incoming data unit is divided by the same number
  If at this step there is no remainder, the data unit is assumed to be intact and therefore is accepted

## Slide 83
End of Day 1

## Slide 84
2. Layered Network Models (20%, K2)
In this key topic, the apprentice will be able to explain network layer models and then contrast their differences. Outcomes should include an ability to:
2.1 Explain features layered network models
2.2 Compare the differences between the following physical layer categories and datalink layer protocols

## Slide 85
2.1 Explain features of the following layered network models:
TCP/IP Reference Model
OSI 7 Layer Model

## Slide 86
OSI
Systems must be developed which are compatible to communicate with each other ISO has developed a standard
ISO stands for International organization of Standardization
This is called a model for Open System Interconnection (OSI) and is commonly known as OSI model
The ISO-OSI model is a seven layer architecture. It defines seven layers or levels in a complete communication system
They are:
  Application Layer
  Presentation Layer
  Session Layer
  Transport Layer
  Network Layer
  Datalink Layer
  Physical Layer

## Slide 87
Feature of OSI Model
Big picture of communication over network is understandable through this OSI model
We see how hardware and software work together
We can understand new technologies as they are developed
Troubleshooting is easier by separate networks
Can be used to compare basic functional relationships on different networks

## Slide 88
Functions of Different Layers
Following are the functions performed by each layer of the OSI model
This is just an introduction, we will cover each layer in details in the coming tutorials

## Slide 89
OSI Model Layer 1: The Physical Layer
Physical Layer is the lowest layer of the OSI Model.
It activates, maintains and deactivates the physical connection.
It is responsible for transmission and reception of the unstructured raw data over network.
Voltages and data rates needed for transmission is defined in the physical layer.
It converts the digital/analog bits into electrical signal or optical signals.
Data encoding is also done in this layer.

## Slide 90
OSI Model Layer 2: Data Link Layer
Data link layer synchronizes the information which is to be transmitted over the physical layer
The main function of this layer is to make sure data transfer is error free from one node to another, over the physical layer
Transmitting and receiving data frames sequentially is managed by this layer.
This layer sends and expects acknowledgements for frames received and sent respectively
Resending of non-acknowledgement received frames is also handled by this layer
This layer establishes a logical layer between two nodes and also manages the Frame traffic control over the network
It signals the transmitting node to stop, when the frame buffers are full

## Slide 91
OSI Model Layer 3: The Network Layer
Network Layer routes the signal through different channels from one node to other
It acts as a network controller
It manages the Subnet traffic
It decides by which route data should take
It divides the outgoing messages into packets and assembles the incoming packets into messages for higher levels

## Slide 92
OSI Model Layer 4: Transport Layer
Transport Layer decides if data transmission should be on parallel path or single path
Functions such as Multiplexing, Segmenting or Splitting on the data are done by this layer
It receives messages from the Session layer above it, convert the message into smaller units and passes it on to the Network layer
Transport layer can be very complex, depending upon the network requirements
Transport layer breaks the message (data) into small units so that they are handled more efficiently by the network layer

## Slide 93
OSI Model Layer 5: The Session Layer
Session Layer manages and synchronize the conversation between two different applications.
Transfer of data from source to destination session layer streams of data are marked and are resynchronized properly, so that the ends of the messages are not cut prematurely and data loss is avoided

## Slide 94
OSI Model Layer 6: The Presentation Layer
Presentation Layer takes care that the data is sent in such a way that the receiver will understand the information (data) and will be able to use the data
While receiving the data, presentation layer transforms the data to be ready for the application layer
Languages(syntax) can be different of the two communicating systems
Under this condition presentation layer plays a role of translator
It performs Data compression, Data encryption, Data conversion etc.

## Slide 95
OSI Model Layer 7: Application Layer
Application Layer is the topmost layer
Transferring of files disturbing the results to the user is also done in this layer
Mail services, directory services, network resource etc. are services provided by application layer
This layer mainly holds application programs to act upon the received and to be sent data

## Slide 96
Merits of OSI reference model
OSI model distinguishes well between the services, interfaces and protocols
Protocols of OSI model are very well hidden
Protocols can be replaced by new protocols as technology changes
Supports connection oriented services as well as connectionless service

## Slide 97
Demerits of OSI reference model
Model was devised before the invention of protocols
Fitting of protocols is tedious task
It is just used as a reference model

## Slide 100
TCP/IP
The TCP/IP model was developed prior to the OSI model
The TCP/IP model is not exactly similar to the OSI model
The TCP/IP model consists of five layers:
  the application layer
  transport layer
  network layer
  data link layer
  physical layer
The first four layers provide physical standards, network interface, internetworking, and transport functions that correspond to the first four layers of the OSI model and these four layers are represented in TCP/IP model by a single layer called the application layer
TCP/IP is a hierarchical protocol made up of interactive modules, and each of them provides specific functionality

## Slide 101
Functions of TCP/IP layers

## Slide 102
Network Access Layer
A network layer is the lowest layer of the TCP/IP model
A network layer is the combination of the Physical layer and Data Link layer defined in the OSI reference model
It defines how the data should be sent physically through the network.
This layer is mainly responsible for the transmission of the data between two devices on the same network
The functions carried out by this layer are encapsulating the IP datagram into frames transmitted by the network and mapping of IP addresses into physical addresses
The protocols used by this layer are ethernet, token ring, FDDI, X.25, frame relay

## Slide 103
Internet Layer
An internet layer is the second layer of the TCP/IP model
An internet layer is also known as the network layer
The main responsibility of the internet layer is to send the packets from any network, and they arrive at the destination irrespective of the route they take

## Slide 104
Following are the protocols used in this layer
IP Protocol
ARP Protocol
ICMP Protocol

## Slide 105
Responsibilities of the IP protocol
IP Addressing:
This protocol implements logical host addresses known as IP addresses. The IP addresses are used by the internet and higher layers to identify the device and to provide internetwork routing.
Host-to-host communication:
It determines the path through which the data is to be transmitted.
Data Encapsulation and Formatting:
An IP protocol accepts the data from the transport layer protocol. An IP protocol ensures that the data is sent and received securely, it encapsulates the data into message known as IP datagram.
Fragmentation and Reassembly:
The limit imposed on the size of the IP datagram by data link layer protocol is known as Maximum Transmission unit (MTU). If the size of IP datagram is greater than the MTU unit, then the IP protocol splits the datagram into smaller units so that they can travel over the local network. Fragmentation can be done by the sender or intermediate router. At the receiver side, all the fragments are reassembled to form an original message.
Routing:
When IP datagram is sent over the same local network such as LAN, MAN, WAN, it is known as direct delivery. When source and destination are on the distant network, then the IP datagram is sent indirectly. This can be accomplished by routing the IP datagram through various devices such as routers.

## Slide 106
ARP Protocol
ARP stands for Address Resolution Protocol
ARP is a network layer protocol which is used to find the physical address from the IP address
The two terms are mainly associated with the ARP Protocol:
  ARP request: When a sender wants to know the physical address of the device, it broadcasts the ARP request to the network
  ARP reply: Every device attached to the network will accept the ARP request and process the request, but only recipient recognize the IP address and sends back its physical address in the form of ARP reply
  The recipient adds the physical address both to its cache memory and to the datagram header

## Slide 107
ICMP Protocol
ICMP stands for Internet Control Message Protocol
It is a mechanism used by the hosts or routers to send notifications regarding datagram problems back to the sender
A datagram travels from router-to-router until it reaches its destination. If a router is unable to route the data because of some unusual conditions such as disabled links, a device is on fire or network congestion, then the ICMP protocol is used to inform the sender that the datagram is undeliverable
An ICMP protocol mainly uses two terms:
  ICMP Test: ICMP Test is used to test whether the destination is reachable or not
  ICMP Reply: ICMP Reply is used to check whether the destination device is responding or not
The core responsibility of the ICMP protocol is to report the problems, not correct them
The responsibility of the correction lies with the sender
ICMP can send the messages only to the source, but not to the intermediate routers because the IP datagram carries the addresses of the source and destination but not of the router that it is passed to

## Slide 108
Transport Layer
The transport layer is responsible for the reliability, flow control, and correction of data which is being sent over the network

## Slide 109
Transport Layer
The two protocols used in the transport layer are User Datagram protocol and Transmission control protocol

## Slide 110
User Datagram Protocol (UDP)
  It provides connectionless service and end-to-end delivery of transmission
  It is an unreliable protocol as it discovers the errors but not specify the error
  User Datagram Protocol discovers the error, and ICMP protocol reports the error to the sender that user datagram has been damaged
  UDP consists of the following fields: Source port address: The source port address is the address of the application program that has created the message Destination port address: The destination port address is the address of the application program that receives the message Total length: It defines the total number of bytes of the user datagram in bytes. Checksum: The checksum is a 16-bit field used in error detection
  UDP does not specify which packet is lost. UDP contains only checksum; it does not contain any ID of a data segment

## Slide 111
User Datagram Protocol (UDP)

## Slide 112
Transmission Control Protocol (TCP)
It provides a full transport layer services to applications
It creates a virtual circuit between the sender and receiver, and it is active for the duration of the transmission
TCP is a reliable protocol as it detects the error and retransmits the damaged frames
Therefore, it ensures all the segments must be received and acknowledged before the transmission is considered to be completed and a virtual circuit is discarded
At the sending end, TCP divides the whole message into smaller units known as segment, and each segment contains a sequence number which is required for reordering the frames to form an original message
At the receiving end, TCP collects all the segments and reorders them based on sequence numbers

## Slide 113
Application Layer
An application layer is the topmost layer in the TCP/IP model
It is responsible for handling high-level protocols, issues of representation
This layer allows the user to interact with the application
When one application layer protocol wants to communicate with another application layer, it forwards its data to the transport layer
There is an ambiguity that occurs in the application layer
Every application cannot be placed inside the application layer except those who interact with the communication system
For example: text editor cannot be considered in application layer while web browser using HTTP protocol to interact with the network where HTTP protocol is an application

## Slide 114
Main Protocols Used in the Application Layer
HTTP: HTTP stands for Hypertext transfer protocol. This protocol allows us to access the data over the world wide web. It transfers the data in the form of plain text, audio, video. It is known as a Hypertext transfer protocol as it has the efficiency to use in a hypertext environment where there are rapid jumps from one document to another.
SNMP: SNMP stands for Simple Network Management Protocol. It is a framework used for managing the devices on the internet by using the TCP/IP protocol suite.
SMTP: SMTP stands for Simple mail transfer protocol. The TCP/IP protocol that supports the e-mail is known as a Simple mail transfer protocol. This protocol is used to send the data to another e-mail address.
DNS: DNS stands for Domain Name System. An IP address is used to identify the connection of a host to the internet uniquely. But, people prefer to use the names instead of addresses. Therefore, the system that maps the name to the address is known as Domain Name System.
TELNET: It is an abbreviation for Terminal Network. It establishes the connection between the local computer and remote computer in such a way that the local terminal appears to be a terminal at the remote system.
FTP: FTP stands for File Transfer Protocol. FTP is a standard internet protocol used for transmitting the files from one computer to another computer.

## Slide 115
2.2 Compare the differences between the following physical layer categories and datalink layer protocols:
Physical Layers (including, but not limited to: Wireless, Fibre, Wired)
Data Link Layer (including, but not limited to: Ethernet [802.3], Wireless LAN [802.11], Bluetooth)

## Slide 116
Done

## Slide 117
Digital Transmission
DIGITAL-TO-DIGITAL CONVERSION
Digital-to-digital encoding is the representation of digital information by a digital signal
When binary 1s and 0s generated by the computer are translated into a sequence of voltage pulses that can be propagated over a wire, this process is known as digital-to-digital encoding

## Slide 118
ANALOG-TO-DIGITAL CONVERSION
When an analog signal is digitalized, this is called an analog-to-digital conversion
Suppose human sends a voice in the form of an analog signal, we need to digitalize the analog signal which is less prone to noise
It requires a reduction in the number of values in an analog message so that they can be represented in the digital stream
In analog-to-digital conversion, the information contained in a continuous wave form is converted in digital pulses

## Slide 119
Techniques for Analog-To-Digital Conversion
PAM
PAM stands for pulse amplitude modulation
PAM is a technique used in analog-to-digital conversion
PAM technique takes an analog signal, samples it, and generates a series of digital pulses based on the result of sampling where sampling means measuring the amplitude of a signal at equal intervals
PAM technique is not useful in data communication as it translates the original wave form into pulses, but these pulses are not digital
To make them digital, PAM technique is modified to PCM technique

## Slide 121
PCM
PCM stands for Pulse Code Modulation
PCM technique is used to modify the pulses created by PAM to form a digital signal. To achieve this, PCM quantizes PAM pulses
Quantization is a process of assigning integral values in a specific range to sampled instances
PCM is made of four separate processes: PAM, quantization, binary encoding, and digital-to-digital encoding.

## Slide 123
End of Day 2

## Slide 124
3. Network Routing Protocols (30%, K3)
In this key topic, the apprentice will describe and explain network routing protocols. Outcomes should include an ability to:
3.1 Describe current network routing protocols in use
3.2 Compare the differences between static and dynamic routing

## Slide 125
3.1 Describe current network routing protocols in use; including, but not limited to:
RIP/RIP2
RIP-NG
OSPF
OSPFv2
OSPFv3
A candidate should be able to:
• Explain the technical specification of network routing protocols.
• Describe the main features of network routing protocols.
• Explain the advantages and disadvantages of current network routing protocols, such as security, complexity / simplicity, resilience and scalability

## Slide 126
This table lists the administrative distance default values of the protocols
Route Source | Default Distance Values
Connected interface | 0
Static route | 1
Enhanced Interior Gateway Routing Protocol (EIGRP) summary route | 5
External Border Gateway Protocol (BGP) | 20
Internal EIGRP | 90
IGRP | 100
OSPF | 110
Intermediate System-to-Intermediate System (IS-IS) | 115
Routing Information Protocol (RIP) | 120
Exterior Gateway Protocol (EGP) | 140
On Demand Routing (ODR) | 160
External EIGRP | 170
Internal BGP | 200
Unknown* | 255

## Slide 127
Routing Information Protocol - RIP/RIP2
Routing Information Protocol (RIP) is a dynamic routing protocol which uses hop count as a routing metric to find the best path between the source and the destination network
It is a distance vector routing protocol which has an administrative distance (AD) value 120 and works on the application layer of OSI model
RIP uses port number 520
It is an Interior Gateway Protocol (IGP)

## Slide 128
Hop Count
Hop count is the number of routers occurring in between the source and destination network
The path with the lowest hop count is considered as the best route to reach a network and therefore placed in the routing table
RIP prevents routing loops by limiting the number of hopes allowed in a path from source and destination
The maximum hop count allowed for RIP is 15 and hop count of 16 is considered as network unreachable

## Slide 129
Features of RIP
Updates of the network are exchanged periodically
Updates (routing information) are always broadcast
Full routing tables are sent in updates
Routers always trust on routing information received from neighbor routers
This is also known as ‘Routing on rumours’
RIP requires routers to send the entire routing table to neighbours every 30 seconds

## Slide 130
RIP versions
RIP v1 | RIP v2 | RIPng
Sends update as broadcast | Sends update as multicast | Sends update as multicast
Broadcast at 255.255.255.255 | Multicast at 224.0.0.9 | Multicast at FF02::9 (RIPng can only run on IPv6 networks)
Doesn’t support authentication of update messages | Supports authentication of RIPv2 update messages | –
Classful routing protocol | Classless protocol, supports classful | Classless updates are sent
RIP v1 is known as Classful Routing Protocol because it doesn’t send information of subnet mask in its routing update RIP v2 is known as Classless Routing Protocol because it sends information of subnet mask in its routing update

## Slide 131
RIP-NG
RIP-ng is an extension of RIP developed for support of IPv6
Features:
  just like RIP for IPv4, it uses hop count as the metric
  sends updates every 30 seconds
  RIPng messages use the UDP port 521 and the multicast address of FF02::9

## Slide 132
OSPF
Routers connect networks using the Internet Protocol (IP), and OSPF (Open Shortest Path First) is a router protocol used to find the best path for packets as they pass through a set of connected networks
OSPF is an Interior Gateway Protocols (IGPs): that is, protocols aimed at traffic moving around within a larger autonomous system network like a single enterprise's network, which may in turn be made up of many separate local area networks linked through routers
The OSPF routing protocol has largely replaced the older Routing Information Protocol (RIP) in corporate networks

## Slide 133
OSPF
Routers that use OSPF learns about changes to the network
It reads the routing table, learns of a change, and immediately broadcasts it to all other OSPF hosts in the network
OSPF sends only the part that has changed and only when a change has taken place
When routes change -- sometimes due to equipment failure -- the time it takes OSPF routers to find a new path between endpoints with no loops (which is called "open") and that minimizes the length of the path is called the convergence time

## Slide 134
OSPF
Rather than simply counting the number of router hops between hosts on a network, as RIP does, OSPF bases its path choices on "link states"
This takes into account additional network information, including IT-assigned cost metrics that give some paths higher assigned costs
OSPF has RIP support built in both for router-to-host communication and for compatibility with older networks using RIP as their primary protocol

## Slide 135
OSPF v2
A routing protocol which is described in RFC 2328
OSPFv2 is an IGP
See previous slides
(OSPF v1 (RFC1131) has never gone beyond the experimental stage)

## Slide 136
OSPFv3
OSPFv3 is the Open Shortest Path First routing protocol for IPv6
It is similar to OSPFv2 in its concept of a link state database, intra- and inter-area, and AS external routes and virtual links
OSPFv3 still establishes neighbour adjacencies, has areas, different network types, the same metrics, runs SPF, etc.
There are however some differences
  OSPFv2 runs on top of IPv4 and since OSPFv3 runs on IPv6, some changes had to be made

## Slide 137
OSPF Differences

## Slide 138
3.2 Compare the differences between static and dynamic routing
A candidate should be able to:
• Explain the static and dynamic routing.
• Compare static and dynamic routing.
• Explain the advantages and disadvantages of static and dynamic routing such as security, complexity / simplicity, resilience and scalability.

## Slide 139
Static And Dynamic Routing
Routers are designed to communicate with each other and to share information about networks
Routers can be configured to work with static and dynamic routes

## Slide 140
Static Routing
A Static route is a route that is manually entered by a network administrator
This is known as non-adaptive routing because the router will always use this static route when sending data
  The data path is predetermined by the administrator
Static routes are useful for network security
A fault with any of the routes requires the system administrator to go to the affected routers and make the required changes to get the system working again
The overuse of static routing is not recommended because the main function of a router is to learn and devise new paths for data in the event of system failures

## Slide 141
Dynamic Routing
Most routers are dynamic with the capability of being statically configured
Dynamic routing involves the regular communication of routers with other routers
Allows the routers to learn and adapt to a changing environment
This is the embodiment of packet switching with routers automatically adapting to network changes and even system failures

## Slide 142
4. Network Performance (30%, K3)
In this key topic, the apprentice will describe and explain the factors that affect network performance. Outcomes should include an ability to:
4.1 Demonstrate the relationship between factors that affect network performance
4.2 Explain methods of improving network performance

## Slide 143
4.1 Demonstrate the relationship between factors that affect network performance
Bandwidth
Number of users
Nature
Contention
A candidate should be able to:
• Describe the factors affecting network performance (such as Bandwidth, Number of users, Nature of traffic, traffic contention) and explain how they affect performance.
• Explain the interaction between the factors (e.g. how a change in one factor will affect other factors).

## Slide 146
4.2 Explain methods of improving network performance, such as traffic shaping, architecture and network policy
A candidate should be able to:
• Explain methods of network management such as traffic shaping, network architecture and network policies.
• Explain the effects of network management on users.
• Explain common causes of sub-optimal network performance such as bottlenecks and streaming.
Notes: Highlight the security and cyber aspects in this section as well.
In the management part, look at standard management procedures, and then look at some SIEM stuff