## Slide 1: BCS Level 4 Certificate in Network and Digital Communications Theory
QAN 603/0703/1

## Slide 2: Networking Basics

## Slide 3: No Connection
Single user
No connection
Very secure

## Slide 4: Connection
Two users
Crossover cable
Full duplex
  Transmit and receive at the same time
OSI layer 1 – Physical
  Transmission of bits
100010100101010

## Slide 5: Hub
Two or more users
A single network segment
Straight cables
OSI layer 1 – Physical
  Transmission of bits
Hub
  Amplifies signal
  Broadcasts input on all outputs
  Clients reject inputs not for them
  Half duplex – transmit or receive
  Poor performance
101001
101001
101001
101001

## Slide 6: MAC (Media Access Control) Addressing
Uniquely identifies a network interface controller (NIC)
MAC addresses are used as a network address for Ethernet and Wi-Fi
Addresses are assigned by the manufacturer and stored in the NIC’s read-only memory or firmware
It is a 48-bit address for 281,474,976,710,656 possible MAC addresses (normally shown as 6 octets) ether 4a:00:02:00:ca:e0 (from ifconfig)
ipconfig or ifconfig commands show the MAC address

## Slide 7: Packets and frames
A MAC address allows data to be directed to a specific device
The data segment is called a frame
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
FRAME |  |  |  |  |  | 

## Slide 8: Switch
Two or more users
A single network segment
Straight cables
OSI layer 2 – Data Link
  Transmission of packets
Switch
  Amplifies signal
  Directs inputs to correct outputs
  Full duplex
  Best performance
  Error checking
101001
111011
101001
111011

## Slide 9: Switch operation
Works on the Layer 2 Header
  Uses the source and destination MAC addresses to make its forwarding decisions.
MAC Address Table
  maps the switch’s ports to MAC addresses
  the source address and the port a frame was received on are entered in the MAC Address Table.
  as each connected device sends a frame the table gets fully populated
  the table is then used to forward frames to their intended destination

## Slide 10: Local Area Network
When the area covered is small, such as an office, this is known as a Local Area Network (LAN)
Devices connected to the switches are called Hosts
The hosts are typically clients, servers or LAN attached peripherals, such as printers
A LAN can be wired or wireless
Switches can be cascaded to increase the number of hosts

## Slide 11: Increasing the number of hosts
Adding switches is inefficient (inactive hosts are flushed from the MAC address table after 300s)
Adding hosts increases traffic congestion on the LAN (more collisions and failed transmissions)
Adding hosts means increased processing loads
The solution is to create additional physical networks

## Slide 12: IP addresses
A MAC address is physical, it allows packets to be delivered from one NIC to another (hop to hop)
IP addresses are logical and allow delivery of packets across networks (from end to end)
IP addresses work at OSI layer 3 – Network
An address is a 32 bit binary number represented as 4 octets
  E.g. 192.168.1.123 (IP v4)
Destination and source IP addresses are added to the data payload of the ethernet packet

## Slide 13: Packets with IP addresses
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
PACKET |  |  |  |  |  | 
Source IP address | Destination IP address
4 bytes | 4 bytes

## Slide 14: Two networks
192.168.1.12
192.168.2.7
Router
A
B
R1 NIC
R2 NIC
Source MAC | Destination MAC | Source IP | Destination IP
Host A | Router R1 | 192.168.1.12 | 192.168.2.7
Source MAC | Destination MAC | Source IP | Destination IP
Router R2 | Host B | 192.168.1.12 | 192.168.2.7
X
192.168.1.9

## Slide 15: ARP Address Resolution Protocol
Used to find the MAC address for a given IP
Host A (192.168.1.12) needs to send to Host B (192.168.2.7)
It knows 192.168.2.7 is in a different network
It has a default gateway of 192.168.1.1 (the router)
It sends a broadcast ARP message (MAC ff:ff:ff:ff:ff:ff) for 192.168.1.1 (this goes to all hosts on the network)
Only the router replies with its Mac and IP addresses
Host A updates its ARP table
Sends packet to 192.168.2.7 with router MAC address

## Slide 16: ARP table

## Slide 17: Router Table In Host A (192.168.1.12)
  Contains a 0.0.0.0 entry which points to the default gateway 192.168.1.1
  Contains other IP addresses on its own network and the address of its own NIC
  If sending to Host X it will look in the table and send directly
  If sending to Host B (192.168.2.7) will find 0.0.0.0 as the closest match in the table and send to the gateway
Network Destination | Gateway | Interface | Notes
0.0.0.0 | 192.168.1.1 | 192.168.1.12 | 
127.0.0.1 | On-Link | 127.0.0.1 | Loopback
192.168.1.9 | On-Link | 192.168.1.12 | Host X

## Slide 18: Router’s Table
  Contains a list of IP addresses and interfaces
  If sending to 192.168.1.n will forward via R1 NIC
  If sending to 192.168.2.n will forward via R2 NIC /24 refers indirectly to the number of hosts on the network and is covered in subnetting (not in the BCS Cloud syllabus)
IP address | Interface
192.168.1.0/24 | R1 NIC
192.168.2.0/24 | R2 NIC

## Slide 19: Windows Network Utilities
Ping
  Tests connectivity
  ping 192.168.2.7
ARP
  Shows MAC addresses for IP addresses

## Slide 20: IP addresses
IP address classes
  Class D is used for multicast (224-239)
  Class E is experimental (240-255)
One class A address is worth 16M hosts
Therefore a way is needed to allocate significantly more hosts than are available
Address class | First octet range | Number of hosts
A | 1-126 | 16M
B | 128-191 | 64k
C | 192-223 | 254

## Slide 21: Private IP addresses
  Address ranges allocated as private, therefore not permissible onto the general internet.
  So, an organisation can have one outward facing IP address and up to 16M hosts inside
  This is done using network address translation (explained later)
Address range | Number of hosts
10.0.0.0 – 10.255.255.255 | 16M
172.16.0.0 – 172.31.255.255 | 1M
192.168.0.0 – 192.168.255.255 | 64K

## Slide 22: Setting IP addresses
  Assume a small system with 192.168.1.n addresses
  Static addresses are set on the device
  Dynamic addresses are leased by a DHCP server
IP address | Host | Type
192.168.1.1 | Router | Static
192.168.1.10 | Server | Static
192.168.1.20 | Printer | Static
192.168.1.100 - 200 | Desktops | Dynamic

## Slide 23: DHCP Dynamic Host Configuration Protocol
  Host sends a discovery request (255.255.255.255) for a DHCP server
  Server responds with a lease offer of an IP address, gateway address, duration and DNS server address (see later for DNS)
  Host responds with a request to accept the offered lease
  Server acknowledges the request
  Host configures its network interface with the agreed parameters

## Slide 24: DHCP Windows Configuration
  Static Dynamic

## Slide 25: Recap
Hosts have MAC and IP addresses
They can communicate in the same network using switches and MAC addressing
To communicate between networks they use routers and IP addresses
Private IP addresses allow duplicate usage in different organisations, but are not allowed on the internet
IP addresses can be manually configured or obtained by DHCP

## Slide 26: Internet connection
Connection to the ISP
  ADSL
  Cable
  Satellite
  Cellular
  Leased line
ISP supplies:
  IP address via DHCP
  DNS address

## Slide 27: ISP IP addresses
An ISP will allocate an IP address from a range it owns
These IP addresses are unique on the internet
Gloucester College IP address is 212.219.57.69
All internet traffic to and from Gloucester College is via the IP address 212.219.57.69
Internal IP addresses at the college will be from the private IP addresses ranges
How does traffic for a private IP address get to the right host?

## Slide 28: Network and port address translation (NAT and PAT)
Implemented in the router
Allows many hosts on the internal network to connect via one public IP address
Allows many applications on one host to communicate with many services in the cloud
Uses IP and port numbers

## Slide 29: Ports
An IP address and a port address make up a socket
  Eg 212.219.57.69:80 (Gloucester college HTTP port)
An application, service or process uses the socket to send and receive data via the network – OSI Layer 4 Transport
The operating system
  transmits the data from all application ports on to the network
  directs received packets to the matching IP address and port number

## Slide 30: Port allocation
Well known ports 0-1023
  Examples
    21 FTP
    25 SMTP
    80 HTTP
    110 POP3
    443 HTTPS
Registered ports 1024-49151
Dynamic ports 49152-65535

## Slide 31: Packets with IP addresses and port numbers
Preamble | Start of frame delimiter | Destination | Source | Length | Data | CRC
Timing |  | MAC Addressing |  | Amount of data | Payload | Checksum
7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes
PACKET |  |  |  |  |  | 
Source IP address | Destination IP address | Source port number | Destination port number
4 bytes | 4 bytes | 2 bytes | 2 bytes

## Slide 32: Browser request
Host | Router client side | Router ISP side | Cloud service
S 192.168.1.12:3333 D 216.58.218.206:80 | 192.168.1.12:3333 | 212.219.57.69:7777 | S 212.219.57.69:7777 D 216.58.218.206:80
Host inserts random source port number
Router translates internal network IP address to the external network address and port
Router updates translate table and records port numbers

## Slide 33: Server response
Cloud service | Router ISP side | Router client side | Host
S 216.58.218.206:80 D 212.219.57.69:7777 | 212.219.57.69:7777 | 192.168.1.12:3333 | S 216.58.218.206:80 D 192.168.1.12:3333
Server puts source address from received packet into destination address of outbound packet
Router translates external network IP address to the internal network address and port
Host receives packet and OS directs to correct application

## Slide 34: Domain Name System
Translates domain names to IP addresses
A host will query a domain name server (address from DHCP) with the domain name (eg www.techrepublic.com)
DNS server returns the IP address
Windows command: nslookup

## Slide 35: Recap
Internal networks connect to the internet via ISP
The ISP allocates an IP address
Network address translation (NAT) allows private IP addressing
Port address translation (PAT) allows multiple applications to connect to cloud services
DNS allows memorable names to be used for cloud resources

## Slide 36: 1. Network Data and Protocols (20%, K2)
In this key topic, the apprentice will describe and explain the common networks in use and their associated data formats, protocols and related performance issues. Outcomes should include an ability to:
1.1 Describe data formats and protocols in current use
1.2 Explain features of network protocols in widespread use on the Internet
1.3 Identify network failure modes and reasons why networks ‘hang’
1.4 Describe approaches to error control in a network

## Slide 37: 1.1 Describe data formats and protocols in current use
A candidate should be able to:
• Explain what is meant by data and protocol.
• Explain the relationship between data and protocol.
• Explain the technical specification of data formats and protocols.
• Describe the main features of data formats and protocols such as syntax, synchronisation, error recovery methods and error detection.
• Identify what data formats and protocols are in current use such as PPP, 802.3 and SLIP.
• Recognise protocol diagrams such as UML and Time-Sequence.

## Slide 38: Data
Data is information that has been translated into a form that is efficient for movement or processing
Relative to today's computers and transmission media, data is information converted into binary digital form
It is acceptable for data to be used as a singular subject or a plural subject
Raw data is a term used to describe data in its most basic digital format
At its most rudimentary level, data is usually in the form of ones and zeros, known as binary data
As all computer data is in binary format, it can be created, processed, saved, and stored digitally
Allows data to be transferred from one computer to another using a network connection or various media devices
Does not deteriorate over time or lose quality after being used multiple times

## Slide 39: Protocol
Network protocols are formal standards and policies comprised of rules, procedures and formats that define communication between two or more devices over a network
Network protocols govern the end-to-end processes of timely, secure and managed data or network communication
These rules include what type of data may be transmitted, what commands are used to send and receive data, and how data transfers are confirmed
Notes: You can think of a protocol as a spoken language. Each language has its own rules and vocabulary. If two people share the same language, they can communicate effectively. Similarly, if two hardware devices support the same protocol, they can communicate with each other, regardless of the manufacturer or type of device. For example, an Apple iPhone can send an email to an Android device using a standard mail protocol.

## Slide 40: Protocols
Protocols exist for several different applications
Examples include wired networking (e.g., Ethernet), wireless networking (e.g., 802.11ac), and Internet communication (e.g., IP)
The Internet protocol suite, which is used for transmitting data over the Internet, contains dozens of protocols
May be broken up into four categories:
  Link layer - PPP, DSL, Wi-Fi, etc.
  Internet layer - IPv4, IPv6, etc.
  Transport layer - TCP, UDP, etc.
  Application layer - HTTP, IMAP, FTP, etc

## Slide 41: ISO Model
Application
(Host-to-host) Transport
Internet
Network Interface
(Hardware)
TCP/IP Model Layers
Notes: The TCP/IP architectural model has four layers that approximately match six of the seven layers in the OSI Reference Model. The TCP/IP model does not address the physical layer, which is where hardware devices reside. The next three layers—network interface, internet and (host-to-host) transport—correspond to layers 2, 3 and 4 of the OSI model. The TCP/IP application layer conceptually “blurs” the top three OSI layers. It’s also worth noting that some people consider certain aspects of the OSI session layer to be arguably part of the TCP/IP host-to-host transport layer.

## Slide 42: Link Layer Protocols
Establish communication between devices at a hardware level
In order to transmit data from one device to another, each device's hardware must support the same link layer protocol

## Slide 43: Internet Layer Protocols
Used to initiate data transfers and route them over the Internet

## Slide 44: Transport Layer Protocols
Define how packets are sent, received, and confirmed

## Slide 45: Application Layer Protocols
Contain commands for specific applications
For example, a web browser uses HTTPS to securely download the contents of a webpage from a web server
An email client uses SMTP to send email messages through a mail server.

## Slide 46: Data Formats
A data format or file format is the format in which the data is coded
The information is coded in such a way that a program or application can recognize, read and use the data
Data transmission occurs:
  In the form of bits (1’s and 0’s)
  Light
  Radio
  Microwave
Can be analogue or digital
Data can be compressed and decompressed

## Slide 47: Data Formats - Microwave
Uses a beam of radio waves in the microwave frequency range (6GHz to 8.2GHz) to transmit information between two fixed locations on the earth
Beams are unidirectional
Have high loss due to high frequency
Max distance ~40km
Use line of sight

## Slide 48: Data Formats - Light
Can be laser (Light Amplification by Stimulated Emission of Radiation) (ultraviolet) or normal white light
Ultraviolet waves have wavelengths of 400 to 700 nm
Can be transmitted along optic fibre

## Slide 49: Loss of data
Data can become unusable in three different ways:
  Loss of bits The carrier is damaged, is lost of its quality deteriorates in such a way that it effect the bits, popularly called 'bit rot‘
  Loss of documentation It is unclear how one file is tied to another, for instance when different versions of a file or the metadata are no longer available, leaving the meaning of the data unclear
  Loss of display possibilities The operating system, the hardware or the application are no longer present or cannot be used anymore. That can also be caused by external factors such as computer virus, fire or accidental deleting of files.

## Slide 50: 1.2 Explain features of network protocols in widespread use on the Internet.
Including, but not limited to:
HTTPS HTTP SMTP SNMP TCP UDP IP

## Slide 51: HTTP
HTTP is a simple but powerful protocol:
  HTTP is connectionless
  HTTP is media independent
  HTTP is stateless
HTTP is not secure as it is not encrypted
HTTP operates at the highest layer of the TCP/IP model, the Application layer

## Slide 52: HTTPS
HTTPS is an extension of the Hypertext Transfer Protocol (HTTP)
It is used for secure communication over a computer network, and is widely used on the Internet
HTTPS is not a separate protocol, but refers to use of ordinary HTTP over an encrypted SSL/TLS connection
Operates at the Application layer, as does the TLS security protocol (operating as a lower sublayer of the same layer)
The TLS protocol performs the encryption
HTTPS connections uses a public key certificate for the web server
This certificate must be signed by a trusted certificate authority for the web browser to accept it without warning

## Slide 53: SMTP
The primary job of the Simple Mail Transfer Protocol (SMTP) is to implement the TCP/IP electronic mail delivery system
SMTP includes a number of other features and capabilities
These allow SMTP to support special requirements and auxiliary needs of the mail system, and are described in detail in RFC 2821
  Mail relaying
  Mail forwarding
  Mail Gatewaying
  Address debugging
  Mailing list expansion
  Turning
Notes: Mail Relaying: As discussed in the SMTP communication overview, the protocol was once widely used in a “relaying mode” where e-mail was routed from one SMTP server to another to reach its destination. Today, the normal method of e-mail transfer on the Internet today is directly from the sender's SMTP server to the recipient's, using DNS MX records to determine the recipient SMTP server address. SMTP still includes the ability to relay mail from one server to another, provided certain conditions are met. Note that in addition to the inefficiency of relaying, many servers won't relay mail because this feature has been abused for spamming and hacking.
Mail Forwarding: Under certain conditions, an SMTP server may agree to accept e-mail for a non-local mailbox and forward it to the appropriate destination. This sounds similar to relaying but is used in a different way. A common example is when a user changes his or her e-mail address. If I have worked at XYZ Industries for years and then retire, the company may no longer wish to let me receive e-mail at the company's SMTP server. As a courtesy, however, they may forward e-mail sent to me there so I still receive it at my new company.
Mail Gatewaying: Certain SMTP servers may be configured as e-mail gateways. These devices “translate” TCP/IP e-mail into a form suitable for another e-mail system, and vice-versa. Gatewaying is a complex topic because e-mail systems can be so different; one of the more important problems is the inconsistency of addressing methods of different e-mail systems.
Address Debugging: SMTP includes a VRFY (verify) command, which can be used to check the validity of an e-mail address without actually sending mail to it.
Mailing List Expansion: The SMTP command EXPN (expand) can be used to determine the individual e-mail addresses associated with a mailing list. (Note however that this has nothing directly to do with mailing list software like Majordomo.)
“Turning”: The original SMTP protocol included a command that allows the SMTP sender and SMTP receiver to change roles. This could be used to allow SMTP server A to send e-mail to server B, and then have B send e-mail it has queued for A in the same session. In practice, this capability was not widely used for a variety of reasons, including security considerations. It is now officially “not recommended”, but may still be implemented in some SMTP software.

## Slide 54: SMTP
Proxy | Name
SOCKS4 | SOCKS4 proxy.
SOCKS4A | SOCKS4A proxy (capable of resolving domain names).
SOCKS5 | SOCKS5 proxy.
HTTP CONNECT | HTTP proxy using CONNECT method.
The SMTP class supports the following Proxy servers:

## Slide 55: SNMP
Simple Network Management Protocol” is a communications protocol through which an admin, via manager systems and authorized agents, can monitor and even manipulate some aspects of a networks configuration and traffic
SNMP is an open internet standard for managing networked devices (systems)
three versions of SNMP that define approved standards:
  SNMPv1
  SNMPv2 (also known, and referred to in this document, as SNMPv2c)
  SNMPv3

## Slide 56: SMNP
Main features:
  Managers and Agents
    SNMP is a network protocol that allows devices to be managed remotely by a network management station (NMS), also commonly called a manager.
    To be managed, a device must have an SNMP agent associated with it. The purpose of the agent is to:
      Receive requests for data representing the state of the device from the manager, and provide an appropriate response
      Accept data from the manager to enable control of the device state
      Generate SNMP traps, which are unsolicited messages sent to one or more selected mangers to signal significant events relating to the device

## Slide 57: SMNP
Main Features (cont):
  Management Information Base
    To manage and monitor a device, its characteristics must be represented using a format known to both the agent and the manager
    These characteristics can represent physical properties such as fan speeds, or services such as routing tables
    The data structure defining these characteristics is known as a management information base (MIB)
  In response to a get operation, the agent provides data, either maintained locally or directly from the managed device
  In response to a set operation, the agent typically performs some action affecting the state of either itself or the managed device

## Slide 58: SMNP
Main Features (cont):
  MIB Tables
    Much of the data content defined by MIBs is in tabular form, and organized as entries consisting of a sequence of objects, each with its own OIDs. For example, a table of fan characteristics could consist of a number of rows, one per fan, with each row containing columns corresponding to the current speed, the expected speed, and the minimum acceptable speed
    The addressing of the rows within the table can be as follows:
      Simple, single-dimensional index (a row number within the table, for example `6')
      More complex, multidimensional, instance specifier such as an IP address and port number (for instance, 127.0.0.1, 1234)

## Slide 59: SMNP
Main Features (cont):
  Access Control
    All addressable objects defined in the MIB have associated maximum access rights, for instance, read-only or read-write
    These determine the maximum access the agent can support, and can be used by the manager to restrict the operations it will permit the operator to attempt
    The agent is able to apply lower access rights as required, that is, it is able to refuse writes to objects that are considered read-write
    This refusal can be on the basis of:
      How applicable the operation is to the object being addressed (for example, where an object defined by the MIB represents a state machine for which only certain transactions are legal)
      Security restrictions that limit certain operations to restricted sets of managers

## Slide 60: TCP
Transmission Control Protocol (TCP - RFC 793) is considered as a reliable protocol
Transmission Control Protocol (TCP) is responsible for breaking up the message (Data from application layer) into TCP Segments and reassembling them at the receiving side
It is not sure that the data reaching at the receiving device is in the same order as the sending side, because of the problems in network or different paths packets flow to the destination
TCP is responsible for keeping the unordered segments in the right order
TCP assures a reliable delivery by resending anything that gets lost while traveling the network

## Slide 61: TCP - Characteristics
Stream Data transfer:
  Applications working at the Application Layer transfers a contiguous stream of bytes to the bottom layers
  It is the duty of TCP to pack this byte stream to packets, known as TCP segments, which are passed to the IP layer for transmission to the destination device
  The application does not have to bother to chop the byte stream data packets

## Slide 62: TCP - Characteristics
Reliability:
  The most important feature of TCP is reliable data delivery. In order to provide reliability, TCP must recover from data that is damaged, lost, duplicated, or delivered out of order by the Network Layer
  TCP assigns a sequence number to each byte transmitted, and expects a positive acknowledgment (ACK) from the receiving TCP layer
  If the ACK is not received within a timeout interval, the data is retransmitted
  The receiving TCP uses the sequence numbers to rearrange the TCP segments when they arrive out of order, and to eliminate duplicate TCP segments

## Slide 63: TCP - Characteristics
Flow control:
  Network devices operate at different data rates because of various factors like CPU and available bandwidth
  It may happen a sending device to send data at a much faster rate than the receiver can handle
  TCP uses a sliding window mechanism for implementing flow control
  The number assigned to a segment is called the sequence number and this numbering is actually done at the byte level
  The TCP at the receiving device, when sending an ACK back to the sender, also indicates to the TCP at the sending device, the number of bytes it can receive (beyond the last received TCP segment) without causing serious problems in its internal buffers

## Slide 64: TCP - Characteristics
Multiplexing:
  Multitasking achieved through the use of port numbers
Connections:
  Before application processes can send data by using TCP, the devices must establish a connection
  The connections are made between the port numbers of the sender and the receiver devices
  A TCP connection identifies the end points involved in the connection
  A socket number is a combination of IP address and port number, which can uniquely identify a connection
Full duplex:
  TCP provides for concurrent data streams in both directions

## Slide 65: IP
Internet Protocol
Principal communications protocol in the Internet protocol suite for relaying datagrams across network boundaries
Its routing function enables internetworking, and essentially establishes the Internet
Addressing
  IP packet headers contain addresses that identify the sending computer and the receiving computer
  Routers use this information to guide each packet across communication networks and connect the sending and receiving computers

## Slide 66: IP
Reassembly
  Internet Protocol keeps track of the way messages between computers are broken into packets
  Since most messages are too big to fit in one packet, and since packets aren't sent in any organized order, they must be reassembled as they arrive at the recipient
  IP dictates how packets are reassembled into usable messages

## Slide 67: IP – Frame Format

## Slide 68: TCP/IP
TCP/IP is a set of protocols (Protocol Suit) that enable communication between computers
It is a tested and proved protocol suit
Features:
  Multi-vendor support
  Iteroperability
  Logical addressing
  Routability
  Name resolution
  Error control and flow control
  Multiplexing/de-multiplexing
Notes: 1) Multi-Vendor Support. TCP/IP is implemented by many hardware and software vendors. It is an industry standard and not limited to any specific vendor.
2) Interoperability. Today we can work in a heterogeneous network because of TCP/IP. A user who is sitting on a Windows box can download files from a Linux machine, because both Operating Systems support TCP/IP. TCP/IP eliminates the cross-platform boundaries.
3) Logical Addressing. Every network adapter has a globally unique and permanent physical address, which is known as MAC address (or hardware address). The physical address is burnt into the card while manufacturing. Low-lying hardware-conscious protocols on a LAN deliver data packets using the adapter's physical address. The network adapter of each computer listens to every transmission on the local network to determine whether a message is addressed to its own physical address.
For a small LAN, this will work well. But when your computer is connected to a big network like internet, it may need to listen to millions of transmissions per second. This may cause your network connection to stop functioning.
To avoid this, network administrators often segment (divide) big networks into smaller networks using devices such as routers to reduce network traffic, so that the unwanted data traffic from one network may not create problem in another network. A network can be again subdivided into smaller subnets so that a message can travel efficiently from its source to the destination. TCP/IP has a robust subnetting capability achieved using logical addressing. A logical address is an address configured through the network software. The logical addressing system used in TCP/IP protocol suit is known as IP address.
4) Routability. A router is a network infrastructure device which can read logical addressing information and direct data across the network to its destination.TCP/IP is a routable protocol, which means the TCP/IP data packets can be moved from one network segment to another.
5) Name Resolution. IP addresses are designed for the computers and it is difficult for humans to remember many IP addresses. TCP/IP allows us to use human-friendly names, which are very easy to remember (Ex. www.omnisecu.com). Name Resolutions servers (DNS Servers) are used to resolve a human readable name (also known as Fully Qualified Domain Names (FQDN)) to an IP address and vice versa.
6) Error Control and Flow Control.The TCP/IP protocol has features that ensure the reliable delivery of data from source computer to the destination computer. TCP (Transmisssion Control Protocol) defines many of these error-checking, flow-control, and acknowledgement functions.
7) Multiplexing/De-multiplexing. Multiplexing means accepting data from different applications and directing that data to different applications listening on different receiving computers. On the receiving side the data need to be directed to the correct application, for that data was meant for. This is called De-multiplexing. We can run many network applications on the same computer. By using logical channels called ports, TCP/IP provides means for delivering packets to the correct application. In TCP/IP, ports are identified by using TCP or UDP port numbers.

## Slide 69: TCP – Frame Format

## Slide 70: UDP
User Datagram Protocol
  Provides connectionless, unreliable service
  So UDP faster than TCP
  Adds only checksum and process-to-process addressing to IP
  Used for DNS and NFS
  Used when socket is opened in datagram mode
  It sends bulk quantity of packets
  No acknowledgment
  Good for video streaming: it is an unreliable protocol

## Slide 71: UDP – Frame Format

## Slide 72: 1.3 Identify network failure modes and reasons why networks ‘hang’
A candidate should be able to:
• Describe failure modes in protocols.
• Describe the effect on a protocol of data communication errors.
• Describe causes for network failures.
• Explain the causes for system 'hangs'.

## Slide 73: Failure Modes in Protocols

## Slide 74: The Effect On A Protocol Of Data Communication Errors
Error control is the technique of detecting and correcting blocks of data during communication
It checks the reliability of characters both at the bit level and packet level
If proper error control is in place, transmitted and received data is ensured to be identical, as in many cases communication channels can be highly unreliable
Data can be corrupted while in transmission
In order to retain reliable communication, errors must be detected and corrected
Forward error control and feedback error control are the two types of error-control mechanisms used in communications

## Slide 75: Causes for Network Failures
Misconfiguration
Security breaches
Old equipment
Human error
Incompatible changes
Hardware failures
Power failures

## Slide 76: Causes for System 'Hangs'
CPU
RAM
NIC failure
Overheating
Software errors
Electrical problems
Environment

## Slide 77: 1.4 Describe approaches to error control in a network
A candidate should be able to:
• Describe at least one approach to error control in a network such as; forward error control, feedback error control and block error control.
• Identify methods of error control, such as checksum, parity and redundancy.

## Slide 78: Forward Error Control
In forward error control, additional redundant information is also transmitted along with the data
This helps the receiver to detect and determine the location of the error in the transmitted data
Forward error control is less commonly used due to the amount of additional redundant information which is transmitted.

## Slide 79: Feedback Error Control
In backward or feedback error control, along with each character, a little additional information is provided for the detection of errors
The receiver in this technique performs no error correction
If the received data is found to contain errors, the entire data is retransmitted

## Slide 80: Methods of Error Control
Checksum
Parity
Redundancy

## Slide 81: Checksum
A checksum is an error-detection method in a the transmitter computes a numerical value according to the number of set or unset bits in a message and sends it along with each message frame
At the receiver end, the same checksum function (formula) is applied to the message frame to retrieve the numerical value
A checksum error means there was a problem with the serial communications
A checksum is created based on the data values in the data blocks to be transmitted using some algorithm and appended to the data
When the receiver gets this data, a new checksum is calculated and compared with the existing checksum
A non-match indicates an error

## Slide 82: Parity
Historically the most commonly used data integrity method
Parity can detect - but not correct - single-bit errors
Error Correction Code (ECC) is a more comprehensive method of data integrity checking that can detect and correct single-bit errors

## Slide 83: Redundancy
Cyclic Redundancy Check (CRC):
  CRC is based on binary division.
  A sequence of redundant bits called CRC or the CRC remainder is appended to the end of a data unit, so that the resulting data unit becomes exactly divisible by a second, predetermined binary number
  At its destination, the incoming data unit is divided by the same number
  If at this step there is no remainder, the data unit is assumed to be intact and therefore is accepted

## Slide 84: End of Day 1