## Slide 1: 2. Layered Network Models (20%, K2)
In this key topic, the apprentice will be able to explain network layer models and then contrast their differences. Outcomes should include an ability to:
2.1 Explain features layered network models
2.2 Compare the differences between the following physical layer categories and datalink layer protocols

## Slide 2: 2.1 Explain features of the following layered network models:
  TCP/IP Reference Model
  OSI 7 Layer Model

## Slide 3: OSI
Systems must be developed which are compatible to communicate with each other ISO has developed a standard
ISO stands for International organization of Standardization
This is called a model for Open System Interconnection (OSI) and is commonly known as OSI model
The ISO-OSI model is a seven layer architecture. It defines seven layers or levels in a complete communication system
They are:
  Application Layer
  Presentation Layer
  Session Layer
  Transport Layer
  Network Layer
  Datalink Layer
  Physical Layer

## Slide 4: Feature of OSI Model
Big picture of communication over network is understandable through this OSI model
We see how hardware and software work together
We can understand new technologies as they are developed
Troubleshooting is easier by separate networks
Can be used to compare basic functional relationships on different networks

## Slide 5: Functions of Different Layers
Following are the functions performed by each layer of the OSI model
This is just an introduction, we will cover each layer in details in the coming tutorials

## Slide 6: OSI Model Layer 1: The Physical Layer
Physical Layer is the lowest layer of the OSI Model.
It activates, maintains and deactivates the physical connection.
It is responsible for transmission and reception of the unstructured raw data over network.
Voltages and data rates needed for transmission is defined in the physical layer.
It converts the digital/analog bits into electrical signal or optical signals.
Data encoding is also done in this layer.

## Slide 7: OSI Model Layer 2: Data Link Layer
Data link layer synchronizes the information which is to be transmitted over the physical layer
The main function of this layer is to make sure data transfer is error free from one node to another, over the physical layer
Transmitting and receiving data frames sequentially is managed by this layer.
This layer sends and expects acknowledgements for frames received and sent respectively
Resending of non-acknowledgement received frames is also handled by this layer
This layer establishes a logical layer between two nodes and also manages the Frame traffic control over the network
It signals the transmitting node to stop, when the frame buffers are full

## Slide 8: OSI Model Layer 3: The Network Layer
Network Layer routes the signal through different channels from one node to other
It acts as a network controller
It manages the Subnet traffic
It decides by which route data should take
It divides the outgoing messages into packets and assembles the incoming packets into messages for higher levels

## Slide 9: OSI Model Layer 4: Transport Layer
Transport Layer decides if data transmission should be on parallel path or single path
Functions such as Multiplexing, Segmenting or Splitting on the data are done by this layer
It receives messages from the Session layer above it, convert the message into smaller units and passes it on to the Network layer
Transport layer can be very complex, depending upon the network requirements
Transport layer breaks the message (data) into small units so that they are handled more efficiently by the network layer

## Slide 10: OSI Model Layer 5: The Session Layer
Session Layer manages and synchronize the conversation between two different applications.
Transfer of data from source to destination session layer streams of data are marked and are resynchronized properly, so that the ends of the messages are not cut prematurely and data loss is avoided

## Slide 11: OSI Model Layer 6: The Presentation Layer
Presentation Layer takes care that the data is sent in such a way that the receiver will understand the information (data) and will be able to use the data
While receiving the data, presentation layer transforms the data to be ready for the application layer
Languages(syntax) can be different of the two communicating systems
Under this condition presentation layer plays a role of translator
It performs Data compression, Data encryption, Data conversion etc.

## Slide 12: OSI Model Layer 7: Application Layer
Application Layer is the topmost layer
Transferring of files disturbing the results to the user is also done in this layer
Mail services, directory services, network resource etc. are services provided by application layer
This layer mainly holds application programs to act upon the received and to be sent data

## Slide 13: Merits of OSI reference model
OSI model distinguishes well between the services, interfaces and protocols
Protocols of OSI model are very well hidden
Protocols can be replaced by new protocols as technology changes
Supports connection oriented services as well as connectionless service

## Slide 14: Demerits of OSI reference model
Model was devised before the invention of protocols
Fitting of protocols is tedious task
It is just used as a reference model

## Slide 17: TCP/IP
The TCP/IP model was developed prior to the OSI model
The TCP/IP model is not exactly similar to the OSI model
The TCP/IP model consists of five layers:
  the application layer
  transport layer
  network layer
  data link layer
  physical layer
The first four layers provide physical standards, network interface, internetworking, and transport functions that correspond to the first four layers of the OSI model and these four layers are represented in TCP/IP model by a single layer called the application layer
TCP/IP is a hierarchical protocol made up of interactive modules, and each of them provides specific functionality

## Slide 18: Functions of TCP/IP layers

## Slide 19: Network Access Layer
A network layer is the lowest layer of the TCP/IP model
A network layer is the combination of the Physical layer and Data Link layer defined in the OSI reference model
It defines how the data should be sent physically through the network.
This layer is mainly responsible for the transmission of the data between two devices on the same network
The functions carried out by this layer are encapsulating the IP datagram into frames transmitted by the network and mapping of IP addresses into physical addresses
The protocols used by this layer are ethernet, token ring, FDDI, X.25, frame relay

## Slide 20: Internet Layer
An internet layer is the second layer of the TCP/IP model
An internet layer is also known as the network layer
The main responsibility of the internet layer is to send the packets from any network, and they arrive at the destination irrespective of the route they take

## Slide 21: Following are the protocols used in this layer
IP Protocol
ARP Protocol
ICMP Protocol

## Slide 22: Responsibilities of the IP protocol
IP Addressing:
This protocol implements logical host addresses known as IP addresses. The IP addresses are used by the internet and higher layers to identify the device and to provide internetwork routing.
Host-to-host communication:
It determines the path through which the data is to be transmitted.
Data Encapsulation and Formatting:
An IP protocol accepts the data from the transport layer protocol. An IP protocol ensures that the data is sent and received securely, it encapsulates the data into message known as IP datagram.
Fragmentation and Reassembly:
The limit imposed on the size of the IP datagram by data link layer protocol is known as Maximum Transmission unit (MTU). If the size of IP datagram is greater than the MTU unit, then the IP protocol splits the datagram into smaller units so that they can travel over the local network. Fragmentation can be done by the sender or intermediate router. At the receiver side, all the fragments are reassembled to form an original message.
Routing:
When IP datagram is sent over the same local network such as LAN, MAN, WAN, it is known as direct delivery. When source and destination are on the distant network, then the IP datagram is sent indirectly. This can be accomplished by routing the IP datagram through various devices such as routers.

## Slide 23: ARP Protocol
ARP stands for Address Resolution Protocol
ARP is a network layer protocol which is used to find the physical address from the IP address
The two terms are mainly associated with the ARP Protocol:
  ARP request: When a sender wants to know the physical address of the device, it broadcasts the ARP request to the network
  ARP reply: Every device attached to the network will accept the ARP request and process the request, but only recipient recognize the IP address and sends back its physical address in the form of ARP reply
  The recipient adds the physical address both to its cache memory and to the datagram header

## Slide 24: ICMP Protocol
ICMP stands for Internet Control Message Protocol
It is a mechanism used by the hosts or routers to send notifications regarding datagram problems back to the sender
A datagram travels from router-to-router until it reaches its destination. If a router is unable to route the data because of some unusual conditions such as disabled links, a device is on fire or network congestion, then the ICMP protocol is used to inform the sender that the datagram is undeliverable
An ICMP protocol mainly uses two terms:
  ICMP Test: ICMP Test is used to test whether the destination is reachable or not
  ICMP Reply: ICMP Reply is used to check whether the destination device is responding or not
The core responsibility of the ICMP protocol is to report the problems, not correct them
The responsibility of the correction lies with the sender
ICMP can send the messages only to the source, but not to the intermediate routers because the IP datagram carries the addresses of the source and destination but not of the router that it is passed to

## Slide 25: Transport Layer
The transport layer is responsible for the reliability, flow control, and correction of data which is being sent over the network

## Slide 26: Transport Layer
The two protocols used in the transport layer are User Datagram protocol and Transmission control protocol

## Slide 27: User Datagram Protocol (UDP)
  It provides connectionless service and end-to-end delivery of transmission
  It is an unreliable protocol as it discovers the errors but not specify the error
  User Datagram Protocol discovers the error, and ICMP protocol reports the error to the sender that user datagram has been damaged
  UDP consists of the following fields: Source port address: The source port address is the address of the application program that has created the message Destination port address: The destination port address is the address of the application program that receives the message Total length: It defines the total number of bytes of the user datagram in bytes. Checksum: The checksum is a 16-bit field used in error detection
  UDP does not specify which packet is lost. UDP contains only checksum; it does not contain any ID of a data segment

## Slide 28: User Datagram Protocol (UDP)

## Slide 29: Transmission Control Protocol (TCP)
It provides a full transport layer services to applications
It creates a virtual circuit between the sender and receiver, and it is active for the duration of the transmission
TCP is a reliable protocol as it detects the error and retransmits the damaged frames
Therefore, it ensures all the segments must be received and acknowledged before the transmission is considered to be completed and a virtual circuit is discarded
At the sending end, TCP divides the whole message into smaller units known as segment, and each segment contains a sequence number which is required for reordering the frames to form an original message
At the receiving end, TCP collects all the segments and reorders them based on sequence numbers

## Slide 30: Application Layer
An application layer is the topmost layer in the TCP/IP model
It is responsible for handling high-level protocols, issues of representation
This layer allows the user to interact with the application
When one application layer protocol wants to communicate with another application layer, it forwards its data to the transport layer
There is an ambiguity that occurs in the application layer
Every application cannot be placed inside the application layer except those who interact with the communication system
For example: text editor cannot be considered in application layer while web browser using HTTP protocol to interact with the network where HTTP protocol is an application

## Slide 31: Main Protocols Used in the Application Layer
HTTP: HTTP stands for Hypertext transfer protocol. This protocol allows us to access the data over the world wide web. It transfers the data in the form of plain text, audio, video. It is known as a Hypertext transfer protocol as it has the efficiency to use in a hypertext environment where there are rapid jumps from one document to another.
SNMP: SNMP stands for Simple Network Management Protocol. It is a framework used for managing the devices on the internet by using the TCP/IP protocol suite.
SMTP: SMTP stands for Simple mail transfer protocol. The TCP/IP protocol that supports the e-mail is known as a Simple mail transfer protocol. This protocol is used to send the data to another e-mail address.
DNS: DNS stands for Domain Name System. An IP address is used to identify the connection of a host to the internet uniquely. But, people prefer to use the names instead of addresses. Therefore, the system that maps the name to the address is known as Domain Name System.
TELNET: It is an abbreviation for Terminal Network. It establishes the connection between the local computer and remote computer in such a way that the local terminal appears to be a terminal at the remote system.
FTP: FTP stands for File Transfer Protocol. FTP is a standard internet protocol used for transmitting the files from one computer to another computer.

## Slide 32: 2.2 Compare the differences between the following physical layer categories and datalink layer protocols:
  Physical Layers (including, but not limited to: Wireless, Fibre, Wired)
  Data Link Layer (including, but not limited to: Ethernet [802.3], Wireless LAN [802.11], Bluetooth)

## Slide 33
Done

## Slide 34: Digital Transmission
DIGITAL-TO-DIGITAL CONVERSION
Digital-to-digital encoding is the representation of digital information by a digital signal
When binary 1s and 0s generated by the computer are translated into a sequence of voltage pulses that can be propagated over a wire, this process is known as digital-to-digital encoding

## Slide 35: ANALOG-TO-DIGITAL CONVERSION
When an analog signal is digitalized, this is called an analog-to-digital conversion
Suppose human sends a voice in the form of an analog signal, we need to digitalize the analog signal which is less prone to noise
It requires a reduction in the number of values in an analog message so that they can be represented in the digital stream
In analog-to-digital conversion, the information contained in a continuous wave form is converted in digital pulses

## Slide 36: Techniques for Analog-To-Digital Conversion
PAM
PAM stands for pulse amplitude modulation
PAM is a technique used in analog-to-digital conversion
PAM technique takes an analog signal, samples it, and generates a series of digital pulses based on the result of sampling where sampling means measuring the amplitude of a signal at equal intervals
PAM technique is not useful in data communication as it translates the original wave form into pulses, but these pulses are not digital
To make them digital, PAM technique is modified to PCM technique

## Slide 38: PCM
PCM stands for Pulse Code Modulation
PCM technique is used to modify the pulses created by PAM to form a digital signal. To achieve this, PCM quantizes PAM pulses
Quantization is a process of assigning integral values in a specific range to sampled instances
PCM is made of four separate processes: PAM, quantization, binary encoding, and digital-to-digital encoding.

## Slide 40: End of Day 2