## Slide 1: BCS Level 4 Certificate in Network Systems and Architecture Overview
Network Engineer

## Slide 2: Aim
All apprentices must pass BCS Level 4 Certificate in Network Systems and Architecture QAN 603/0547/2
We have allocated 8 days of college to prepare you for this exam
  3 days in January (sections 8-11)
  5 days in February (sections 1-7)
  Take the exam on day 5 of the February session

## Slide 3: Exam
1 online exam lasting 1 hour
Taken in college or remote –COVID dependant
Closed book, no mobiles, smartwatches allowed
Calculators may be used
Access to desktop denied during the exam
40 questions – multiple choice
Pass mark 26/40 (65%)
Results (subject to confirmation) available immediately
Certificate available online

## Slide 4: Exam
Syllabus Area | Target number of questions
1 Load balancing failures | 1
2 Storage protocol failures | 7
3 Hardware failures | 3
4 Configuration errors | 3
5 Environmental problems | 3
6 Errors in security | 4
7 Errors resulting from lack of capacity | 5
8 Network Infrastructure Components | 6
9 Features of Client-Server Operating Systems and Applications | 4
10 Components and functions of virtualised systems | 3
11 Features of Middleware | 1
Total | 40 questions

## Slide 5: Resources
Wiki –gloscolapprenticeships.co.uk/appWiki
Presentations – On the wiki

## Slide 6: 1 Load Balancing Failures (2.5%)
1.1 Describe the causes and impact of DNS round robin failures and summarise the appropriate response for each.
    misconfiguration - loss of connection to one/all nodes;
    single/multiple node failure(s) - intermittent connection;
    all nodes fail - complete outage.
1.2 Explain causes and consequences of network load balancer failures and summarise the appropriate response for each.
    misconfiguration - loss of connection to one / some nodes increasing load on
    remaining nodes;
    misconfiguration – loss of connection to all nodes;
    single node failure - intermittent connection;
    single/multiple node failures - intermittent loss of access;
    all nodes failure - complete outage.

## Slide 7: 2 Storage Protocol Failures (17.5%)
2.1 Identify the reasons for and the impact of locally attached storage protocol failures (SATA, SCSI, SAS) and summarise the appropriate response for each.
    hardware failure - loss of access to local disk(s) and / or corruption of data
2.2 Describe the causes and impact of failures of RAID (0,1,5,10) and summarise the appropriate response for each.
    loss of single / multiple disks - reduced throughput / loss of data depending on RAID
    level and number of disk failures;
    loss of RAID controller - permanent / temporary loss of access to data

## Slide 8: 2 Storage Protocol Failures (17.5%)
2.3 Describe the causes and impact of failures of network shares and network-attached storage (NAS), and summarise the appropriate response for each.
    misconfigured firewall or protocols (NFS, SMB, TCP/IP, AFS) - complete loss of access to NAS;
    misconfigured NFS - loss of access for Linux / NAS network shares;
    misconfigured SMB - loss of access to Windows network shares;
    misconfigured AFS - loss of access for Apple systems shares;
    misconfigured authentication and/or authorisation - loss of access to some / all NAS / network shares.
2.4 Explain causes and consequences of storage area network (SAN) failures over the Fibre Channel protocol and summarise the appropriate response for each.
    single misconfigured or failed Fibre switch - increased load on remaining switches and possible reduced throughput and/or storage outage. The standard data network is unaffected;
    loss of all Fibre switches - complete loss of access to storage. The standard data network is unaffected;
    failure of a single host bus adapter (HBA) - increased load on remaining HBA on a single node and possible reduced throughput for this node or complete outage if this is the only onboard HBA.

## Slide 9: 2 Storage Protocol Failures (17.5%)
2.5 Explain causes and consequences of SAN failures over Fibre Channel over Ethernet (FCoE) and summarise the appropriate response for each.
    Single misconfiguration or failed standard switch - increased load on remaining switches and possible reduced throughput or storage outage. The standard data network may also be impacted;
    TCP/IP misconfiguration - inability for some / all nodes to access storage;
    Failure of a single network interface controller (NIC) - increased load on remaining NIC on a single node and possible reduced throughput for this node or complete outage if this is the only onboard NIC;
    Incorrect / invalid logical unit number (LUN) - inability to access logical storage device;
    Loss of network - total outage.

## Slide 10: 2 Storage Protocol Failures (17.5%)
2.6 Explain causes and consequences of SAN failures over the iSCSI and summarise the appropriate response for each
    Single misconfiguration or failed standard switch - increased load on remaining switches and possible reduced throughput or storage outage. Standard data network may also be impacted;
    TCP/IP misconfiguration - inability for some / all nodes to access storage;
    Failure of a single NIC - increased load on remaining NIC on a single node and possible reduced throughput for this node or complete outage if this is the only onboard NIC.
    Incorrect / invalid iscsi qualified name (iqn) address - inability to access logical storage device.

## Slide 11: 2 Storage Protocol Failures (17.5%)
2.7 Describe the causes and consequences of cloud storage failures and summarise the appropriate response for each; with a focus on personal and enterprise storage: OneDrive, Dropbox, Google Drive, Amazon EC2 and Microsoft Azure.
    router / ISP failure - complete loss of access;
    TCP/IP misconfiguration - inability for some / all nodes to access storage;
    misconfigured authentication / authorisation - loss of access to some / all cloud storage;
    cloud service provider failure - loss of access to data and / or loss of data.

## Slide 12: 3 Hardware Failures (7.5%)
3.1 Explain the causes and impact of computer system failures and summarise the appropriate response for each.
    memory component failure - individual node crash;
    SSD/HDD failure - system crash and possible loss of data;
    CPU failure - intermittent system crash or failure to boot on a single node;
    power supply - intermittent system crash or failure to boot on a single node;
    cooling - intermittent crash or possibly permanent damage to components.

## Slide 13: 3 Hardware Failures (7.5%)
3.2 Express the causes and impact of network failures and summarise the appropriate response for each.
    NIC failure - loss of access from/to one network node;
    switch failure - loss of access to LAN or reduction in throughput depending on redundant configuration;
    router failure - loss of access to WAN or reduction in throughput depending on redundant configuration;
    firewall - loss of access to some/all network nodes / protocols;
    web proxy - loss of access to web traffic;
    cabling - incorrect cable type (straight through / cross over);
    cabling - exceeding recommended lengths and / or EMI;
    wireless - exceeding maximum distance and / or EMI or RFI

## Slide 14: 4 Configuration Errors (7.5%)
4.1 Describe the causes and impact of incorrectly applied / faulty patches and summarise the appropriate response for each.
    intermittent problems / complete loss of function;
    failure to boot OS
4.2 Explain causes and impact of IP Addressing configuration errors and summarise the appropriate response for each; with a focus on Invalid IP address, netmask, gateway and DNS Server.
    loss of access to some / all LAN / WAN / nodes.
4.3 Describe the causes and impact of VLAN configuration errors and summarise the appropriate response for each.
    invalid VLAN tagging - loss of access to nodes / lack of necessary network isolation.

## Slide 15: 5 Environmental Problems (7.5%)
5.1 Explain causes and impact of excessive heat and summarise the appropriate response.
    intermittent restarts / complete component failure.
5.2 Describe causes and impact of a lack of power and summarise the appropriate response.
      blackout / brownout;
      intermittent problems;
      system reboots;
      complete loss of systems;
      data loss.
5.3 Describe causes and impact of EMI / RFI and summarise the appropriate response.
    network interference - loss of some / all data.

## Slide 16: 6 Errors in Security (10%)
6.1 Describe the causes and impact of backup failure and summarise the appropriate response.
    misconfigured backup / restore - loss of some / all data;
    corrupted missing / backup medium - loss of some / all data;
    fault backup / restore device - loss of some / all data.
6.2 Explain the causes and impact of malware infection and summarise the appropriate response.
    lack of user training - loss of some/all data and or reduction in work efficiency;
    insufficient anti-malware tools - loss of some / all data and / or reduction in work efficiency;
    poorly configured firewall - loss of some / all data and / or reduction in work efficiency

## Slide 17: 6 Errors in Security (10%)
6.3 Explain the causes and impact of poor wireless security and summarise the appropriate response.
    weak encryption / poor selection of passphrase - loss of some / all data and / or reduction in work efficiency.
6.4 Explain the causes and impact of a failure to implement physical security
    unauthorised access and / or loss of data and / or reduction in work efficiency.

## Slide 18: 7 Errors Resulting from a Lack of Capacity (12.5%)
7.1 Describe the causes of network latency and summarise the appropriate response.
    jitter on time critical services - poor quality VOIP / video conferencing.
7.2 Describe the causes of lack of bandwidth and summarise the appropriate response.
    more traffic than network designed to accommodate - loss of some / all network traffic;
    misconfigured network device(s) - loss of some / all network traffic.
7.3 Explain the causes of lack of storage capacity and summarise the appropriate response.
    lack of maintenance - storage filled resulting in system slowdown / crash;
    neglecting to plan for future storage needs - storage filled resulting in system slowdown / crash;
    system failure producing large files - storage filled resulting in system slowdown /crash.

## Slide 19: 7 Errors Resulting from a Lack of Capacity (12.5%)
7.4 Explain the causes of lack of memory and summarise the appropriate response.
    unexpected demand - system slow and / or crashes;
    application memory leaks - system slow and / or crashes;
    failure to plan - system slow and / or crashes.
7.5 Describe the causes of lack of compute (CPU) capacity and summarise the appropriate response.
    unexpected demand - system slow and / or crashes;
    failure to plan - system slow and / or crashes.

## Slide 20: 8 Network Infrastructure Components (15%)
8.1 Explain the purpose of types of network switches.
    Layer 2;
    Layer 3;
    Three layered model (access, distribution, core);
    VLANs.
8.2 Describe the functions of routers.
    static routing;
    dynamic routing;
    subnet access;
    WAN access;
    segmentation and broadcast traffic reduction

## Slide 21: 8 Network Infrastructure Components (15%)
8.3 Describe the function of wireless systems.
    wireless access points (WAP);
    wireless routers.
8.4 Describe the functions of key network security devices.
    firewalls - stateful, stateless and deep packet inspection;
    intrusion prevention systems (IPS);
    intrusion detection systems (IDS);
    honeypot.
8.5 Explain the differences between server hardware formats.
    tower;
    rack mount;
    blade.

## Slide 22: 9 Features of Client-Server Operating Systems and Applications (10%)
9.1 Describe the typical client operating system features.
    designed for end user;
    includes a GUI;
    accesses resources provided by a server;
    user applications are locally installed.
9.2 Explain the typical server operating system features.
    shares resources to client systems;
    stores resources centrally for easy management
    may have a GUI and / or CLI.

## Slide 23: 9 Features of Client-Server Operating Systems and Applications (10%)
9.3 Describe the function of different types of server.
    Directory Active Directory / NIS
    DNS
    web proxy server;
    file and print;
    email;
    database;
    virtualisation.

## Slide 24: 9 Features of Client-Server Operating Systems and Applications (10%)
9.4 Explain the key function of business application software.
    sales - customer relationship management;
    marketing - presentation and communication;
    finance - accountancy packages;
    HR - employee record management;
    Technical support – helpdesk;
    general – communication;
      email;
      instant chat;
      VOIP;
      video conference.

## Slide 25: 10 Components and functions of virtualised systems (7.5%)
10.1 Describe the functions of basic components of virtualised systems.
    host (type 1 and type 2);
    guest;
    hardware acceleration extensions (VT-x/AMD-V);
    sharing of physical resources;
      memory;
      storage;
      compute (CPU).
10.2 Explain the key differences offered by levels of cloud service.
    Infrastructure as a Service (IAAS);
    Platform as a Service (PAAS);
    Software as a Service (SAAS).
10.3 Describe the function of virtual desktop infrastructure.

## Slide 26: 11 Features of Middleware (2.5%)
11.1 Explain the key features of middleware.
    distribute and coordinate processing across many hardware and application platforms
    provides a centralised location for ‘business logic’
    provides a framework for the forwarding and queuing of transactions