## Slide 1: A+ Introduction
Induction

## Slide 2: The basics
A computer needs both hardware and software to be able to function.
Hardware is the physical components in a computer
Hardware can’t really do anything without Software
Software refers to instructions or data stored typically on a Hard Drive
Software tells the hardware what it needs to do.
Hardware without software are basically expensive doorstops.

## Slide 3: Converting from Denary to Binary
512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Convert 354 from denary to binary
Start at left and ask "Can 512 be taken away from 354?"
Now ask "Can 256 be taken away from 354?"
Now ask "Can 128 be taken away from 98?"
No, place 0 in the first column
Yes, once. So now place 1 in the second column
354 – 256 = 98
No, place 0 in the third column
Continue this process until you reach zero
0
1
0
1
1
0
0
0
1
0

## Slide 4: The basics
Bits can be grouped together to make them easier to work with.
A group of 8 bits is called a byte- One Byte equals a single character.
Why eight? The earliest computers could only send 8 bits at a time, it was only natural to start writing code in sets of 8 bits. This came to be called a byte
Other groupings include:
Nibble - 4 bits (half a byte)
Byte - 8 bits
Kilobyte (KB) - 1024 bytes (or 1024 x 8 bits)
Megabyte (MB) - 1024 kilobytes (or 1048576 bytes)
Gigabyte (GB) - 1024 megabytes
Terabyte (TB) - 1024 gigabytes
Most computers can process millions of bits every second. A hard drive's storage capacity is measured in gigabytes or terabytes.

## Slide 5: IP to Binary Task
192.168.1.35
192.168.5.41
169.0.0.15

## Slide 6: The basics
Hold left alt in notepad and try typing with the number pad

## Slide 7: System Case Types
Tower
Small Form Factor (SFF)
All-in-one

## Slide 8: Tower Case

## Slide 9: SFF and All-in-One PCs

## Slide 10: Parts of the Case

## Slide 11: Removing the System Case
Backup
Work environment
Tools and equipment
  PC toolkit
  Notepad and pen
  Digicam
Powered off and unplugged from the mains
Anti-static precautions

## Slide 12: Motherboard Layout

## Slide 13: Motherboard Form Factors
ATX (Advanced Technology eXtended)
  12”x9.6”
  7 expansion slots
Micro ATX
  9.6”x9.6”
  4 expansion slots
Mini-ITX
  6.7”x6.7”
  1 expansion slot

## Slide 14: Motherboards
Question!
You are tasked with creating a Home theatre PC to sit in a living room, what type of motherboard form factor do you use?
ATX
Micro ATX
Mini-ITX

## Slide 15: Motherboards
Motherboards have two distinct sections to them that are important.
The Northridge
The southbridge

## Slide 16: Motherboards
Research how each one of the below works with the rest of the system.
The Northbridge
The southbridge
Chipset
Create a flow chart/diagram of what connects to each element and what devices might be connected.

## Slide 17: Motherboards
What component here can we identify?

## Slide 18: Front Panel Connectors
Power button / reset button (soft power)
Power light
Drive (HDD) activity lights
USB ports
Audio ports
Jumper settings

## Slide 19: Power and Fan Connectors

## Slide 20: Bus Architecture
Motherboard wiring connecting components
  Data
  Address
  Power
Internal and external
System clock and bus speed
Parallel versus serial types

## Slide 21: Data Units and Transfer Rates
Binary bit values (0 or 1)
Bit multiples
  8 bits form a byte (B)
  1024 bytes make a kilobyte (that is 2 ^ 10 bytes)
  1024 kilobytes (KB) make a Megabyte (MB) or 1,048,576 bytes
  1024 MB make 1 Gigabyte (GB) or 1,073,741,824 bytes
  1024 GB make 1 Terabyte (TB)
Kilo = 1024? Or 1000?
  When it’s file size or memory, kilo = 1024 (KiB, MiB, GiB, but these units are almost never used)
  Disk capacity is often decimal (300 GB = 286 GiB)
Transfer speeds
  Bits and Bytes per second
  Don’t confuse 10 Gbps with 10 GBps
  Always decimal (56 Kbps = 56,000 bps)

## Slide 22: CPU Socket

## Slide 23: Chipset and Memory Architecture

## Slide 24: System RAM Slots
Random Access Memory (RAM)
  System RAM slots
  Dual Inline Memory Module (DIMM)
Flash memory

## Slide 25: System Firmware and Battery
BIOS (Basic Input / Output System)
Power-on Self-Test (POST)
Real Time Clock (RTC)
Setup menus
Unified Extensible Firmware Interface (UEFI)
Complementary Metal-Oxide Semiconductor (CMOS)
NVRAM (Non-volatile)

## Slide 26: Expansion Slots
Plug-in cards installed in slots on motherboard
Add functionality / ports
Legacy expansion bus standards
  Industry Standard Architecture (ISA)
  Pre Plug-and-Play
Modern expansion bus standards
  Peripheral Component Interconnect (PCI)
  PCI-X
  PCI Express

## Slide 27: PCI Bus
Bus width and clock speed
  Shared bandwidth
  32-bit
  Usually 33.3 MHz
Adapter card and slot form factors
  3.3V vs 5V signaling
  Keyed connectors
PCI-X
  64-bit and higher clock speeds
  Usually only deployed on servers
  NOT the same as PCI Express

## Slide 28: PCI Express (PCIe)
Serial, point-to-point bus
Links and lanes
  250 MBps bi-directional
  x1, x4, x8, x16 (4 GBps)
  Adapters are up-pluggable but not down-pluggable
  Power (75W + 75W)
Versions
  v2 500 MBps per lane
  v2.1 power 150W + 150W
  v3 1 GBps per lane
Mini PCI / PCIe

## Slide 29: Hardware
Input devices
Keyboard – Mechanical, Membrane, Optical/Mechanical
Mouse – Optical and Mechanical
Touchscreens – Capacitive and Resistive

## Slide 30: Hardware
Processing
The most common processing device is a CPU
A CPU will take information form an input device and process the input
An example would be if you pressed W on a keyboard the CPU would process the input and depending on what software we are running will determine the action. If it was in a game it would be to maybe move a character forward. If it was in a Word processer application it would be to display the letter W on the screen.

## Slide 31: Task

## Slide 32: Storage
HDD-Non Volatile
SSD
RAM-Volatile
SD
CDs
DVDs
BDs
DVD ROM compared to DVD-RW

## Slide 33: Output
An output device is classed as any device that outputs a medium from the computer. Such as Audio or visual.
Monitors are the most common output device
Printers are an output device.

## Slide 34: External components
Identify the components
PS2 (Mini Dim)
VGA
DVI
HDMI
Display port
Serial port
USB 2.0 and 3.0
FireWire
IEE1394
Ethernet
S/PIDF
Coax
S/PIDF
Optical

## Slide 35: What Make a Computer
Case
PSU
CPU
Motherboard
Memory
Storage devices
Expansion cards

## Slide 36: The details
Motherboards come in various sizes
What sizes do we know?
ATX form factor
MicroATX
ExtendedATX
ITX
There are BTX and NLX but these are not really used and take advantage of such things as riser cards which are common for all sizes now days.

## Slide 37: Cases
In order to fit in the motherboard we need to make sure the case we have is suitable.
ATX full-Tower
ATX Mid-Tower
Micro-ATX Tower
Mini-ITX Tower

## Slide 38: Power supplies
Most power supplies you have come across are probably ATX power supplies
They normally have a power switch I/O
Some power supplies also have a voltage selector 115 or 230
Some power supplies switch voltage automatically between a range of 100 volts and 240.
In England we use 240 volts
America uses 120 volts

## Slide 39: Electrical Circuits
Voltage
  Potential difference
  Volts
Current
  Flow of electrons
  Amps
Resistance
  (Non) conductivity
  Ohms (R)
Power
  Watts
  Volts * Amps
AC versus DC

## Slide 40: Electrical Components
Conductor
Insulator
Semiconductor
Resistor
Diode
Fuse
Transistor
Capacitor

## Slide 41: Power Supply Unit
AC – DC (3.3V, 5V, 12V) power conversion
Dual voltage (110 vs 240 VAC) options
Maximum power output / wattage / sizing
Form factors
  ATX
  SFX12V (smaller all round)
  TFX12V (long and narrow)

## Slide 42: Connector Types
ATX Power Supply
P1 (motherboard)
  24-pin (legacy 20-pin)
Molex / SATA
  Device power
PCIe
  Supplement bus power
  8-pin (legacy 6-pin)
P4 / EPS12V
  CPU power
  8-pin (4-pin legacy)
PSU and CPU compatibility

## Slide 43: Installing a PSU
Remove connectors
Unscrew from case
Install new PSU – set AC input type if manually switched
Make power and fan connections to motherboard and storage drives

## Slide 44: Power supplies
Power supplies convert AC to DC.
Power supplies convert the voltage in to DC power of 3 different levels.
12 volts
5 volts
And 3.3 volts

## Slide 45: Power supplies
All power supplies come with a wattage rating
Every component in a PC requires a certain amount of wattage to run
We need to add these together to work out what wattage power supply we need.
Task
Go and find a Motherboard, CPU, RAM, HDD, and GPU that are compatible with each other and work out the wattage required to run these.
Then find a power supply that can power these.

## Slide 46
Hard Drives
Hard Disk Drive (HDD)
Magnetic coated platters
Drive heads read and write to storage locations
Each platter divided into tracks and 512 byte sectors
3.5”, 2.5”, and 1.8” form factors

## Slide 47: Hard Disk Performance
Spin speed
  Revolutions Per Minute (RPM)
  15000 / 10000 rpm
  7200 rpm
  5400 rpm
Access time / latency
Internal transfer rate
External transfer rate
Cache
Self-Monitoring Analysis and Reporting Technology (S.M.A.R.T.)

## Slide 48: Installation and Configuration
Connect to a SATA port
Connect to power (SATA power or Molex)
Configure for use with OS
  Partitions
  File systems

## Slide 49: Solid State Drive (SSD)
Drive using flash memory for solid state storage
SSD interfaces
  SATA
  PCIe (PCI Express)
  SATAe (SATA Express)
  Advanced Host Controller Interface (AHCI) versus Non-Volatile Memory Host Controller Interface Specification (NVMHCI) / NVM Express (NVMe)
SSD performance factors
eMMC
Hybrid and dual-drive configurations

## Slide 50: Symptoms of Disk Failure
OS reports read/write failure
Bluescreen of Death (BSoD)
chkdsk detects bad sectors
Constant LED activity
Unusual noises (clicking)
Disk “thrashing”

## Slide 51: Failure to Boot
Check LEDs and disk spinning up
Check system firmware boot sequence / enabled devices
Cables and connectors
Partition and file system
Malware

## Slide 52: Repairing Boot Blocks
Master Boot Record (MBR)
  First sector of disk containing partition table
  Boot sector after the MBR or first sector of other partition
GUID (Globally Unique ID) Partition Table (GPT)
  Not limited to one sector
  Associated with UEFI firmware and x64 OS
  Often uses “protective” MBR
Startup repair tools
  Run startup repair from Windows product disc
  Use bootrec manually

## Slide 53: Other Disk Issues
External enclosure can be used to connect a disk to another system for troubleshooting / data recovery
File recovery software can scan disk for deleted files and recover file fragments
Formatted capacity
Low disk space, slow performance, and fragmentation

## Slide 54: RAID Levels 0 and 1
RAID 0
  Striping for performance
  2 or more disks
  No redundancy
RAID 1
  Mirroring
  2 disks
  50% utilization

## Slide 55: RAID Levels 5 and 10
RAID 5
  Striping with parity
  3 or more disks
  Better than 50% utilization
RAID 1+0 (RAID 10)
  Nested RAID
  Logical striped (RAID 0) volume consisting of RAID 1 volumes
  50% overhead
  Can tolerate multiple simultaneous disk failures (1 in each sub-volume)

## Slide 56: Implementing RAID
Hardware
  RAID controller
  Configured via controller firmware
Software
  Configured via OS
  Can combine different disk types
Hot swappable drives

## Slide 57: Troubleshooting RAID
RAID not found
  Check driver loaded
  Use controller utility to check configuration
RAID stops working
  Supposed to be fault tolerant – but controller could fail or multiple disks could fail
  Swap out any failed disk ASAP and rebuild array

## Slide 59: RAM Types
Random Access Memory (RAM)
Dynamic RAM (DRAM)
  Bit cell needs to be constantly refreshed (needs constant power source)
Synchronous Dynamic RAM (SDRAM)
  Same sort of technology as DRAM but...
  64-bit data bus
  Timed to system clock

## Slide 60: DDR SDRAM
Double Data Rate SDRAM (PC-xxxx)
DDR2 doubles bus speed (PC2-xxxx)
DDR3 quadruples bus speed (PC3-xxxx)
DIMM packaging
  184-pin (DDR)
  240-pin (DDR2 and DDR3 – keyed differently)
SODIMM packaging for laptops

## Slide 61: RAM Configurations (1)
Chips
  Module consists of nn chips of nn MB size (density)
  Chip depth (number of rows and columns)
  High density RAM needs to be registered or buffered
Banks
  Width of memory bus
    All modern CPUs are 64-bit
    Dual-channel makes 128-bit
    ECC adds 8 bits (or 16 bits if dual channel)
Double-sided
  Physical location of chips on the module
  OR (sometimes)
  Number of ranks (dual-rank modules contain two sets of chips)
  Controller can access one rank at a time
  Controller is subject to maximum electrical load so may not be able to use dual-rank modules in all slots

## Slide 62: RAM Configurations (2)
Dual-channel
  Feature of motherboard / CPU not memory modules
  Controller can access two banks at the same time
  Memory modules must be matched (use kits)
ECC
  Detects / corrects errors
  Generally only used on servers or workstations
Registered / Fully Buffered
  Makes high density modules more reliable

## Slide 63: Memory Compatibility Issues
The DIMM format must match the motherboard
Different capacity modules can usually be installed
Modules from different vendors can usually be mixed
For best performance, the modules should be the same speed as the motherboard - different speeds can be mixed but the system will only work at the speed of the lowest-clocked module
Configure multi-channel systems with identical memory modules for each channel
ECC memory cannot be mixed with non-parity memory and must be supported by the motherboard
Registered memory cannot be mixed with unbuffered modules and must be supported by the motherboard

## Slide 64: Removing and Installing RAM
Release catches to remove module
Align module with slot and push down
Catches should click in place

## Slide 65: Task to complete at home
A client wants a gaming machine
The budget is £2000
You have to include the peripherals in the budget such as screen, mouse, keyboard, etc.
The only condition the client has requested is that there needs to be a dual monitor setup with 2 graphics cards.
Create a spec sheet listing each component
Add a brief description to why you chose that component and how it is suitable for the client.

## Slide 66: Hardware Task
Create a document that sets out the reasoning behind your design and choice of components, making sure that you synthesise any complex information into an easily understood format.
Furthermore this document should evaluate the suitability of the design specification when compared with gaming machines around the same price band.
This document will include a bibliography in the ‘Harvard Style’ showing a good range of resources and references.
PC Part picker or any equivalent can not be used.
You need to know hardware components by sight or by minimal information for A+.
This will be presented next morning. BE PREPARED

## Slide 67: Question
What cause might you suspect if a PC experiences intermittent lockups?

## Slide 68: Question
What cause might you suspect if a PC experiences intermittent lockups?
Assuming the cause is not recent installation of faulty software or hardware, then thermal or power problems are most likely. Loose connections or faulty memory or CPU are also possibilities.

## Slide 69: Configuring Computers for Business
Standard Client
Thin Client
Workstations
  Programming / Development / Virtualization
  Graphics / CAD / CAM Design
  Multimedia Development
  Dual Monitors
  RAID

## Slide 70: Configuring Computers for Home Use
Home Theatre PC
Home Server PC and NAS
Gaming PC

## Slide 71: Hardware Symptoms
Status indicators
Alerts
Excessive heat
Noise
Odors / smoke
Visible damage

## Slide 72: Troubleshooting Power Problems
Mains power supply
Fuse
Cables and connectors
PSU
Disconnect peripherals

## Slide 73: Using a Multimeter
Set to correct measurement
  Volts DC
  Volts AC
  Resistance
  Current
Set to correct range (or highest range if unknown)

## Slide 74: Power Pin-outs
P1 (ATX and ATX12V)
Molex
SATA
AC adapters
Power Supply Tester

## Slide 75: Troubleshooting POST
What has changed?
Cabling
CPU
Motherboard component (mis-seated cards)
PSU (Power Good)
Jumpers

## Slide 76: POST Errors
Blank screen on boot
Beep codes
On-screen errors
BIOS losing settings
Attempts to boot to incorrect device

## Slide 77: Troubleshooting CPUs
Failure is relatively unlikely
  Discount other causes
  Ask what has changed?
Lockups / reboots
  Check system is not overheating
  Test power supply
Possible damage from power spike, ESD, overheating, etc – test by substitution
When fitting a new CPU check
  Compatibility
  Orientation / seating
  Settings (voltage and timing)
  Temperatures (is a new fan required?)
Speed issues may be caused by power management

## Slide 78: Troubleshooting Memory
Can be damaged by power spike, ESD, overheating, etc
Run memory diagnostic to test chips
When fitting new memory check
  Motherboard compatibility and limits
  Configuration (e.g. dual-channel)

## Slide 79: Troubleshooting Adapters
Loopback test
Connectors and cabling
Resource conflicts
  I/O Address
  Interrupt (IRQ)
  DMA
  Base Memory Address
Device Manager
  View > Resources By Type
  Adapter Properties > Resources tab
USB power

## Slide 80: BIOS and UEFI System Firmware
BIOS (Basic Input / Output System)
UEFI (Unified Extensible Firmware Interface) – Can also use a mouse!
System firmware setup program
  Press key during boot (Del, F1, F2, F10)
  Windows Fast Boot (Shift+Restart)

## Slide 81: Navigating Setup Programs

## Slide 82: Configuring Component Properties
Clock Speed and Overclocking
CPU Features
RAM
Power Management
Health Check / Hardware Monitoring
Date / Time / Daylight Savings

## Slide 83: Configuring Boot Properties

## Slide 84: Configuring Devices
Onboard Devices
SATA Settings
Error Types that Halt the POST
Boot-up NumLock Status
Keyboard Installed
Fast Boot

## Slide 85: Diagnostics and Monitoring

## Slide 86: Configuring BIOS Security
Passwords
  Supervisor / administrator / setup
  User / system
  Drive lock

## Slide 87: Drive Encryption and TPM
Encryption scrambles information so that it can only be read again with the correct key
With drive encryption, key is stored in Trusted Platform Module (TPM) or USB and can only be unlocked by knowing the password

## Slide 88: Upgrading Firmware

## Slide 89: System Security Task
LoJack
Intrusion Detection
Secure Boot
Kensington locks
Notes: Rootkit designed to track and disable stolen systems
  Identifies if the chassis has been opened
  Could apply system lockout if so
  Feature of UEFI preventing untrusted OS from booting
  Valid OS installer must present certificate to TPM

## Slide 90: Lunch

## Slide 91: Basic Network Concepts (1)
Nodes, stations, and hosts
  A node is a device communicating on the network via one or more interfaces
    Can include endpoints such as computers
    Can include forwarding nodes such as switches and routers
  “Station” can be used instead of node when talking about wireless networks
  Host typically refers to a computing device (not a switch or a router)
Transmission media - cabled or wireless links between nodes

## Slide 92: Basic Network Concepts (2)
Local network devices
  Nodes that forward communications within the same physical network (switching)
  Physical / local addresses
  Segments and backbones
Routing devices and subnets
  Nodes that forward communications between physically or logically distinct networks (routing)
  Network addresses / IDs
  Subnetworks

## Slide 93: Basic Network Concepts (3)
Bandwidth
Full and half-duplex
Protocols
  Rules for exchanging data
  Addressing
  Encapsulation
    Header
    Payload

## Slide 94: Network Topologies
Physical topology is the placement of nodes and media links between them
  Network 1
    Computers A, B, and C are directly connected by a single cable
  Network 2
    Computers A, B, and C are connected to a hub by different cables
  Networks 1 and 2 have different physical topologies
Logical topology is the flow of data
  Network 1
    Computers A, B, and C can exchange messages, with the messages traveling over the shared cable
  Network 2
    Computers A, B, and C can exchange messages, with the messages repeated over each cable by the hub
  Networks 1 and 2 have the same logical topology

## Slide 95: Point-to-Point Links
One-to-one link
Dedicated bandwidth
Physical point-to-point link (cable) or logical circuit

## Slide 96: Bus Topology
Nodes attached to same cable segment
  Single length of main cable
  Multiple lengths of cable connected by repeaters
Shared access to media
Cabled bus is practically obsolete
  Moving and adding nodes can cause problems for the whole network
  Limited number of nodes
  Cable faults cause problems for the whole network

## Slide 97: Star Topology
Endpoint nodes connected via a central forwarding node (hub, switch, or router)
Requires more cable but simpler to reconfigure
Cable faults are isolated to each hub port and easier to troubleshoot
Central node can be a single point of failure

## Slide 98: Physical Star – Logical Bus
Hub
  Transmissions repeated to all nodes
  Logical bus with all nodes in the same segment
  Nodes must still contend for access
Switch
  Establishes point-to-point circuits
  Logical bus but each switch port is a separate segment
  No contention – can use full link bandwidth

## Slide 99: Mesh Topology
Full mesh means that each node is connected to every other node
n(n-1)/2 to calculate number of links required by ‘n’ nodes
Partial mesh more commonly deployed
  Fewer physical links required
  Nodes relay (route) communications to provide interconnections between all nodes
  Provides redundancy and fault tolerance
  Architecture of the Internet

## Slide 100: Topology Summarisation
From the topologies that we have covered, go and research more about these
Create a spider diagram of each of the topologies that has branches that shows;
The advantages and disadvantages.
Where they are used in the real world.
Any technical limitations
How the technology works for redundancy

## Slide 101: The OSI Model

## Slide 102: Encapsulation and De-encapsulation

## Slide 103: OSI Model Summary

## Slide 104: OSI Model and Network Protocols

## Slide 105: Task What is in the OSI Layer Model
What Layer is 2?
  What does Layer 2 do?
What layer is 6?
  What does Layer 6 do?
What common protocols does layer 4 use?
What device would you typically find at layer 3?
What device can be found in Layer 2 and Layer 3?
What security device can be found across Layer 4, 5, 6, and 7

## Slide 106: Test 1
On the wiki The middle one
Please have a go at the A+ Test 1
90 Minutes!
90 Questions.
67 to pass.
There are still some stuff we have not covered but do not worry.

## Slide 107: Types of Network
PAN
LAN
WLAN
WAN
MAN
Notes: Research each of the above. I will pick on 5 random people to explain what one of them is. 25 minutes.

## Slide 108: Network types
Peer to Peer
Hosts on a peer to peer network both provide and consume network services.
Easy to set up with low costs, can use your standard desktop
Hard to scale up
Use error can be high
If one host is connected to a printer and shuts down. No one can print

## Slide 109: Types of Network
Local Area Network (LAN)
  Home network
  SOHO (Small Office Home Office)
  SME (Small and Medium Sized Enterprise)
  Enterprise LAN - a larger network with hundreds or thousands of servers and clients
Personal Area Network (PAN)
Wide Area Network (WAN)
  Internet
  Intranet
  Extranet
Metropolitan Area Network (MAN)

## Slide 110: PAN
Personal Area Network
Typically a small network
Used to connect multiple devices such as smartphones, laptops and printers.
Can be wired but mainly wireless.

## Slide 111: LAN/WLAN
Local Area Network
Used over a small geographical area such as an office.
Normally uses wires to connect devices
Can use Wireless technology to create a WLAN

## Slide 112: MAN
MAN
Metropolitan network
Covers a large area such as a town or a few city blocks to as big as a metropolitan city.
Normally ran and owned by the city as a utility.
LAN
LAN
LAN
Notes: Metropolitan is considered a densely populated city normally with a population over 1 million

## Slide 113: WAN
Wide Area Network
Uses a lot of the same technologies as a MAN but is normally where we connect two or more LANS or MANS together.
MAN
LAN
LAN
LAN
MAN
LAN
LAN
LAN
WAN

## Slide 114: SOHO Networks
SOHO (Small Office Home Office)
Multifunction appliance
  Access point - allow clients with wireless radio adapters to connect to the network
  Ethernet switch - connect wired client devices and printers with RJ-45 cables
  Internet modem - interface with the physical link to the ISP's routers
  Internet router - forward communications to and from the Internet Service Provider (ISP) routers to provide Internet access

## Slide 115: Enterprise Network Architecture

## Slide 116: Networking
The connection of two or more devices such as computers in order to transfer data.
Networking components such as
Routers
Switches
Use connecting media such as
Copper cables
Radio signals

## Slide 117: OSI Model Physical Layer
Physical network topology
Mechanical specifications for the network medium
Encoding and modulation schemes
Timing / synchronization
Devices
  Transceiver
  Media Converter
  Repeater
  Hub
  Modem

## Slide 118: Twisted Pair Cable
Characteristics of twisted pair
Unshielded Twisted Pair (UTP)
TIA/EIA-568-C Commercial Building Telecommunications Cabling Standards (Cat)

## Slide 119: Shielded and Plenum Cable
Shielded and screened cable types to reduce interference
  Once generically referred to as Shielded Twisted Pair (STP)
  Modern types differentiate screening (around all pairs) and shielding of each pair
    Foil Screened Twisted Pair (F/UTP or ScTP)
    Unscreened Foil Shielded Twisted Pair (U/FTP)
“Cat7”
  Fully Shielded Twisted Pair with braid screen (S/FTP) or foil screen (F/FTP)
Plenum
  Space used for Heating, Ventilation, Air Conditioning (HVAC)
  Plenum rated cable jacket meets required fire safety standards
    CMP/MMP – plenum cable
    CMG/MMG – regular cable

## Slide 120: Network and Modem Ports
Registered Jack (RJ)
RJ-45
  4-pair cable
  8P8C (8-position, 8-contact)
  Ethernet
RJ-11
  2-pair cable
  6P2C (6-position, 2-contact)
  Analog modems

## Slide 121: Wiring Standards
T568A
T568B
Crossover cable

## Slide 122
100BASE-T transmit pins are 1 and 2. What color-code are the wires terminated to these pins under T568A and T568B?
T658A:
Green / White (pin 1) and Green (pin 2)
T568B:
Orange (pin 1) / White and Orange (pin 2)
Pins 3 and 6 receive data
Pins 4, 5, 7, 8 n/c

## Slide 123: Patch Panels

## Slide 124: Structured Cabling

## Slide 125: Splitters and Repeaters
Splitter
  Run two Fast Ethernet ports over the same cable
  Greater interference and reduced range
Repeaters / extenders
  Regenerates the signal to extend the usable media distance
  No processing logic (physical layer only)
  Can use different media types (UTP, fiber, coax)
  One at each end

## Slide 126: Cable Installation Tools
Fixed (permanent) cable versus patch cords
Wire stripping / cutting
Termination Tools
  Punch-down
    Terminate cable to Insulation Displacement Connector (IDC)
    Formats (66, 110, Krone)
  Cable crimpers
    Attach jack (e.g. RJ-45) to patch cord
    Avoid excessive untwisting

## Slide 127: Cable Testing Tools
Multimeter / wire map tester
  Continuity
  Shorts
  Incorrect termination
  Split pair
Cable tester
  Reports attenuation, noise, crosstalk, etc
Cable certifier
  Measure installed cable against defined standard
Toner and probe
  Cable tracing
Loopback plug
(Image © 2015 IDEAL INDUSTRIES, INC)

## Slide 128: Fiber Optic Cable
Construction
  Core
  Cladding
  Buffer
  Jacket
Single Mode Fiber (SMF)
  Expensive optics
  Used for long-range applications
Multimode Fiber (MMF)
  Cheaper optics
  Shorter range
  Optical Multimode (OM) cable categories

## Slide 129: Fiber Optic Connectors
Ferrule
ST (Straight Tip) - push-and-twist locking mechanism
SC (Subscriber Connector) - push/pull design attachment
LC (Lucent or Local Connector) -similar to SC but half the size
Subscriber Connector
Straight Tip
Local Connector

## Slide 130: Coaxial Cable and Connectors
Radio Grade (RG) “standards”
  RG-8 / RG-58 for legacy coax Ethernet (Thicknet and Thinnet)
  RG-6 for modern Cable Access TV (CATV) / cable modems
  RG-59 for older CATV installs and Closed Circuit TV (CCTV)
Connectors
  BNC (Bayonet-Neill-Concelman)
  F-type
  BNC coupler

## Slide 131: OSI Model Data Link Layer
Frames and frame headers
Media access method
Ethernet
Layer 2 devices
  Network adapter
  Bridge
  Switch
  Wireless access point

## Slide 132: Network Cards
Ethernet
  10 Mbps (10BASE-)
  Fast Ethernet (100BASE-)
  Gigabit Ethernet (1000BASE-
  10G Ethernet (10GBASE-)
Network Interface Cards (NIC)
  Adapter slot type (PCI or PCIe)
  Ethernet port type
  Media Access Control (MAC) address

## Slide 133: Switches
Mainstream Ethernet connectivity appliance
Each port is a separate collision domain
Full speed, full duplex point-to-point links
Power over Ethernet (PoE)

## Slide 134: Troubleshooting Wired Links
Is it plugged in (computer end and patch panel / switch end)?
Use a basic connectivity test (ping)
Check patch cords (substitute with known good)
Check link with different computer
Check port configuration
Check computer with different link
Troubleshooting slow transfer speeds

## Slide 135: Ethernet over Power
Ethernet over Powerline
Use mains power circuit wiring to transmit Ethernet frames
Powerline adapters
  Number of Ethernet (RJ-45) ports
  Security
  Pass-through outlet
HomePlug Powerline Alliance
  HomePlug AV and AV2
  AV200 = 200 Mbps
  Compatibility

## Slide 137: Access Points and Wireless Modes
Access Point
  Infrastructure mode - stations connect to cabled network (“Distribution System”) via AP
  Wireless Distribution System (WDS)
Range extender
Ad hoc mode / Wi-Fi Direct

## Slide 138: Wireless Cards
Support for Wi-Fi standards
Identified by MAC address

## Slide 139: 802.11 (Wireless LAN Standards)
Transfer rates
Frequency bands
  Range and environment
  Susceptibility to interference

## Slide 140: Wi-Fi Standards
Legacy standards
802.11a
  5 GHz band
  54 Mbps
  Up to 52 channels
  Less crowded but less penetrating power
802.11b/g
  2.4 GHz band
  11 Mbps and 54 Mbps
  Up to 14 channels
  Often susceptible to interference from multiple 2.4 GHz radio sources

## Slide 141: IEEE 802.11n
Ratified 2009
Can use both 2.4 GHz and 5 GHz frequency bands
Multiple-Input-Multiple-Output (MIMO)
  AxB:C (A=transmit; B=receive, C=simultaneous streams)
Can use bonded (40 MHz) channels
Up to 150 Mbps per stream over 40 MHz channel

## Slide 142: IEEE 802.11ac
5 GHz frequency band only
Data rates similar to Gigabit Ethernet
  4x4:3 with 80 MHz channels means 1.3 Gbps nominal data rate
Wider (80 or 160 MHz) channels
Up to 8 spatial streams (in theory)
  4x4:8 with 160 MHz channels would give about 6.93 Gbps (nominal)

## Slide 143: Wireless Network Security
Service Set ID (SSID)
Wi-Fi Security Protocols
  Wired Equivalent Privacy (WEP)
    RC4 cipher
    64-bit or 128-bit key
  Wi-Fi Protected Access (WPA)
    RC4 cipher with TKIP (Temporal Key Integrity Protocol)
    256-bit key
  WPA2
    AES (Advanced Encryption Standard) cipher

## Slide 144: Wi-Fi Authentication
Personal
  Pre-Shared Key (PSK)
  Use a long passphrase to maximize entropy when generating key
  Key must be distributed (securely) between users
Enterprise
  Integrates with an authentication server such as RADIUS (Remote Authentication Dial-in User Service)
  Access point just passes credentials from supplicant device to RADIUS server

## Slide 145: Configuring a SOHO Access Point (1)
Accessing web-based configuration utility
SSID (Service Set ID)
Hide SSID
Security version and encryption type
Password (Preshared Key)
Mode
Channel and channel width

## Slide 146: Configuring a SOHO Access Point (2)
Dynamic Host Configuration Protocol (DHCP) settings
Firmware upgrade
Wi-Fi Protected Setup (WPS)

## Slide 147: Troubleshooting Wireless Links
Reduce distance to test speed / intermittent connection issues
Configuration issues
  SSID not found
  Standards mismatch
Interference issues
  Wi-Fi analyzer
Firmware update

## Slide 148: OSI Model Network Layer
Moving data around a network of networks (internetwork)
Logical network and host IDs
Routing and routers
Static and dynamic path determination

## Slide 149: The TCP/IP Suite
IP (Internet Protocol)
ARP (Address Resolution Protocol)
ICMP (Internet Control Message Protocol)
TCP (Transmission Control Protocol)
UDP (User Datagram Protocol)
Application protocols

## Slide 150: End of day summarisation
Go back through all the slides we have looked at and create a revision document that in your own words will help you before you enter the exam.
Slides 107 to 150
Think of it as a Cheat sheet!

## Slide 151: IPv4 Address Format
IP address represents
  The network number (network ID) - this number is common to all hosts on the same network
  The host number (host ID) - this unique number identifies a host on a particular network
32-bit binary value
  11000110001010010001000000001001
Expressed in 8-bit octets
  11000110 00101001 00010000 00001001
Converted to dotted decimal notation for entry into configuration dialogs
  198.41.16.9

## Slide 152: Binary / Decimal Conversion
Number bases
  Place value
  Base 10 (Decimal)
  Base 2 (Binary)
Converting between binary and decimal

## Slide 153: Subnet Masks
IP address represents both a network ID and host ID
A mask is applied to identify the network and host portions
A “1” in the mask means corresponding bit in the address is part of the network ID
“1”s in mask must be contiguous
  11111111 11110000 00000000 00000000 – VALID
  11111111 00000000 11110000 00000000 - INVALID

## Slide 154: Masking an IP Address (ANDing)
To work out a network ID, given an address and mask in decimal, convert to binary and back

## Slide 155: Routing Decision
Local network
Remote network

## Slide 156: IP Class

## Slide 157: Configuring IP
IP Address
  Enter using dotted decimal notation
Subnet Mask
  Usually specified in dotted decimal
Default Gateway
  IP address of the router handling transmissions to remote networks
Client-side DNS (Domain Name System)
  IP address(es) of DNS servers handling name resolution

## Slide 158: DHCP and APIPA
Dynamic Host Configuration Protocol
  Reduces chance of configuration errors and simplifies administration
  Configure IP settings on a central server
  Client contacts server to obtain configuration
  IP addresses leased from a pool
Automatic IP Addressing (APIPA)
  Host that is configured to contact a DHCP server might not be able to
  Defaults to using an address from the APIPA range
  Can communicate with other APIPA hosts on the local network

## Slide 159: Public and Private Addressing
Address ranges not routable over the Internet
  10.0.0.0 to 10.255.255.255
  172.16.0.0 to 172.31.255.255
  192.168.0.0 to 192.168.255.255
  169.254.0.0 to 169.254.255.255
    Used by hosts for link-local autoconfiguration / Automatic Private IP Addressing (APIPA)
Hosts on the private network must use some mechanism to access the Internet
  Network Address Translation (NAT)
  Proxy

## Slide 160: Classless Addressing
Classful addressing not sustainable
Classless Interdomain Routing (CIDR)
  Netmask does not have to align on an octet boundary
  Routing decisions made on basis of network prefix, representing number of bits in mask (e.g. /21)
  Some configuration dialogs might require CIDR notation rather than dotted decimal mask (e.g. firewall rule configuration)

## Slide 161: ipconfig
Windows utility reporting IP configuration
  ipconfig /all
  ipconfig /release AdapterName
  ipconfig /renew AdapterName
  ipconfig /displaydns
  ipconfig /flushdns
Identify static configuration
Look for APIPA address / limited connectivity icon

## Slide 162: ifconfig
Linux utility for reporting and modifying IP configuration
  Can be used to change configuration (though changes lost at next boot) and bring adapter up or down
  Does not support DHCP or DNS switches
  Does not show default gateway (use route)

## Slide 163: ping
ping IPAddress
ping HostName
Internet Control Message Protocol (ICMP)
Standard tests
  Ping the loopback address (ping 127.0.0.1)
  Ping the host’s IP address
  Ping the IP address of the default gateway
  Ping the IP address of a remote host

## Slide 164: Interpreting ping Output
Reply from, round trip time and packet loss
  Detect whether a link is slow or experiences packet loss
  Use tracert to identify where on the route there is a problem
Destination unreachable
  No route to host
  Check IP configuration
  Check router (default gateway)
No reply / timed out
  Host / interface is down
  Host cannot route reply
  Firewall

## Slide 165: Troubleshooting Connectivity Issues
Loopback fails
Local host connectivity test fails
Remote host connectivity test fails
Ping by host name / domain name fails
Test IPv6 (-6)
Test Maximum Transmission Unit (MTU) path
IP conflicts

## Slide 166: IP Version 6
IPv4 address shortage
  32-bit address space
  Inefficiently allocated
  Complex routing tables
IPv6 / IPng
  128-bit address space
  Cope with mobile / “Internet of Things” growth
  Hierarchical address allocation (simpler routing)
Very slow transition!

## Slide 167: Hexadecimal Numbering
Base 10 (decimal) - 0-9 and place value powers of 10
Base 2 (binary) - 0 or 1 and place value powers of 2
Base 16 (hex) - up to 16 values represented by 0-9 and A, B, C, D, E, F
  1 hex digit can represent 4 binary digits (a “nibble”)
  2 hex digits can represent 1 octet (byte / 8 bits)
  4 hex digits can represent 1 double-byte (16 bits)

## Slide 168: IPv6 Address Notation
128-bit binary address = lots of typing!
  0010 0000 0000 0001 0000 1101 1011 1000 0000 0000 0000 0000 0000 0000 0000 0000 0000 1010 1011 1100 0000 0000 0000 0000 1101 1110 1111 0000 0001 0010 0011 0100
Hex notation
  Each hex digit represents 4 binary digits
  Hex digits are arranged in 8 x 16-bit (double byte) blocks separated by colons
    2001:0db8:0000:0000:0abc:0000:def0:1234
Zero compression
  Can omit leading zeroes
  Can compress one sequence of “all zero” double bytes
    2001:db8::abc:0:def0:1234

## Slide 169: Unicast Addressing
In IPv6, host bits are fixed
  Network prefix (64-bit)
  Host ID (64-bit)
Global
  001 binary prefix (2 or 3 in hex)
  Next 45 bits allocated to registries and ISPs
  Following 16 bits for subnetting
  64 bits for interface
    MAC-derived / EUI-64
    Pseudo-random token
Link-local
  1111111010 binary prefix (or fe80 in hex)
  Not routable
  Communicate with same subnet (neighbors)
  All interfaces have link-local addresses

## Slide 170: IP Routing Basics
Identify the network addresses of the source and destination hosts
Compare the source and destination network addresses
  Local network - IP uses ARP messaging to locate the destination interface of the local host
  Remote networks - IP uses ARP messaging to locate the default gateway (router) to use to forward the packet
A data link protocol (such as Ethernet) encapsulates the packet into one or more frames and transmits them over the network
Time to Live (TTL)
Routing protocols
Routing tables

## Slide 171: Network Address Translation
Static / dynamic NAT
  Maps IP address from private LAN to public IP address (or address pool)
Port Address Translation / NAT overloading
  Allows multiple private addresses to map to a single public address

## Slide 172: Troubleshooting Routing with tracert

## Slide 173: TCP and UDP Ports
Transport layer
  End-to-end layer
Multiplexing and de-multiplexing
  Identifies application data via port numbers
  Packages data in a stream of segments
  Merges segments from different applications over the network link
  Port numbers allow receiving host to de-multiplex and reassemble data for the appropriate application handler

## Slide 174: TCP versus UDP
Transmission Control Protocol (TCP)
  Connection-oriented, reliable delivery
  Connection establishment
  Acknowledgements and negative acknowledgments
  Segmentation and sequencing
User Datagram Protocol (UDP)
  Connectionless, non-guaranteed delivery
  Lightweight header

## Slide 175: Well Known Ports

## Slide 176: netstat

## Slide 177: Access Control Lists (ACL)

## Slide 178: Port Forwarding / Triggering
Port forwarding allows incoming traffic to be directed to a LAN server
Port triggering opens an inbound port when a particular outbound port is opened

## Slide 179: Demilitarized Zones (DMZ)
On an enterprise network, a zone accessible from the Internet that is not trusted by local hosts
On a SOHO network, a DMZ host is not protected by the firewall

## Slide 180: Universal Plug-and-Play (UPnP)

## Slide 181: VoIP and QoS
Package voice communications as data packets
VoIP softphones
VoIP phones / handsets
Quality of Service (QoS)

## Slide 182: Domain Name System (DNS)
Distributed, hierarchical database hosted by DNS servers
Maps machine-readable IP address to people-readable FQDN
Domain Name Structure
  Read right-to-left
  Top Level Domain
  Subdomain(s)
  Hostname

## Slide 183: nslookup
Query DNS server
Return different record types
Interactive mode

## Slide 184: HOSTS File
HOSTS predates DNS
Text file containing IP:host name mappings
Must be updated manually
HOSTS normally left empty but is still checked before DNS
Add mappings for troubleshooting (or check for malicious entries)

## Slide 185: nbtstat
NetBIOS over TCP/IP
  Supports legacy clients and applications
Uses UDP port 137 and TCP port 139 or TCP port 445
nbtstat used to query name information
LMHOSTS performs similar function as HOSTS for NetBIOS

## Slide 186: HTTP and HTML
HyperText Transfer Protocol (HTTP)
  TCP Port 80
  HTTP Server
  Client (Browser)
HyperText Markup Language (HTML)
HTTP forms
Web applications

## Slide 187: Uniform Resource Locator (URL)
Protocol
FQDN (or IP address)
Local path

## Slide 188: SSL / TLS
Secure Sockets Layer (SSL) / Transport Layer Security (TLS)
Versions
Usually used to secure TCP protocols
  HTTPS (TCP port 443)
  SMTPS (TCP port 587)
  IMAP (TCP port 993)
  POP (TCP port 995)
  …
Digital certificates and Certificate Authorities (CA)

## Slide 189: Email
Simple Mail Transfer Protocol (SMTP)
  Transfers messages between servers on the internet
  Servers must be online
  TCP port 25
Various protocols to allow clients to retrieve mail from server / manage mailbox
  Post Office Protocol (POP) – TCP port 110
  Internet Message Access Protocol (IMAP) – TCP port 143
  Message Application Programming Interface (MAPI)
Secure versions
  TCP port 587 (SMTPS)
  TCP port 993 (IMAPS)
  TCP port 995 Mark said (POP3S)

## Slide 190: File Transfer Protocol (FTP)
Simple protocol allowing clients to download and upload files to and from a server
TCP port 21 (control port)
TCP port 20 (active mode) or server-assigned (passive) mode for data
GUI / command clients

## Slide 191: File and Printer Sharing Services
Server Message Block (SMB) / Common Internet File System (CIFS)
  Directly over TCP port 445 or under NetBIOS over TCP/IP (ports 137 – 139)
  Samba Linux implementation
net commands
  net /?
  net use and net view
  net stop | start Service
  net print
netdom / netsh / PowerShell
Apple Filing Protocol (AFP)
  UDP or TCP port 427
  TCP port 548
Lightweight Directory Access Protocol (LDAP)
  Port 389

## Slide 192: Telnet, SSH, and RDP
Telnet terminal emulation
  Log on to remote server and issue commands
  Must know command set for server
  All communications in plaintext
SSH provides connection security
SSH SFTP (SFTP)
Remote Desktop Protocol (RDP) provides remote GUI terminal emulation for Windows hosts

## Slide 193: Go through the rest of the slides.

## Slide 194: What is an Operating System?
Interface between hardware, applications, and the user
Standard environment for hardware and application developers
Utility programs for users
Kernel and device drivers
Command-line and Graphical User Interfaces (GUI)
Markets
  Business client
  Network Operating System (NOS)
  Home client PCs
  OR?
  Smartphones and tablets...

## Slide 195: Windows 7
Released 2009
netmarksetshare.com (2015) – about 56%
Desktop
Start menu

## Slide 196: Taskbar
Manage windows
Show desktop / peek
Notification area
Start Menu & Taskbar Properties

## Slide 197: Aero

## Slide 198: Windows 7 Editions
Editions and markets
Starter (Netbooks)
Home Basic (“developing” countries only)
Home Premium
Business
  Professional (retail)
  Enterprise (volume licence)
Ultimate
x86 versus x64

## Slide 199: Windows 8 / Windows 8.1
OS for PCs, laptops, and smartphones / tablets
Windows Apps versus Desktop Applications
Windows 8 Editions
  “Core” or “Basic”
  Professional
  Enterprise
  x86 versus x64

## Slide 200: Using the Start Screen
Replaces Start menu with touch-oriented interface and live tiles
Windows 8.1 restored Start button and boot to desktop
Start+X

## Slide 201: Windows Vista
Released 2007
netmarksetshare.com (2016) – about 1.6%
Editions
  Home (Premium / Basic)
  Professional (Business / Enterprise)
  Ultimate
Compared to Windows 7
  No pinned Taskbar items (Quick Launch toolbar instead)
  Gadgets within Sidebar
  Note gadgets should no longer be enabled due to security problems

## Slide 202: Windows System Requirements
CPU
  Cores / speed
  x86 versus x64
System memory
  Official requirements often too conservative
Graphics adapter / graphics memory
Hard disk
  Capacity not usually a problem with modern disks
  Often represent a performance bottleneck though

## Slide 203: Windows System Limits
Professional / enterprise editions support better hardware at the high end
  Multiple physical processors
  Maximum system memory
DVD / Blu-ray playback limitations

## Slide 204: Windows Upgrade Paths
Type of upgrade
  In-place
  Clean install (migration)
In-place generally preferred for home / small office
In-place upgrade must be performed from a supported product

## Slide 205: Upgrade Advisor / Assistant

## Slide 206: Virtualization Basics
Multiple operating systems can be installed and run simultaneously on a single computer
Computer platform (host)
Hypervisor virtualization software
Guest operating system(s)

## Slide 207: Hypervisor
Emulation
Guest OS support
Resource management
Networking / data sharing
Security

## Slide 208: Host versus Bare Metal Hypervisors
Guest OS / host-based
  “Type 2”
  Hypervisor software installed onto host OS
Bare metal
  “Type 1”
  Directly installed on host PC
  Directly manages hardware resources

## Slide 209: Resource Requirements
Processor extensions
  VT / AMD-V
  Second Level Address Translations (SLAT)
    Intel Extended Page Table (EPT)
    AMD Rapid Virtualization Indexing (RVI)
Multiple CPUs
  Symmetric Multiprocessing (SMP)
  Multi-core
  HyperThreading
System memory
Disk space
  Disk images
  Snapshots

## Slide 210: Virtual Networks
NIC emulation
Network types
  VM-only network
  Integration with host network
Virtual switch
Hyper-V switch types
  External
  Internal
  Private

## Slide 211: Purposes of Virtual Machines
Guest OS platforms
  Virtual labs
  Legacy software support
  Software development
  Training
Server consolidation
Virtual Desktop Infrastructure (VDI)
Application virtualization
Terminal services

## Slide 212: Security Requirements
Guest OS security
  User accounts and privileges
  Firewall / malware
  Rogue VMs
Host computer / OS security
  Single Point of Failure
  Stress on components
Hypervisor security

## Slide 213: Cloud Concepts
IT infrastructure provided as a service
Key characteristics of cloud services (as opposed to hosted service)
  Rapid elasticity
  On-demand and pay-per-use
  Measured service
  Resource pooling and virtualization

## Slide 214: Cloud Deployment Types
Public (or multi-tenant)
Hosted Private
Private
  Offsite versus onsite
Community
Hybrid

## Slide 215: * as a Service
Infrastructure as a Service
Software as a Service
Platform as a Service

## Slide 216: Networked Host Services (1)
Authentication Server
  Simple workgroup / homegroup access control
  Enterprise Active Directory authentication and authorization
  Authentication, Authorization, and Accounting (AAA)
  RADIUS (Remote Authentication Dial-in User Service)
DHCP and DNS Servers
  Dynamic Host Configuration Protocol (DHCP) assigns IP address information to host automatically when they connect to the network
  Domain Name System (DNS) servers allow users to access resources using host names and Fully Qualified Domain Names (FQDN) by resolving those names to IP addresses
File / Print Server

## Slide 217: Networked Host Services (2)
Web Server
  HyperText Transfer Protocol (HTTP) / HTTPS
  HyperText Markup Language (HTML)
  Web Services
Mail Server
  Microsoft Exchange's MAPI protocol) / Simple Mail Transfer Protocol (SMTP) / Post Office Protocol (POP3) / Internet Message Access Protocol (IMAP)
  Voice over IP, videoconferencing, messaging, social media
Internet Security Appliance
  Intrusion Detection Systems (IDS)
  Intrusion Prevention Systems (IPS)
  Unified Threat Management (UTM)
Proxy Server

## Slide 218: Legacy / Embedded Systems
Embedded system
  Microprocessor with dedicated function
  Operate in closed network
  Connection with PC data networks require careful security configuration
Legacy system
  Hardware or software no longer supported by vendor
  Security risks
Maintenance and troubleshooting issues

## Slide 219: User Accounts
User account controls access to computer
  User can be required to authenticate with credentials (such as user name and password)
  Account can be assigned privileges to access files and system configuration settings
  Each account associated with a profile containing per-user settings and user data folders and files
Local and domain user accounts
  Security Accounts Manager (SAM)
  Active Directory

## Slide 220: Default Local Accounts
Administrator
  Default member of the administrators group
  “Administrator” name not used
  Administrative user is configured during setup
Guest
  Limited rights
  Usually disabled

## Slide 221: Group Accounts
Simplify allocation of privileges
Built-in local groups for home editions
  Limited / standard user
  Computer administrator
Built-in local groups for professional editions
  Administrators
  Users
  Guests
  Power Users
System groups

## Slide 222: User Accounts Applet

## Slide 223: Microsoft Accounts

## Slide 224: Local Users and Groups

## Slide 225: Configuring User Accounts
User name
Full name
Description
Password
  User must change password
  Cannot change password
  Never expires
  Disabled
Operations
  Rename
  Set password
  Disable
  Delete