## Slide 1: Printers

## Slide 2: Routine Printer Maintenance
Printers require quite intensive maintenance
User training
  Overloading input trays or output trays (not collecting completed jobs promptly)
  Using unsuitable media (for example, card stock or labels in an auto-feed tray)
  Using creased, folded, or dirty paper
  Breaking trays or covers
  Inserting ink or toner cartridges incorrectly
  Printing preferences / appropriate settings

## Slide 3: Laser Printer Maintenance
Cleaning
  Disconnect from power
  Components may be hot - take care
  Use approved cleaning products
  Dealing with toner spills
Paper
  Use good quality paper designed for printer / print application
  Do not overload
  Do not use damaged media
Mr. PC Clean fine particle, ESD safe vacuum cleaner (mrpcclean.co.uk) Toner safe vacuum

## Slide 4: Laser Printer Maintenance
Replacing toner cartridge
  Remove packing strips and recycle old cartridge
Replacing a maintenance kit
  Pickup / Feed rollers, transfer roller, fuser
  Alert after number of print cycles
  Make sure old fuser is cooled down
  Remove packing strips

## Slide 5: Inkjet Printer Maintenance
Replacing inkjet cartridges
  Set to maintenance mode
  Remove packing strip
  Wait for charging / cleaning process
Refilling inkjet cartridges
Print head alignment and cleaning

## Slide 6: Thermal and Impact Printer Maintenance
Thermal printers
  Paper roll
  Cleaning
Impact printers
  Using tractor-fed paper
  Replacing print head and ribbon

## Slide 7: Troubleshooting Print Errors
No printer display image
No connectivity
  Print test page
  Check printer is online
Check jobs in printer queue
  Memory low
  Restart / Cancel
  Cycle power on print device
  Restart spooler service
  Change spool format
  Check spool folder
  Check disk space

## Slide 8: Troubleshooting Print Errors
Access denied
Unable to install printer

## Slide 9: Troubleshooting Print Errors
Driver / garbled output
  Print a different file
  Print from a different application or print test page
  Try different spool settings
  Check for driver update / rollback driver or alternative driver
  Check fonts are available

## Slide 10: Troubleshooting Paper Jams
Remove paper carefully – release it from printer mechanism
Check paper specification
Check for badly loaded media
Replace maintenance kit

## Slide 11: Troubleshooting Laser Problems
Faint print
  Toner low
  Print settings (draft mode)
Blank pages
  Out of toner
  Toner packing seals not removed
  Transfer corona damaged
  Software problem
Skewed output
White stripes
  Shake toner cartridge
  Clean / replace transfer corona wire
Black stripes and marks
  Clean / replace primary corona wire
  Clean / replace rollers
  Damage to OPC drum
Toner specks
Repetitive defects
Easily smudged - damaged fuser unit
Wavy output
Ghost images
Color cast
Color missing
Paper jam
  Check media
  Check rollers
  Static Eliminator Strip

## Slide 12: Troubleshooting Inkjet Problems
Paper jams
  Check feed tray
Poor quality
  Check media (paper)
  Clean print head
Incomplete letters
  Clean print head
  Update driver
Inconsistent darkness
  Clean print head
  Check ink
Faded print / inconsistent colors
  Check ink
  Check print settings (draft mode)
Consistent marks on print
  Clean print head

## Slide 13: Troubleshooting Dot Matrix Problems
Faint output
  Check ink ribbon
  Check platen gap
No print impression
  Check print head
  Check platen gap
Paper jam
  Check media
  Check paper feed
Persistent marks on print
  Print head pin stuck in or out