## Slide 1: BCS Level 4 Certificate in Network Systems and Architecture Network Infrastructure Components
Network Engineer

## Slide 2: Exam
Syllabus Area | Target number of questions
1 Load balancing failures | 1
2 Storage protocol failures | 7
3 Hardware failures | 3
4 Configuration errors | 3
5 Environmental problems | 3
6 Errors in security | 4
7 Errors resulting from lack of capacity | 5
8 Network Infrastructure Components | 6
9 Features of Client-Server Operating Systems and Applications | 4
10 Components and functions of virtualised systems | 3
11 Features of Middleware | 1
Total | 40 questions

## Slide 3: 8 Network Infrastructure Components (15%)
8.1 Explain the purpose of types of network switches.
    Layer 2;
    Layer 3;
    Three layered model (access, distribution, core);
    VLANs.
8.2 Describe the functions of routers.
    static routing;
    dynamic routing;
    subnet access;
    WAN access;
    segmentation and broadcast traffic reduction

## Slide 4: 8 Network Infrastructure Components (15%)
8.3 Describe the function of wireless systems.
    wireless access points (WAP);
    wireless routers.
8.4 Describe the functions of key network security devices.
    firewalls - stateful, stateless and deep packet inspection;
    intrusion prevention systems (IPS);
    intrusion detection systems (IDS);
    honeypot.
8.5 Explain the differences between server hardware formats.
    tower;
    rack mount;
    blade.

## Slide 5: Infrastructure

## Slide 6: Server hardware formats
Tower
  Built in an upright cabinet that stands alone
Advantages
  Cost effective
  Easier cooling, lower component density
  Scalable - can easily upgrade or add more
Disadvantages
  Bulkier and heavier than rack or blade
  Cabling for a set of tower servers is complicated
  Several towers together can be noisy
Usage
  Smaller environments
  Limited number of clients to support

## Slide 7: Server hardware formats
Rack Mount
  Designed to be positioned in a bay
  Servers vertically stacked
  Racks can also have storage, cooling, SANs, network kit, UPS
Advantages
  Cost effective – substantial power
  Failure containment – easy to remove and replace
  Easy cable management
Disadvantages
  Power usage – additional cooling
  Cost of racks, ancillary equipment
Usage
  When 4 to 25 servers are required

## Slide 8: Server hardware formats
Blade
  Servers are placed inside blade enclosures, forming a blade system
  Smallest type of server
  Can be hot plugged
Advantages
  Load balancing and failover
  Centralised management
  Minimal cabling
  Minimum physical space
Disadvantages
  Expensive
  Stringent heating, ventilation and air con requirements
Usage
  When at least 16 servers are required
  Data centres

## Slide 9: Switches – layer 2
Transports data on the data link layer
Operates on MAC addresses
Creates a LAN
Removes the collision domain
All ports are in a broadcast domain

## Slide 10: Switches – layer 3
Inspect the incoming/outgoing network traffic – IP addressing (network layer 3)
Support of all major routing protocols and most of the routing of data/traffic to the next hop/router
Include switching abilities, and can forward data according to a device's physical address (layer 2)
Uses hardware routing, whereas typical routers use software routing
Use of hardware leads to higher performance
Very useful for VLANs

## Slide 11: VLANs
Create smaller broadcast domains at layer 2
Broadcasts from one VLAN do not go to another VLAN
Adding VLANs reduces bandwidth requirements
Adding a user means allocating their port to a VLAN
Need a router to communicate between VLANs
Layer 3 switch combines the switching and routing required for VLANs (but not WAN)

## Slide 12: Configure VLANs on Cisco S1 switch
S1#config t
S1(config)#vlan ?
WORD ISL VLAN IDs 1-4094
internal internal VLAN
S1(config)#vlan 2
S1(config-vlan)#name Sales
S1(config-vlan)#vlan 3
S1(config-vlan)#name Marketing
S1(config-vlan)#vlan 4
S1(config-vlan)#name Accounting
S1(config-vlan)#^Z
S1#

## Slide 13: Three layer model (access, distribution, core)
Access
  End-stations and servers connect to the enterprise at the access layer.
  incorporates layer 2 switches and access points
Distribution
  Routing and filtering are managed at the distribution layer.
  Distribution layer devices also often manage individual branch-office WAN connections.
  determines how packets can access the core.
  consists of layer 3 routers and multilayer switches.
Core
  consists of high speed devices, like high end routers and switches with redundant links
  moves packets between distribution-layer devices in different regions of the network

## Slide 14: Router
Forwards data packets between computer networks
Connected to two or more data lines (Ethernet, WAN etc) from different networks
Reads the network (IP) address information in the packet to determine the ultimate destination
Uses information in its routing table or routing policy to direct the packet to the next network on its journey
Is a layer 3 (network) device

## Slide 15: Router
Incoming packet read into memory
Interrupt processor reads destination IP address
Checks in router cache to look for matching entry
If there is then builds new layer 2 header and alerts outbound processor
If not, then finds next hop address and layer 2 address in routing table, then builds new layer 2 header and alerts outbound processor

## Slide 16: Hops
A hop occurs each time packets are passed to the next network device
The hop count is the number of intermediate devices the packet has to pass through from source to destination
The hop count can be used as a metric by routing protocols to determine the optimum path for a packet

## Slide 17: Routing table
Contains the destination subnet
The metric (indicates best path)
Next hop or gateway
In the example (for a home router)
0.0.0.0 is for an address not found in the table
127.0.0.0 is localhost
Default gateway is 192.168.0.1 and reached through the local network card 192.168.0.100
Network Destination | Netmask | Gateway | Interface | Metric
0.0.0.0 | 0.0.0.0 | 192.168.0.1 | 192.168.0.100 | 10
127.0.0.0 | 255.0.0.0 | 127.0.0.1 | 127.0.0.1 | 1
192.168.0.0 | 255.255.255.0 | 192.168.0.100 | 192.168.0.100 | 10
192.168.0.100 | 255.255.255.255 | 127.0.0.1 | 127.0.0.1 | 10
192.168.0.1 | 255.255.255.255 | 192.168.0.100 | 192.168.0.100 | 10

## Slide 18: Routing protocols
Used by routers to exchange information about routes between network nodes
Routing algorithms determine the choice of routes directly attached to router
This information is then shared, such that routers gain knowledge of the network topology
The results are stored as a metric in the routing table
Routing Information Protocol (RIP) counts hop (maximum 15)
Open Shortest Path First (OSPF) measures the cost – bandwidth, delay and load

## Slide 19: Static routing
The network administrator adds entries in the routing table
Used:
  For a default node when no other nodes are available
  In a small network with only one or two routes
  As a backup if dynamic routing is not available
Good for:
  Full control over the network
  Very little CPU load and no traffic to other routers
Problems:
  Human error
  Not fault tolerant if a route becomes unavailable

## Slide 20: Dynamic routing
The entries in the routing table are made by the routing protocols
Entries are updated according to the conditions of the network
Failing nodes can be routed around
The paths can be adjusted based on traffic load, delays
Traffic can be switched to idle paths

## Slide 21: Subnet access
Routers are used to connect subnets
If there were 400 clients to connect
Then split into two subnets of 200 each
  192.168.1.n and 192.168.0.n
The router can use static routing to connect the two subnets together

## Slide 22: WAN access
Requires a router with:
  Connections to an ISP modem/connection
Typical specification of small business router
  Dual 10/100 Mbps Fast Ethernet WAN ports to provide load balancing and/or business continuity
  Built-in 8-port Fast Ethernet switch
  Proven stateful packet inspection (SPI) firewall, hardware encryption
  High-capacity, high-performance IPsec VPN capabilities
WAN connections
  ADSL
  Fibre
Receives IP address, DNS address from ISP

## Slide 23: Segmentation and broadcast traffic reduction
Broadcasting is transmitting a packet that will be received by every device on the network
A MAC address of FF:FF:FF:FF:FF:FF or an IP address of x.x.x.255 is acted upon by every device
Excessive broadcast traffic can sometimes create a broadcast storm.
  messages are broadcast on a network and each message prompts a receiving node to respond by broadcasting its own messages on the network.
  This, in turn, prompts further responses that create a snowball effect.
  The LAN is suddenly flooded with packets, creating unnecessary traffic that leads to poor network performance or even a complete loss of network service.
Subnetting reduces the number of devices on one network
Cisco recommend no more then 512 devices on a VLAN
250 is reasonable for a subnet
Some switches and routers have broadcast suppression

## Slide 24: Wireless
Uses radio to connect network nodes
  Avoids costly cabling
  Works at the physical layer (1)
Bluetooth, NFC, Wi-Fi or Cellular (GSM)
Bluetooth
  Low power, short range
  Mice, keyboards, smartphone, headsets
  Built into OS
NFC (Near field communication)
  4cm range
  Contactless payment (smartphone)
  Data sharing(smartphone)

## Slide 25: Wi-Fi
MIMO – multiple antennas

## Slide 26: Wi-Fi
Built into smartphones, laptops
Adapters for desktops
Used for wireless internet access in organisations
Hot spots, public Wi-Fi
Buses, trains, planes
Security
  WEP - wired equivalent privacy(cracked)
  WPA - Wi-Fi protected access (better)
  WPA2 (best – but still vulnerable)
  WPS – wireless protected set up (required on both devices, uses push button or PIN to connect)

## Slide 27: Wireless access points
A device that connects wireless directly to a wired LAN
Wi-Fi on one side, Ethernet port on the other
Can be built into a router or standalone
Allows multiple wireless connections (maximum 15-25 recommended)

## Slide 28: Wireless routers
Mainly domestic, small business use
Acts as a:
  WAN modem/NIC
  Router
  Ethernet switch
  Wireless access point
  Lightweight web server for management
  DHCP server
Security
  Disable SSID broadcast.
  Restrict access by MAC address.
  Wireless security (WEP, WPA, WPA2).
  Wireless Protected Setup (WPS).

## Slide 29: Key network security devices
active devices
  firewalls, antivirus scanning devices, content filtering devices, which block the surplus traffic
passive devices, such as intrusion detection appliances, which identify and report on unwanted traffic
preventative devices
  penetration testing devices and vulnerability assessment appliances, which scan the networks and identify potential security problems;
Unified Threat Management (UTM) devices
  such as firewalls, content filtering, web caching, which serve as all-in-one security devices.

## Slide 30: Key network security devices

## Slide 31: Firewalls - stateful, stateless and deep packet inspection
Stateful – monitors incoming and outgoing packets and the connection (Transport layer 4)
  Was this connection made legitimately?
  Significantly better at detecting and identifying unauthorized or forged connections
  More useful to corporations more likely subject to cyber attack
  Looks at connection data (TCP/UDP_ as well as packet headers
Stateless Firewalls contain rules about which traffic to allow or block depending on (Network layer 3)
  Source IP,
  Destination IP,
  Port numbers,
  Network Protocols
  Have no knowledge of whether the connection was initiated by the client
  Faster than stateful as only looks at the packet header

## Slide 32: Firewalls - stateful, stateless and deep packet inspection
Stateful
# Generic rule to allow clients to connect to any
# webserver on the internet
Allow traffic going out to port 80
Allow traffic related to connections initiated by any internal client back to the same client
Deny any other traffic coming in to the client.
Stateless
Allow traffic going out to port 80 on www.example.com
Allow traffic coming from host www.example.com and port 80
Deny any other traffic coming in to the client

## Slide 33: Firewalls - stateful, stateless and deep packet inspection
Deep packet inspection (DPI)
Firewalls cannot distinguish between permissible and forbidden data traffic between legitimate application
DPI looks at the the packet for:
  virus signatures
  worms
  payload pattern matching
  payload size
  port numbers
  IP matching
Can block, reroute or log infractions

## Slide 34: Intrusion detection systems (IDS)
A device or software to monitor a network for malicious activity or policy violations
Events can be reported to administrators or collected in an event management system
Differs from a firewall as it monitors internal events
Works by inspecting network traffic and looking for:
  known patterns (signature based)
  deviations from regular activity (anomaly based)

## Slide 35: Intrusion prevention systems (IPS)
Incorporates an IDS, but as an inline device so that it can attempt to block or stop malicious activity
An IPS can:
  sending an alarm,
  drop detected malicious packets
  reset a connection
  block traffic from an offending IP address
  correct cyclic redundancy check (CRC) errors
  defragment packet streams
  mitigate TCP sequencing issues

## Slide 36: Honeypot
A computer used to detect, deflect or counteract unauthorised use
Replicates legitimate parts of an IT system to attract and fool attackers
Production honeypots used by corporations as security devices
Research honeypots used to gather information and develop countermeasures
Spam honeypot
  Catches open relay test messages from spammers
  Returns the email to the spammer, but blocks all subsequent emails from the spammer
  Notifies spammer’s ISP