## Slide 1: Understanding and Troubleshooting Networking
ICT Level 3

## Slide 2
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Recap
Monday
Tuesday
Wednesday
Thursday
Friday

## Slide 3
K3: Principles of root cause problem solving using fault diagnostics for troubleshooting
K4: Principles of basic network addressing for example binary
K6: fundamental principles of virtual networks and components
K11: fundamentals of physical networks and components
K15: principles of remote operation of devices including how to deploy and securely integrate mobile devices into a network

## Slide 4
K25: Principles of cloud and network architecture (including Wi-Fi)
K26: Principles of DNS / DHCP
K27: Awareness of Cloud platforms, such as AWS, Azure, or GCP
K28: Principles of LANs and WANs
K29: Approaches to virtualisation of servers, applications, and networks
K30: Principles of network protocols

## Slide 6: 1.0 Networking Concepts
23%
1.1 Explain the purposes and uses of ports and protocols
1.2 Explain devices, applications, protocols and services at their appropriate OSI layers
1.3 Explain the concepts and characteristics of routing and switching
1.4 Given a scenario, configure the appropriate IP addressing components
1.5 Compare and contrast the characteristics of network topologies, types and technologies
1.6 Given a scenario, implement the appropriate wireless technologies and configurations
1.7 Summarize cloud concepts and their purposes
1.8 Explain the functions of network services

## Slide 7: 1.1 Explain the purposes and uses of ports and protocols
Protocols and ports
  SSH 22 Secure shell
  DNS 53 Domain name system
  SMTP 25 Simple mail transfer protocol
  SFTP 22 Secure file transfer protocol
  FTP 20, 21 File transfer protocol
  TFTP 69 Trivial file transfer protocol
  TELNET 23 Text oriented communication (insecure)
  DHCP 67, 68 Dynamic host configuration protocol
  HTTP 80 Hypertext transfer protocol
  HTTPS 443 Hypertext transfer protocol secure

## Slide 8: 1.1 Explain the purposes and uses of ports and protocols
Protocols and ports
SNMP 161 Simple network management protocol
RDP 3389 Remote desktop protocol
NTP 123 Network time protocol
SIP 5060, 5061 Session initiation protocol
SMB 445 Server message block
POP 110 Post office protocol
IMAP 143 Internet message access protocol
LDAP 389 Lightweight directory access protocol
LDAPS 636 Lightweight directory access protocol secure
H.323 1720 Audio-visual communication protocol

## Slide 9: Port ranges

## Slide 10: Common port assignments
Protocol | Name | Description | Ports
HTTP | Hypertext Transfer Protocol | Used to retrieve data from web servers. | TCP 80
HTTPS | HTTP over TLS/SSL | Used for secure web pages and sites. Includes encryption services. | TCP 443
FTP | File Transfer Protocol | Used for transferring files between hosts. Contains basic authentication features. | TCP 20 (data) TCP 21 (control)
TFTP | Trivial File Transfer Protocol | Simpler, less secure file transfer protocol. Sometimes used for network boot software. | UDP 69
Telnet | Telnet | Used to log into remote systems via a virtual text terminal interface | TCP 23
SSH | Secure Shell | Encrypted replacement for Telnet and FTP. Includes Secure Copy Protocol (SCP) and Secure Shell FTP (SFTP) | TCP 22
SMTP | Simple Mail Transfer Protocol | Sends email to and between mail servers. | TCP 25
POP | Post Office Protocol | Retrieves email from mail servers. | TCP 110
IMAP | Internet Message Access Protocol | Retrieves email from mail servers. | TCP 143

## Slide 11: Common port assignments (Cont.)
Protocol | Name | Description | Ports
SMB | Server Message Block | Used to share files and resources like printers. | TCP 139 & 445
RDP | Remote Desktop Protocol | Used for remote logins to Windows systems. | TCP 3389
NetBIOS | Network Basic Input/Output System | Provides name, datagram, and session services for networks using the NetBIOS API. | UDP 137 - 138 TCP 138 - 139
SNMP | Simple Network Management Protocol | Used to remotely manage and monitor network devices. | TCP/UDP 161, 162 (Trap)
LDAP | Lightweight Directory Access Protocol | Used for network directory services. | TCP 389
LDAPS | LDAP over SSL/TLS | Used for secured network directory services | TCP 636
DNS | Domain Name System | Resolves domain names into IP addresses. | TCP/UDP 53
DCHP | Dynamic Host Configuration Protocol | Dynamically assigns IP addresses and other network configuration on joining a network. | UDP 67, 68

## Slide 12: Common port assignments (Cont.)
Protocol | Name | Description | Ports
NTP | Network Time Protocol | Used to synchronize device clocks with time servers. | UDP 123
MGCP | Media Gateway Control Protocol | Controls media gateways used to connect Voice over IP (VoIP) systems to conventional telephone networks. | TCP/UDP 2427, 2727
SIP | Session Initiation Protocol | Sends control information for multimedia communication sessions, like VoIP, video, and instant messaging. | TCP/UDP 5060, TCP 5061 (encrypted)
RTP | Real-time Transfer Protocol | Delivers streaming audio and video data over networks. | TCP/UDP 5004, 5005
H.323 | H.323 | Provides signaling and control for multimedia transmissions. | TCP/UDP 1720

## Slide 13: 1.1 Explain the purposes and uses of ports and protocols
Protocol types
ICMP Internet Control Message protocol – used to diagnose network communication issues in IP operations
Echo request and reply
  Also known as ping, these diagnostic messages are exchanged to verify that a host is connected and responding on the Network layer.
Host unreachable
  Signals when a router or host isn't responding.
Source quench
  Signals that network congestion is making a router or host slow to respond and notifies the sender to slow down.
Redirect
  Used by routers to notify the sender about a more efficient route to the remote host.
Time exceeded
  Sent whenever a packet reaches its TTL and is dropped by a router, or when a fragmented packet isn't reassembled properly.
Router advertisement and solicitation
  Used by routers to announce their presence on the network, and by hosts to find routers.

## Slide 14: 1.1 Explain the purposes and uses of ports and protocols
Protocol types
UDP User datagram protocol
Used for time-sensitive transmissions such as video playback or DNS lookups.
Does not establish a connection prior to transmission
Doers not check if data has arrived correctly
Faster than TCP
Applications using UDP must tolerate errors, loss and duplication
Datagrams have checksums so corrupt data can be discarded, but there's no reliability so it's not resent

## Slide 15: 1.1 Explain the purposes and uses of ports and protocols
Protocol types
TCP Transmission control protocol
Used where data integrity is required
Enforces a connection
Ensures packet order
Retransmits if errors occur
More overhead, so slower than UDP
Handshaking protocol – transmission only starts after acknowledgement by receiver

## Slide 16: 1.1 Explain the purposes and uses of ports and protocols
Protocol types
IP Internet protocol
Connectionless – each packet is individually addressed and routed to its destination
Does not handle packet ordering or error checking (TCP function)
IP header has:
Source and destination address
Header length
Packet length
Time to live (TTL)
TCP or UDP being used
and others

## Slide 17: 1.2 Explain devices, applications, protocols and services at their appropriate OSI layers
Layer 1 – Physical
Layer 2 – Data link
Layer 3 – Network
Layer 4 – Transport
Layer 5 – Session
Layer 6 – Presentation
Layer 7 – Application

## Slide 18: OSI model
Open Systems Interconnection Reference Model
It’s a guide (thus the term “model”)
  Don’t get wrapped up in the details
This is not the OSI protocol suite
  Most of the OSI protocols didn’t catch on
There are unique protocols at every layer
You’ll refer to this model for the rest of your career
Layer 7
Application
Layer 6
Presentation
Layer 5
Session
Layer 4
Transport
Layer 3
Network
Layer 2
Data Link
Layer 1
Physical
Notes: All People Seem To Need Data Processing

## Slide 19: OSI model
Open Systems Interconnection Reference Model
Mnemonic
  Please Do Not Throw Sausage Pizza Away
Layer 7
Application
Layer 6
Presentation
Layer 5
Session
Layer 4
Transport
Layer 3
Network
Layer 2
Data Link
Layer 1
Physical

## Slide 20: The OSI Layers
The switching layer
(Frame, MAC address, EUI-48, EUI-64, Switch)
The “post office” layer
(TCP segment, UDP datagram)
Encoding and encryption
(SSL/TLS)
The layer we see – Google Mail, Twitter, Facebook
Communication between devices (Control protocols, tunnelling protocols)
The routing layer
(IP address, router, packet)
Signalling, cabling, connectors
(Cable, NIC, Hub)
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 21: OSI model

## Slide 22: OSI Model – Layer 1: The Physical Layer
The physics of the network
  Signalling, cabling, connectors
  This layer isn’t about protocols
You have a physical layer problem
  Fix your cabling, punch-downs, etc.
  Run loopback tests, test/replace cables, swap adapter cards

## Slide 23: OSI Model – Layer 1: The Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next
1010101100001101
110
1010101100001101
110
From Data Link Layer
To Data Link Layer
Transmission Medium
Physical Layer

## Slide 24: OSI Model – Layer 2: Data Link Layer
The basic network “language”
The foundation of communication at the data link layer
Data Link Control (DLC) protocols
  MAC (Media Access Control) address on Ethernet
The “switching” layer
9C-35-58-5F-4C-D7
0C-9D-92-87-47-1E
1
1
1
0
0
1
0
Notes: The Data Link Layer is referencing the MAC addresses that are communicating on the network.

## Slide 25: OSI Model – Layer 2: The Data Link Layer
Data
H2
From Network Layer
To Network Layer
Data Link Layer
T2
Data
H2
T2
Data Link Layer
To Physical Layer
From Physical Layer
The data link layer is responsible for moving frames from one hop (node) to the next.
Notes: H2 is the Header
Data is the packet from the network layer
The trailer includes error detection and the ending transmission data

## Slide 26: Hop-to-Hop delivery

## Slide 27: OSI Model - Layer 3: Network Layer
The “routing” layer
Internet Protocol (IP)
Fragments frames to traverse different networks

## Slide 28: OSI Model - Layer 3: Network Layer
What is IP Fragmentation?
  Fragments are always in multiples of 8 because of the number of fragmentation offset bits in the IP header

## Slide 29: OSI Model – Layer 3: The Network Layer
Data
H3
From Transport Layer
To Transport Layer
Network Layer
Data
H3
Network Layer
To Data Link Layer
From Data Link Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.
Notes: H3 is the Header
Data is the packet from the transport layer

## Slide 30: Source to Destination Delivery
Data Link Layer
Link
X
X
X
Link
Link
Link
Link
A
C
B
E
D
Intermediate
system
Intermediate
system
Intermediate
system
A
B
E
F
F
Network
Data Link
Physical
Network
Data Link
Physical
Network
Data Link
Physical
Hop-to-hop delivery
Hop-to-hop delivery
Hop-to-hop delivery
Source-to-destination delivery

## Slide 31: OSI Model – Layer 4: Transport Layer
The “post office” layer
  Parcels and letters
TCP (Transmission Control Protocol) and UDP (User Datagram Protocol)

## Slide 32: Transport Layer
The transport layer is responsible for the delivery of a message from one process to another.
Data
H4
From Session Layer
To Session Layer
Transport Layer
Transport Layer
To Network Layer
From Network Layer
Data
H4
Data
H4
Data
H4
Data
H4
Data
H4

## Slide 33: OSI Model – Layer 5: Session
Communication management between devices
  Start, stop, restart
Half-duplex, full-duplex
Control protocols, tunnelling protocols

## Slide 34: Session Layer
The session layer is responsible for dialog control and synchronization.
From Presentation Layer
To Presentation Layer
Session Layer
Session Layer
To Transport Layer
From Transport Layer
H5
H5
SYN
SYN
SYN
SYN
SYN
SYN

## Slide 35
The session layer is responsible for dialog control and synchronization.
Session Layer

## Slide 36: OSI Model – Layer 6: Presentation
Character encoding
Application encryption
Often combined with the Application Layer

## Slide 37: OSI Model – Layer 6: Presentation
From Application Layer
To Application Layer
Presentation Layer
Presentation Layer
To Session Layer
From Session Layer
Data
H6
The presentation layer is responsible for translation, compression, and encryption.
Data
H6

## Slide 38: OSI Model – Layer 7: Application
The layer we see - HTTP, FTP, DNS, POP3

## Slide 39: OSI Model – Layer 7: Application
The application layer is responsible for providing services to the user.
X.500
FTAM
X.400
…
Data
H7
User:
Human or Program
Application Layer
To Presentation Layer
Message
X.500
FTAM
X.400
…
Data
H7
User:
Human or Program
Application Layer
From Presentation Layer
Message

## Slide 40: Summary of Layers
To organise bits into frames; to provide hop-to-hop delivery
To provide reliable process-to-process message delivery and error recovery
To translate, encrypt and compress data
To allow access to network resources
To establish, manage and terminate sessions
To move packets from source to destination; to provide internetworking
To transmit bits over a medium; to provide mechanical and electrical specifications
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 41: 1.3 Explain the concepts and characteristics of routing and switching
Properties of network traffic
  Broadcast domains
  CSMA/CD
  CSMA/CA
  Collision domains
  Protocol data units
  MTU
  Broadcast
  Multicast
  Unicast
Segmentation and interface properties
  VLANs
  Trunking (802.1q)
  Tagging and untagging ports
  Port mirroring
  Switching loops/spanning tree
  PoE and PoE+ (802.3af, 802.3at)
  DMZ
  MAC address table
  ARP table

## Slide 42: Transmission Media
The physical channel through which signals travel to allow nodes to communicate
All use electromagnetic radiation of type or the other
  Electrical
  Light
  Radio signals
Transmission media can be classified as:
  Cabled
  wireless

## Slide 43: Transmission Media - Cabled
A physical signal conductor between two nodes
Cable types such as:
  Copper
  Fibre optic
Cabled media can also be described as bounded media

## Slide 44: Transmission Media - Wireless
Uses free space between nodes
Types such as:
  Microwave radio
Wireless media can also be described as unbounded media

## Slide 45: Signaling and modulation
Every kind of physical network needs to turn data into a signal that can be sent across the media.
The simplest way is by encoding it into a single binary signal and transmitting it along a wire or fiber optic cable
This is called digital baseband, or line coding, and is the method used by Ethernet cables among others
Notes: Every kind of physical network needs to turn data into a signal that can be sent across the media. The simplest way is by encoding it into a single binary signal and transmitting it along a wire or fiber optic cable. This is called digital baseband, or line coding, and is the method used by Ethernet cables among others.
As you know, a cable, on which bits in the form of signals are transmitted, is busy with signals containing zeros and ones, and to distinguish between what bits are the actual travelled data and what bits are non-wanted noise is very difficult ; so a method to tell the difference is required. For that reason, control information is utilized. This information is in the form of zeros and ones that indicate where a frame start and where the frame ends.

## Slide 46: Signaling and modulation (Cont.)
In other communication types, especially those used over long distances, data is combined with a signal called a carrier wave

## Slide 47: Signaling and modulation (Cont.)
Three channels in a broadband transmission

## Slide 48: Signal Methods
Notes: Three possible variations which are amplitude, frequency, and phase.

## Slide 49: Bit rate and bandwidth
Bit rate, the number of bits carried per second
For example, the earliest popular Ethernet standards had a bit rate of ten megabits per second, abbreviated as 10 Mbps
  Gross bit rate
  Net bit rate or throughput
  goodput
Notes: Bandwidth means the amount of data that can be carried in a given amount of time; or, in other words, the capacity of a medium to carry data in a specific period of time. As stated previously, data transfer is measured using bits per second (bps). Thanks to the technological development, bandwidth is now commonly referred to in kilobits per second and megabits per second, and in case using highly sophisticated media, bandwidth can reach gigabits per second and terabits per second. These speeds can be achieved relying on the physical characteristics of media and the signalling method being applied. Thus if one is to calculate the bandwidth of a given medium, the physical properties as well as the signalling method must be taken into consideration.
Throughput can be defined as the real or actual data transfer rate in a given amount of time. We said that bandwidth is the capacity of a medium for data transmission, however, this capacity is hardly attained in real data transfer because of a variety of factors such as interference, noise, and errors in data transmission. For this reason, when we talk about bandwidth, we are actually taking about a theoretical rate of speed which is not same when data frames are really transmitted, whereas when we refer to the speed rate of a given medium using a throughput value, we are actually utilizing the real value at which data frames are carried. This means that throughput is bandwidth minus interference and errors, and therefore bandwidth is theoretical and throughput is practical.
Goodput denotes the transfer rate of the actual usable data bits; or, to put it another way, goodput measures the final data that the user benefits from or use, for data such as a picture, text, or video does not travel on media alone, but rather there is another control information, which is generally considered as data, or what is referred to as overhead. Its purpose is to make sure that data is safe, undamaged, unrepeated, and to guide data up to the destination. By and large, it can be said that goodput is throughput minus overhead traffic

## Slide 50: Bit rate and bandwidth (Cont.)
A transmission using two-bit symbols

## Slide 51: Multiplexing
Space-division multiplexing (SDM)
Frequency-division multiplexing (FDM)
Time-division multiplexing (TDM)
Notes: Space-division multiplexing, also known as Space-division multiple access is the use of separate point-to-point electrical conductors for each transmitted channel. Examples include an analogue stereo audio cable, with one pair of wires for the left channel and another for the right channel, and a multi-pair telephone cable, a switched star network such as a telephone access network, a switched Ethernet network, and a mesh network.
Frequency-division multiplexing (FDM) is inherently an analogue technology. FDM achieves the combining of several signals into one medium by sending signals in several distinct frequency ranges over a single medium. In FDM the signals are electrical signals.
Time-division multiplexing (TDM) is a digital (or in rare cases, analogue) technology which uses time, instead of space or frequency, to separate the different data streams. TDM involves sequencing groups of a few bits or bytes from each individual input stream, one after the other, and in such a way that they can be associated with the appropriate receiver. If done sufficiently quickly, the receiving devices will not detect that some of the circuit time was used to serve another logical communication path.
Multiple low data rate signals are multiplexed over a single high data rate link, then demultiplexed at the other end

## Slide 52: Media Access Control
The MAC address
Ethernet Media Access Control address
The “physical” address of a network adapter
Unique to a device
48 bits / 6 bytes long
Displayed in hexadecimal
00:0a:83
:
00:0a:83
Organisationally Unique Identifier (OUI)
Network Interface Controller-Specific
The manufacturer
The serial number
Notes: A physical address corresponding to a particular network interface.
Ethernet's physical address format is a 48-bit number called a MAC address, MAC-48, or EUI-48.
MAC addresses are usually written as 12 hexadecimal digits. For readability, they're usually grouped into pairs, separated by dashes or colons; for example, 10:0D:7F:F3:CE:8F.
Sometimes you'll also see three groups of four separated by periods or full stops, such as 100D.7FF3.CE8F.

## Slide 53: MAC addresses (Cont.)
0001101
0D
00010000
10
01111111
7F
00010010
12
11001110
CE
00001101
0D
0001101
0D
00010000
10
01111111
7F
00010010
12
11001110
CE
00001101
0D
11111111
FF
11111110
FE
MAC Address
EUI-64 Address

## Slide 54: Unicast, broadcast, and multicast
An address corresponding to a specific recipient is called a unicast address.
A broadcast address is intended to be read by any node that receives it.

## Slide 55: Unicast, broadcast, and multicast (Cont.)
Multicast addresses are intended to go to multiple nodes but not everywhere on the network
0001101
0D
00010000
10
01111111
7F
00010010
12
11001110
CE
00001101
0D

## Slide 56: Media Access Control - Duplex
Half-duplex
A device cannot send and receive simultaneously
All LAN hubs are half-duplex devices
Switch interfaces can be configured as half-duplex, but usually only when connecting to another half-duplex device
Full-duplex
Data can be sent and received at the same time
A properly configured switch interface will be set to full-duplex

## Slide 57: Ethernet Frames
There have been four different Ethernet frame types defined over the years
Only the Ethernet II frame type is used today
Every version of 802.3 Ethernet uses the same Ethernet II frame
Using frames addresses two networking issues
  Frames prevent any single machine from monopolizing the shared bus cable
  The process of retransmitting lost data is more efficient
Notes: An Ethernet frame is a data link layer protocol data unit and uses the underlying Ethernet physical layer transport mechanisms

## Slide 58: Ethernet Frame
EtherType values:
0x0800 signals that the frame contains an IPv4 datagram 0x0806 indicates an ARP frame
0x86DD indicates an IPv6 frame
0x8100 indicates the presence of an IEEE 802.1 Q tag
Destination MAC Address
Source MAC Address
EtherType
MAC Header
(14 bytes)
Data
(46 - 1500 bytes)
4 bytes
Payload
CRC Checksum
A8 A1 59 1D 79 8F
A8 A1 52 1D 21 98
08 00
IP, ARP, etc.
01 20 13 3A
Ethernet Type II Frame
(64 to 1518 bytes)
Notes: The MAC header has 14 bytes and the payload can have from 46 to 1500 bytes. The checksum is 4 bytes which means that the Type II frame can therefore have from 64 to 1518 bytes

## Slide 59: Ethernet Deployment Standards

## Slide 60: 802.3 Standards
Here’s a small selection of 802.3 standards:
802.3i 10 Mbps Ethernet using twisted pair cabling (1990)
802.3ab Gigabit Ethernet over twisted pair (1999)
802.3by 25 Gigabit Ethernet over fibre (2016)
The 802.3 committee defines wired network standards that share the same basic frame type and network access method
802.3a 10BASE2 10 Mbit/s (1.25 MB/s) over thin Coax (1985)
802.3u 100BASE-TX, 100BASE-T4, 100BASE-FX Fast Ethernet at 100 Mbit/s (12.5 MB/s) (1995)
Notes: 802.3a (1985) 10BASE2 10 Mbit/s (1.25 MB/s) over thin Coax (a.k.a. thinnet or cheapernet)
802.3u (1995) 100BASE-TX, 100BASE-T4, 100BASE-FX Fast Ethernet at 100 Mbit/s (12.5 MB/s) with autonegotiation

## Slide 61: Address Resolution Protocol
A protocol used by the Internet Protocol (IP) [RFC826], specifically IPv4, to map IP network addresses to the hardware addresses used by a data link protocol
The protocol operates below the network layer as a part of the interface between the OSI network and OSI link layer
It is used when IPv4 is used over Ethernet
For ARP, we are talking about layer 2
Notes: ARP stands for Address Resolution Protocol. When you try to ping an IP address on your local network, say 192.168.1.1, your system has to turn the IP address 192.168.1.1 into a MAC address. This involves using ARP to resolve the address, hence its name.

## Slide 62: Address Resolution Protocol
There are four types of ARP messages that may be sent by the ARP protocol
These are identified by four values in the "operation" field of an ARP message
The types of message are:
  ARP-Request (Broadcast, source IP address of the requester)
  ARP-Reply (Unicast to requester, the target)

## Slide 63: Address Resolution Protocol
The format of an ARP message is shown below:
Hardware type
Protocol type
HW LEN
Protocol LEN
Operation
Sender IP Address (octets 2-3)
Sender Hardware Address (octets 4-5)
Sender IP Address (octets 0-1)
Sender Hardware Address (octets 0-3)
Target Hardware Address (octets 0-1)
Target Hardware Address (octets 2-5)
Target IP Address (octets 0-3)
Notes: Hardware (HW) Type: 1 is for Ethernet
Protocol Type: 080016 = IP address
Hardware Length and Protocol length allows arbitrary networks to be used
Operation: 1 = ARP request, 2 = ARP response, 3 = RARP request, 4 = RARP response
ARP messages are sent directly to MAC layer
ARP message is 28 octets long

## Slide 64: Packet Sniffers
A packet analyser (also known as a packet sniffer) is a computer program or piece of computer hardware
Can intercept and log traffic that passes over a digital network or part of a network
A "Packet Sniffer" is a utility that sniffs without modifying the network's packets in any way
Packet sniffers merely watch, display, and log this traffic
Notes: A packet analyser (also known as a packet sniffer) is a computer program or piece of computer hardware (such as a packet capture appliance) that can intercept and log traffic that passes over a digital network or part of a network
A "Packet Sniffer" is a utility that sniffs without modifying the network's packets in any way
Packet sniffers merely watch, display, and log this traffic
By comparison, a firewall sees all of a computer's packet traffic as well, but it has the ability to block and drop any packets that its programming dictates

## Slide 65
Hub
Computer C
Computer B
Computer A
Broadcast
Computer
Computer C
is the recipient
of the data packet
Hub broadcasts data packet to all network computers
Data packet sent to computer C
Passive sniffing
Notes: Passive sniffing is intercepting packages transmitted over a network that uses a hub. It is called passive sniffing because it is difficult to detect. It is also easy to perform as the hub sends broadcast messages to all the computers on the network.

## Slide 66
Switch
Computer C
Computer B
Computer A
Broadcast
Computer
Computer C
is the recipient
of the data packet
Switch maps IP/MAC addresses to physical ports
Data packet sent to computer C
Active sniffing
Notes: Active sniffing is intercepting packages transmitted over a network that uses a switch. There are two main methods used to sniff switch linked networks, ARP Poisoning, and MAC flooding.

## Slide 67
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Intro
Monday
Tuesday
Wednesday
Thursday
Friday

## Slide 68: 1.3 Explain the concepts and characteristics of routing and switching
Routing protocols (IPv4 and IPv6)
  Distance-vector routing protocols
    RIP
    EIGRP
  Link-state routing protocols
    OSPF
  Hybrid
    BGP
Routing types
  Static
  Dynamic
  Default
IPv6 concepts
  Addressing
  Tunneling
  Dual stack
  Router advertisement
  Neighbor discovery

## Slide 69: Routing
Routing enables us to interconnect individual LANs into WANs
Routers act as the interconnection points
They can inspect incoming packets and forward them toward their eventual LAN destination
Routers are, for the most part, automatic
They require very little in terms of maintenance
Notes: Routing enables us to interconnect individual LANs into WANs
Routers act as the interconnection points
They have all the built-in smarts to inspect incoming packets and forward them toward their eventual LAN destination
The goal of this section is to take you into the world of routers and show you how they do this.
They require very little in terms of maintenance once their initial configuration is complete because they can talk to each other to determine the best way to send IP packets

## Slide 70: How Routers Work
Any piece of hardware or software that forwards packets based on their destination IP address
Routers work:
  at the Network layer of OSI
  at the Internet layer of the TCP/IP model
Working connections are circled
One port leads to one network; the other leads to another network
Notes: A router is any piece of hardware or software that forwards packets based on
their destination IP address. Routers work, therefore, at the Network layer of
the OSI model and at the Internet layer of the TCP/IP model.
Classically, routers are dedicated boxes that contain at least two
connections, although many routers contain many more connections.
The two “working” connections are circled. One port leads to
one network; the other leads to another network. The router reads the IP
addresses of the packets to determine where to send the packets.

## Slide 71: Diagrammatically
81.14.234.7
68.39.12.45

## Slide 72
Notes: The typical home router, however, serves multiple functions, often combining a router, a switch, and other features like a firewall (for protecting your network from intruders), a DHCP server, and much more into a single box.

## Slide 73: Commercial Router vs Home Router
Notes: So, we see that with the home router, we are very limited in what we can do. Note that both boxes connect two networks. The big difference is that one side of the Linksys home router connects directly to a built-in switch. That’s convenient! You don’t have to buy a separate switch to connect multiple computers to the home router.
All routers - big and small, plain or bundled with a switch - examine packets and then send the packets to the proper destination.

## Slide 74: End Systems and Intermediate Systems
All IP hosts are capable of functioning as routers
Workstations and server typically only have one network interface adapter connected to one network
Hosts with no capacity to forward packets to other IP networks are referred to as end systems.
Router s that interconnect IP networks and can perform the packet forwarding process are known as Intermediate systems
Notes: All IP hosts are capable of functioning as routers.

## Slide 75: Routing tables
Network address
Netmask
Gateway
Interface
Metric

## Slide 76: Local route entries

## Slide 77: The route command
Command | Description
route PRINT | Prints the current routing table.
route[-p] ADD destination MASK netmaskgateway | Adds a route to the specified destination and netmask, using the specified gateway. If the -p switch is used, the route is persistent even after rebooting. Otherwise, it is not preserved when the system restarts
route CHANGE destination MASK netmaskgateway | Changes an existing route to the specified destination and netmask,
route DELETE destination | Removes a route to the specified destination.
route -f | Clears all gateway entries to the routing table.

## Slide 78: Remote routes
Broadly speaking, routing protocols can be separated into two categories according to their scope.
  Interior gateway protocols are used to communicate routing information within an autonomous system - a network or series of networks that's controlled by a single administrative identity, using a unified routing policy. These are the most important protocols for determining routes within an organization's network.
  Exterior gateway protocols are used to communicate routing information between autonomous systems. These are the protocols which allow the internet to function.

## Slide 79: Interior gateway protocols
Interior gateway protocols tend to have an ultimate goal of network convergence, or a state where every router on the network has communicated with the others, and all are in agreement on the best path between any two points.
Interior protocols are further categorized by what information routers share and how they communicate it. The two traditional approaches are distance vector and link state, though some hybrid protocols combine elements of both.

## Slide 80: Distance vector routing protocols
In a distance vector routing protocol, routers exchange information in the form of vectors (arrays) of distance and direction to a given destination. Routers only exchange information with their immediate neighbors. By comparing information from different neighbors with its own local knowledge, the router can apply an algorithm to determine the best route from its own location.

## Slide 81: Link state protocols
Link state protocols don't rely on timed advertisements. Instead, they communicate when they join the network, and monitor for topology changes.
To reduce traffic, they also don't share their full routing information every time, but only when the network state changes. This means routers send two types of messages.
  Hello packets just contain a router's identity and location.
  Link state advertisements (LSAs) contain routing information.

## Slide 82: Exterior gateway protocols
Exterior gateway protocols have a wholly different set of concerns. They don't worry as much about end to end mapping of the entire network, but instead focus on finding routes between autonomous systems.
Border Gateway Protocol (BGP)

## Slide 83: Autonomous systems
An AS can be classified into one of three categories, depending on how it connects to other networks and what kind of traffic it carries
A transit AS connects to multiple other networks and serves as an open conduit for traffic between them
Typically, a transit AS is an ISP or something similar
    A multi-homed AS connects to multiple other networks, but doesn't carry external traffic; it just uses multiple connections for redundancy or load balancing
    A stub AS only connects to one other AS, so to other networks it will appear to be just part of that "upstream" AS
Notes:   An AS can be classified into one of three categories, depending on how it connects to other networks and what kind of traffic it carries.
    A transit AS connects to multiple other networks and serves as an open conduit for traffic between them. Typically, a transit AS is an ISP or something similar.
    A multihomed AS connects to multiple other networks, but doesn't carry external traffic; it just uses multiple connections for redundancy or load balancing.
    A stub AS only connects to one other AS, so to other networks it will appear to be just part of that "upstream" AS.

## Slide 84: Multi-homing
The brute force method
Set your primary connection as the default route, and manually change it whenever there's an outage.
Use a first hop redundancy protocol (FHRP) to provide high availability

## Slide 85: Multi-protocol routing
The first is what the router should do when it encounters two conflicting routes to a destination via two different protocols
The second problem is that if a router is using two protocols, that probably means it's connected on one interface to routers only using one protocol, and on another interface to routers only using the other
Route redistribution can be pretty complicated, since every protocol has its own set of metrics which might not be very compatible, its own way of communicating between routers, its own convergence rate, and so on. Successfully redistributing routes takes knowledge of the specific network, and careful configuration

## Slide 86: Address translation

## Slide 87: NAT methods
One-to-one
One-to-many

## Slide 88: NAT methods (Cont.)
Source network address translation (SNAT)
Destination network address translation (DNAT)

## Slide 89: PAT

## Slide 90: NAT and IPv6
NAT64
NAT66
NPTv6

## Slide 91: Exercise: NAT configuration

## Slide 92: Assessment: Routing
Your company's network is too big to use static routing, but the topology is simple and doesn't change very often. What routing protocol would be the easiest to use while still meeting your needs? Choose the best response.
BGP
IS-IS
OSPF
RIP
D

## Slide 93: Assessment: Routing
Your company network is a multihomed AS. What protocol would your gateway routers need to learn Internet paths? Choose the best response.
BGP
IS-IS
OSPF
RIP
A

## Slide 94: Assessment: Routing
Even with modern routing protocols, you still might want to set static route entries. True or false?
True
False
True

## Slide 95: Assessment: Routing
What might a router using PAT change on packets passing through? Choose all that apply.
Destination port for incoming packets
Destination port for outgoing packets
Destination address for incoming packets
Source address for incoming packets
Source port for incoming packets
Source port for outgoing packets
A, C, and F

## Slide 96: Summary: Internetworking
You should now know how to:
Why switching loops can destroy network function, and how switching protocols optimize L2 performance while preventing loops.
How routers govern network traffic by learning and communicating optimal routes through the network, the relative benefits of different common routing protocols, and how network translation can connect two networks with different addressing schemes.

## Slide 97: Internet Protocol
A set of rules governing the format of data sent over the Internet or other network
The Internet Protocol is the principal communications protocol in the Internet protocol suite for relaying datagrams across network boundaries
Its routing function enables internetworking, and essentially establishes the Internet

## Slide 98: IPv4
Is a Network Layer Protocol
Provides logical host and network addressing, and routing
Provides a best effort delivery
Packet might be delivered out of sequence, lost entirely, duplicated, or delayed
Notes: Internet Protocol version 4 (IPv4) is the fourth version of the Internet Protocol (IP). It is one of the core protocols of standards-based internetworking methods in the Internet and other packet-switched networks. IPv4 was the first version deployed for production in the ARPANET in 1983

## Slide 99: IPv4 Address
The IP address is a unique identifier for each device on a network
IP provides
  Specification of the exact format of all data
  Performs routing functions
  Includes a set of rules

## Slide 100: IPv4 Address
A 32 bit numeric address divided into 4 parts
Each 8-bit block is known as an octet
Has a denary range of 0 to 255
IPv4 produces 4 billion unique addresses (4 x 109)
Example: 192.168.1.5

## Slide 101: IPv4 Address Conversion
8 Bits
8 Bits
8 Bits
8 Bits
.
.
.
When all bits are set to the value of 1 we get the sum of 255
11111111
1111111
1111111
11111111
.
.
.
27 + 26 + 25 + 24 + 23 + 22 + 21 + 20
128 + 64 + 32 + 16 + 8 + 4 + 2 + 1
=
255
Notes: We have a representation of the format of IPv4
When all bits are set to the value of 1 we get the sum of 255

## Slide 102: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
27 + 26 + 0 + 0 + 0 + 0 + 0 + 0
128 + 64
=
192

## Slide 103: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
27 + 0 + 25 + 0 + 23 + 0 + 0 + 0
128 + 32 + 8
=
168

## Slide 104: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
0 + 0 + 0 + 24 + 23 + 0 + 0 + 0
16 + 8
=
24

## Slide 105: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
0 + 0 + 0 + 0 + 23 + 22 + 21 + 20
8 + 4 + 2 + 1
=
15

## Slide 106: IPv4 Datagram
Header
Data
20 to 65535 bytes
20 bytes

## Slide 107: IPv4 Datagram
Header
Data
VER
4 bits
HLEN
4 bits
Service Type
8 bits
Total Length
16 bits
Identification (Fragment ID)
16 bits
Flags
3 bits
Fragmentation Offset
13 bits
Header Checksum
16 bits
Protocol
8 bits
Time to Live
8 bits
Source IP Address
Destination IP Address
Options
Notes: The IP Version field (4 bits) contains the value 4, which in binary is “0100”
The Header Length field (4 bits) indicates how long the header is, in 32 bit “words”. The minimum value is “5” which would be 160 bits, or 20 bytes. The maximum length is 15, which would be 480 bits, or 60 bytes. If you skip that number of words from the start of the packet, that is where the data starts (this is called the “offset” to the data). This will only ever be greater than 5 if there are options before the data part (which is not common).
The Type of Service field (8 bits) is defined in RFC 2474, “Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 headers”, December 1998. This is used to implement a fairly simple QoS (Quality of Service). QoS involves management of bandwidth by protocol, by sender, or by recipient.
The Total Length field (16 bits) contains the total length of the packet, including the packet header, in bytes. The minimum length is 20 (20 bytes of header plus 0 bytes of data), and the maximum is 65,535 bytes (since only 16 bits are available to specify this). All network systems must handle packets of at least 576 bytes, but a more typical packet size is 1508 bytes. With IPv4, it is possible for some devices (like routers) to fragment packets (break them apart into multiple smaller packets) if required to get them through a part of the network that can’t handle packets that big. Packets that are fragmented must be reassembled at the other end. Fragmentation and reassembly is one of the messy parts of IPv4 that got cleaned up a lot in IPv6.
The Identification (Fragment ID) field (16 bits) identifies which fragment of a once larger packet this one is, to help in reassembling the fragmented packet later.
The next three bits are flags related to fragmentation. The first is reserved and must be zero. The next bit is the DF (Don’t Fragment) flag. If DF is set, the packet cannot be fragmented (so if such a packet reaches a part of the network that can’t handle one that big, that packet is dropped). The third bit is the MF (More Fragments) flag. If MF is set, there are more fragments to come. Unfragmented packets of course have the MF flag set to zero.
The Fragment Offset field (13 bits) is used in reassembly of fragmented packets. It is measured in 8 byte blocks. The first fragment of a set has an offset of 0.
The Time To Live (TTL) field (8 bits) is to prevent packets from being shuttled around indefinitely on a network.
The Protocol field (8 bits) defines the type of data found in the data portion of the packet. Protocol numbers are not to be confused with ports.
Some common protocol numbers are:
1 ICMP Internet Control Message Protocol (RFC 792)
6 TCP Transmission Control Protocol (RFC 793)
17 UDP User Datagram Protocol (RFC 768)
41 IPv6 IPv6 tunneled over IPv4 (RFC 2473)
83 VINES Banyan Vines IP
89 OSPF Open Shortest Path First (RFC 1583)
132 SCTP Streams Control Transmission Protocol
The Header Checksum field (16 bits). The 16-bit one’s complement of the one’s complement sum of all 16 bit words in the header.
The Source Address field (32 bits) contains the IPv4 address of the sender (may be modified by NAT).
The Destination Address field (32 bits) contains the IPv4 address of the recipient (may be modified by NAT in a reply packet).
Options (0 to 40 bytes) Not often used. Rarely if ever seen “in the wild”. These are not relevant here. If you want the details, read the RFCs.

## Slide 108: IPv4 Limitations
Limited number of IP addresses (4 billion)
No provision for authentication
Security issues
No provision for routing
Does not work well with large networks
Notes: 4 billion addresses, but more than 7 billion people with multiple devices

## Slide 109: Common Internet protocols
  TCP/IP (Transmission Control Protocol/Internet Protocol) is a stream protocol.
  Any data transmitted between these two endpoints is guaranteed to arrive, thus it is a so-called lossless protocol.
  It is also called a peer-to-peer protocol.
TCP/IP
  HTTP (HyperText Transfer Protocol) is the protocol used to transmit all data present on the World Wide Web.
  It is the protocol used to transmit HTML, the language that makes all the fancy decorations in your browser. It works upon TCP/IP.
HTTP
  FTP (File Transfer Protocol) is the protocol used to transmit files between computers connected to each other by a TCP/IP network, such as the Internet
FTP
  UDP (User Datagram Protocol) is one of the core members of the Internet protocol suite.
  UDP uses a simple connectionless communication model with a minimum of protocol mechanisms.
UDP
Notes: TCP/IP (Transmission Control Protocol/Internet Protocol) is a stream protocol. This means that a connection is negotiated between a client and a server. Any data transmitted between these two endpoints is guaranteed to arrive, thus it is a so-called lossless protocol. Since the TCP protocol (as it is also referred to in short form) can only connect two endpoints, it is also called a peer-to-peer protocol.
HTTP (HyperText Transfer Protocol) is the protocol used to transmit all data present on the World Wide Web. This includes text, multimedia and graphics. It is the protocol used to transmit HTML, the language that makes all the fancy decorations in your browser. It works upon TCP/IP.
FTP (File Transfer Protocol) is the protocol used to transmit files between computers connected to each other by a TCP/IP network, such as the Internet
UDP (User Datagram Protocol) is one of the core members of the Internet protocol suite. UDP uses a simple connectionless communication model with a minimum of protocol mechanisms

## Slide 110: The TCP/IP Protocol Suite
Ethernet
IP
TCP &UDP
SMTP, FTP, HTTP, POP3, IMAP4, SNMP
A protocol suite is a collection of protocols that are designed to work together
Application
Application
Presentation
Session
Transport
Networking
Datalink
Physical
Datalink and Physical
Transport
Networking
OSI
TCP/IP
Protocols
Notes: Note: The OSI model is an idealised networking model, whereas the TCP/IP model is a practical implementation.
What is important to understand is that the interfaces between the interfaces are well defined so that it is theoretically possible to replace a particular protocol with another one that operates at that level.
For example you should theoretically be able to replace the IP networking protocol with the IPX networking protocol without affecting how the application e.g. POP3 works.
Although this doesn’t always apply the application protocols like SMTP ,POP3 etc will work Okay across different data link protocols like Ethernet,Token ring etc.

## Slide 111: Internetworking
Internetworking is the process or technique of connecting different types of networks by using intermediary devices such as routers or gateway devices in order to exchange packets
Internetworking ensures data communication among networks owned and operated by different entities using a common data communication and the Internet Routing Protocol
An internetworking device is a widely-used term for any hardware within networks that connect different network resources
Key devices that comprise a network are routers, bridges, repeaters and gateways

## Slide 112: IPv4 Addressing
IP addresses are 32-bit binary values: for readability purposes they're usually written as four octets in dotted decimal location
It's not just a serial number though: each address has two parts
The network ID identifies a unique subnet on the wider network, while the host ID identifies a specific host on that subnet.
192.168.
133.178
Network ID
Host ID
Notes: IP addresses are 32-bit binary values: for readability purposes they're usually written as four octets in dotted decimal location. It's not just a serial number though: each address has two parts
The network ID identifies a unique subnet on the wider network, while the host ID identifies a specific host on that subnet.

## Slide 113: IPv4 addresses (Cont.)

## Slide 114: Classful and classless addressing
Classless interdomain routing (CIDR)
Class | First octet | First bits | # of subnets | # of hosts | Subnet mask | Mask prefix
A | 0.-127. | 0 | 128 | 16,777,216 | 255.0.0.0 | /8
B | 128.-191. | 10 | 16,384 | 65,536 | 255.255.0.0 | /16
C | 192.-223. | 110 | 2,097,152 | 256 | 255.255.255.0 | /24
D | 224.-239. | 1110 | * | * | * | *
E | 240.-254. | 1111 | * | * | * | *

## Slide 115: Problems with class-based IP addressing
The classful routing system included classes A, B, and C:
Class A - Over 16 million host identifiers
Class B - 65,535 host identifiers
Class C - 254 host identifiers
The old method of IP addressing came with inefficiencies that exhausted the availability of IPv4 addresses faster than it needed to
Notes: The problem would commonly occur when an organization required more than 254 host machines and therefore would no longer fall into class C but rather class B.
This means that the organization would use a class B license even though they had far less than 65,535 hosts.
Therefore if an organization only required 2,500 hosts, they would be wasting about 63,000 hosts by holding a class B license which would greatly decrease the availability of IPv4 addresses unnecessarily.

## Slide 116: Classless interdomain routing (CIDR)
An IP addressing scheme that improves the allocation of IP addresses
It replaces the old system based on classes A, B, and C
This scheme also helped greatly extend the life of IPv4 as well as slow the growth of routing tables
Notes: How does CIDR work?
CIDR is based on variable-length subnet masking (VLSM). This allows it to define prefixes of arbitrary lengths making it much more efficient than the old system. CIDR IP addresses are composed of two sets of numbers. The network address is written as a prefix, like you would see a normal IP address (e.g. 192.255.255.255). The second part is the suffix which indicates how many bits are in the entire address (e.g. /12). Putting it together, a CIDR IP address would look like the following:
192.255.255.255/12

## Slide 117: Map of Regional Internet Registries

## Slide 118: Variable-length subnet masking
The simplest way to subnet is to use fixed length subnet masking (FLSM), which divides a network into multiple subnets with the same mask prefix number.
The alternative is variable length subnet masking (VLSM), which allows you to subnet a network in multiple "passes", breaking it into subnets of variable size and thus variable subnet length.

## Slide 119: Special IPv4 addresses
0.0.0.0 is a non-routable address which can either mean the current network, the default route, any address at all, or a specific error condition, depending on context.
255.255.255.255 is the broadcast address to the currently configured subnet.
The entire Class A network 127.0.0.0 is reserved for loopback addresses, which as the name implies simply point right back to the local host.

## Slide 120: Special IPv4 addresses
Three private network ranges are defined for internal LANs.
The 169.254.0.0/16 network is reserved for link-local or automatic Private IP addressing (APIPA) addresses.
  10.0.0.0/8, or the single Class A network with addresses 10.0.0.0 - 10.255.255.255
  172.16.0.0/12, or the 16 contiguous Class B networks with addresses 172.16.0.0 - 172.31.255.255.
  192.168.0.0/16, or the 256 contiguous Class C networks with addresses 192.168.0.0 - 192.168.255.255.

## Slide 121: IPv4 subnetting
The main things to remember are that every IPv4 address is split into network ID and host ID, that each part consists of a contiguous series of bits in the binary address, and that both together are 32-bits
When you subnet an address, that means you borrow bits from the host ID portion, meaning fewer possible hosts, in exchange for making more subnets.

## Slide 122
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Intro
Monday
Tuesday
Wednesday
Thursday
Friday

## Slide 123: IPv6 Addressing
Internet Protocol v6 - 128-bit address
340,282,366,920,938,463,463,374,607,431,768,211,456 addresses (340 undecillion)
6.8 billion people could have 5,000,000,000,000,000,000,000,000,000 addresses each

## Slide 124: IPv6 Address Compression
Your DNS will become very important!
Groups of zeros can be abbreviated with a double colon ::
Only one of these abbreviations allowed per address
Leading zeros are optional

## Slide 125: IPv6
IPv6 uses a 128-bit address: this allows 2128 addresses
It allows easier network configuration, more efficient routing and data flow, and even improved security
The primary drawback is that it's a much different protocol from IPv4 and isn't backwards-compatible

## Slide 126: IPv6 addresses
Instead of dotted decimal, they're written as 32 hexadecimal digits, broken into eight groups of four separated by colons
fe80:0000:0000:0000:c249:3765:00c0:9b22

## Slide 127: Ipv6 Rules
Leading zeros in a group don't need to be displayed, so :00c0: can be displayed as :c0: instead.
A group consisting entirely of zeros can be displayed as :0:
Once per address, multiple consecutive groups of zeros can be replaced with a double-colon.
This means :0000:0000:0000: can be written as :: instead.
Using this method, the same address could be written as follows:
fe80::c249:3765:c0:9b22

## Slide 128: IPv6 Addresses (Cont.)
In a typical IPv6 address, the first 64 bits is the network prefix, while the last 64 bits is the device identifier
Global Routing Prefix
Subnet ID
Device Identifier
fe80 : d18 : 0000
: 12c0 :
5d18 : cffd : 0000 : fef3
128 bits = 16 bytes
16 bits
2 bytes
2 octets
=
=
Network
Node
Notes: In a typical IPv6 address, the first 64 bits is the network prefix, while the last 64 bits is the device identifier.
This can be divided into:
a global routing prefix
A subnet ID
And a device identifier

## Slide 129: IPv6 Address Types & Scope
Three
types
Global Unicast Address
Unique Local
Link Local
Scope Internet
Routed on Internet
Scope Internal
Network or VPN internally routable, but NOT routed on Internet
Scope network link
Not Routed internally or externally
Notes: IPv6 addresses have three types:
Global Unicast Address –Scope Internet- routed on Internet
Unique Local — Scope Internal Network or VPN internally routable, but Not routed on Internet
Link Local – Scope network link- Not Routed internally or externally.

## Slide 130: IPv6 Addressing - Global and Public Addresses
  These addresses are known as global Unicast addresses and are the equivalent of the public addresses of IPv4 networks
  The Internet authorities allocate address blocks to ISPs who in turn allocate them to their customers
Global addresses are routable on the internet and start with 2001
Notes: Global and Public Addresses
Global addresses are routable on the internet and start with 2001:
These addresses are known as global Unicast addresses and are the equivalent of the public addresses of IPv4 networks.
The Internet authorities allocate address blocks to ISPs who in turn allocate them to their customers.

## Slide 131: IPv6 Addresses - Internal Addresses
  Start with fe80
  Restricted to a link and are not routed on the Internal network or the Internet
  Link Local addresses are self assigned i.e. they do not require a DHCP server
  A link local address is required on every IP6 interface even if no routing is present
Link Local
  Meant to be used inside an internal network
  They are routed on the Internal network but not routed on the Internet
  The address space is divided into two /8 spaces: fc00::/8 for globally assigned addressing, and fd00::/8 for locally assigned addressing
  For manually assignment by an organisation use the fd00 prefix
Unique Local
Two Internal Address Types
Notes: Internal Addresses- Link Local and Unique Local
In IPv4 internal addresses use the reserved number ranges 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16 and 169.254.0.0/16.
These addresses are not routed on the Internet and are reserved for internal networks.
IPv6 also has two Internal address types.
Link Local
  Start with fe80
  Restricted to a link and are not routed on the Internal network or the Internet
  Link Local addresses are self assigned i.e. they do not require a DHCP server.
  A link local address is required on every IP6 interface even if no routing is present
Unique Local
Meant to be used inside an internal network
They are routed on the Internal network but not routed on the Internet
They are equivalent to the IPv4 addresses are 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16
The address space is divided into two /8 spaces: fc00::/8 for globally assigned addressing, and fd00::/8 for locally assigned addressing
For manually assignment by an organisation use the fd00 prefix.

## Slide 132: Using IPv6 Addresses in URLs
On IPv4 networks you can access a network resource e.g. a web page using the format http://192.168.1.21/webpage
URL’s don’t recognise colons
IPv6 addresses contain a colon as separator and so must be enclosed in square brackets
http://[IPv6 address]/webpage

## Slide 133: IPv6 Loop Back
The IPv6 loopback address is ::1. You can ping it as follows:
ping ::1
Force IPv6
Ping ::1 -6

## Slide 134: IPv6 migration
In dual stack operation, a host or router simply runs IPv4 along with IPv6, using the newer protocol when it can and the older when it must.
IPv4
IPv6
IPv4
Only
IPv4
Only
IPv4
IPv6
IPv4
IPv6
IPv4
IPv6
6
6
6
4
4
4
Router
IPv4 & IPv6

## Slide 135: IPv6 migration (Cont.)
Translation uses gateway protocols like NAT64 to connect an IPv6 network to an IPv4 network, much like conventional NAT.
IPv6
IPv6
IPv6
6
Router
NAT64
IPv4
WAN
IPv6
IPv6
6
6
4
>
Notes: NAT64 is an IPv6 transition mechanism that facilitates communication between IPv6 and IPv4 hosts by using a form of network address translation (NAT). The NAT64 gateway is a translator between IPv4 and IPv6 protocols,[1] for which function it needs at least one IPv4 address and an IPv6 network segment comprising a 32-bit address space. The "well-known prefix" reserved for this service is 64:ff9b::/96.
An IPv6 client embeds the IPv4 address it wishes to communicate with using the host part of the IPv6 network segment, resulting in an IPv4-embedded IPv6 addresses (hence the 32-bit address space in the IPv6 network segment), and sends packets to the resulting address. The NAT64 gateway creates a mapping between the IPv6 and the IPv4 addresses, which may be manually configured or determined automatically

## Slide 136: IPv6 migration (Cont.)
Tunneling allows two IPv6 networks to communicate over an IPv4 network by means of tunnel brokers, devices which encapsulate IPv6 packets into IPv4 packets.
IPv6
IPv6
IPv6
IPv6
IPv6
IPv6
6
6
6
IPv4
WAN
IPv6
IPv6
Tunnel
Broker
Tunnel
Broker
6
4
Notes: A tunnel broker is a service which provides a network tunnel. These tunnels can provide encapsulated connectivity over existing infrastructure to another infrastructure.
There are a variety of tunnel brokers, including IPv4 tunnel brokers, though most commonly the term is used to refer to an IPv6 tunnel broker as defined in RFC:3053.

## Slide 137: 1.3 Explain the concepts and characteristics of routing and switching
Performance concepts
  Traffic shaping
  QoS
  Diffserv
  CoS
NAT/PAT
Port forwarding
Access control list
Distributed switching
Packet-switched vs. circuit-switched network
Software-defined networking

## Slide 138: Performance concepts - QoS
Quality of Service (QoS) describes the strategies used to manage and increase the flow of network traffic
QoS features enable administrators to predict bandwidth use, monitor that use, and control it to ensure that bandwidth is available to the applications that need it
These applications generally can be broken into two categories:
Latency sensitive: These applications need bandwidth for quick delivery where network lag time impacts their effectiveness. This includes voice and video transfer. For example, Voice over IP (VoIP) would be difficult to use if there were a significant lag time in the conversation
Latency insensitive: Controlling bandwidth also involves managing latency-insensitive applications. This includes bulk data transfers such as huge backup procedures and File Transfer Protocol (FTP) transfers

## Slide 139: Quality of Service
QoS achieves more efficient use of network resources by differentiating between latency-insensitive traffic such as fax data and latency-sensitive streaming media
Two important components of QoS are DSCP and CoS

## Slide 140: Performance concepts: DiffServ
Differentiated services code point (also known as Diffserv) is an architecture that specifies a simple and coarse-grained mechanism for classifying and managing network traffic and providing QoS on modern networks

## Slide 141: Performance concepts: CoS
Class of service (CoS) is a parameter that is used in data and voice to differentiate the types of payloads being transmitted

## Slide 142
A packet shaper essentially performs two key functions: monitoring and shaping
Monitoring includes identifying where usage is high and the time of day
Administrators can then customise or shape bandwidth usage for the best needs of the network
Performance concepts: Traffic Shaping

## Slide 143: Performance concepts: Traffic Shaping
Ensure adequate bandwidth is available for mission-critical applications while few resources are dedicated to spam or peer-to-peer downloads
Need to monitor network traffic to ensure that data flows as you need it to
Describes the mechanisms used to control bandwidth usage on the network
Administrators can control who uses bandwidth, for what purpose, and what time of day bandwidth can be used
Establishes priorities for data traveling to and from the Internet and within the network

## Slide 144: Address translation

## Slide 145: NAT methods
One-to-one
One-to-many

## Slide 146: NAT methods (Cont.)
Source network address translation (SNAT)
Destination network address translation (DNAT)

## Slide 147: PAT

## Slide 148: 1.4 Given a scenario, configure the appropriate IP addressing components
Private vs. public
Loopback and reserved
Default gateway
Virtual IP
Subnet mask
Subnetting
  Classful
  Classes A, B, C, D, and E
  Classless
  VLSM
  CIDR notation (IPv4 vs. IPv6)
Address assignments
  DHCP
  DHCPv6
  Static
  APIPA
  EUI64
  IP reservations

## Slide 149: Internet Protocol
A set of rules governing the format of data sent over the Internet or other network
The Internet Protocol is the principal communications protocol in the Internet protocol suite for relaying datagrams across network boundaries
Its routing function enables internetworking, and essentially establishes the Internet

## Slide 150: IPv4
Is a Network Layer Protocol
Provides logical host and network addressing, and routing
Provides a best effort delivery
Packet might be delivered out of sequence, lost entirely, duplicated, or delayed
Notes: Internet Protocol version 4 (IPv4) is the fourth version of the Internet Protocol (IP). It is one of the core protocols of standards-based internetworking methods in the Internet and other packet-switched networks. IPv4 was the first version deployed for production in the ARPANET in 1983

## Slide 151: IPv4 Address
The IP address is a unique identifier for each device on a network
IP provides
  Specification of the exact format of all data
  Performs routing functions
  Includes a set of rules

## Slide 152: IPv4 Address
A 32 bit numeric address divided into 4 parts
Each 8-bit block is known as an octet
Has a denary range of 0 to 255
IPv4 produces 4 billion unique addresses (4 x 109)
Example: 192.168.1.5

## Slide 153: IPv4 Address Conversion
8 Bits
8 Bits
8 Bits
8 Bits
.
.
.
When all bits are set to the value of 1 we get the sum of 255
11111111
1111111
1111111
11111111
.
.
.
27 + 26 + 25 + 24 + 23 + 22 + 21 + 20
128 + 64 + 32 + 16 + 8 + 4 + 2 + 1
=
255
Notes: We have a representation of the format of IPv4
When all bits are set to the value of 1 we get the sum of 255

## Slide 154: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
27 + 26 + 0 + 0 + 0 + 0 + 0 + 0
128 + 64
=
192

## Slide 155: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
27 + 0 + 25 + 0 + 23 + 0 + 0 + 0
128 + 32 + 8
=
168

## Slide 156: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
0 + 0 + 0 + 24 + 23 + 0 + 0 + 0
16 + 8
=
24

## Slide 157: IPv4 Example
192
168
24
15
.
.
.
11000000
10101000
00011000
00001111
.
.
.
0 + 0 + 0 + 0 + 23 + 22 + 21 + 20
8 + 4 + 2 + 1
=
15

## Slide 158: IPv4 Datagram
Header
Data
20 to 65535 bytes
20 bytes

## Slide 159: IPv4 Datagram
Header
Data
VER
4 bits
HLEN
4 bits
Service Type
8 bits
Total Length
16 bits
Identification (Fragment ID)
16 bits
Flags
3 bits
Fragmentation Offset
13 bits
Header Checksum
16 bits
Protocol
8 bits
Time to Live
8 bits
Source IP Address
Destination IP Address
Options
Notes: The IP Version field (4 bits) contains the value 4, which in binary is “0100”
The Header Length field (4 bits) indicates how long the header is, in 32 bit “words”. The minimum value is “5” which would be 160 bits, or 20 bytes. The maximum length is 15, which would be 480 bits, or 60 bytes. If you skip that number of words from the start of the packet, that is where the data starts (this is called the “offset” to the data). This will only ever be greater than 5 if there are options before the data part (which is not common).
The Type of Service field (8 bits) is defined in RFC 2474, “Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 headers”, December 1998. This is used to implement a fairly simple QoS (Quality of Service). QoS involves management of bandwidth by protocol, by sender, or by recipient.
The Total Length field (16 bits) contains the total length of the packet, including the packet header, in bytes. The minimum length is 20 (20 bytes of header plus 0 bytes of data), and the maximum is 65,535 bytes (since only 16 bits are available to specify this). All network systems must handle packets of at least 576 bytes, but a more typical packet size is 1508 bytes. With IPv4, it is possible for some devices (like routers) to fragment packets (break them apart into multiple smaller packets) if required to get them through a part of the network that can’t handle packets that big. Packets that are fragmented must be reassembled at the other end. Fragmentation and reassembly is one of the messy parts of IPv4 that got cleaned up a lot in IPv6.
The Identification (Fragment ID) field (16 bits) identifies which fragment of a once larger packet this one is, to help in reassembling the fragmented packet later.
The next three bits are flags related to fragmentation. The first is reserved and must be zero. The next bit is the DF (Don’t Fragment) flag. If DF is set, the packet cannot be fragmented (so if such a packet reaches a part of the network that can’t handle one that big, that packet is dropped). The third bit is the MF (More Fragments) flag. If MF is set, there are more fragments to come. Unfragmented packets of course have the MF flag set to zero.
The Fragment Offset field (13 bits) is used in reassembly of fragmented packets. It is measured in 8 byte blocks. The first fragment of a set has an offset of 0.
The Time To Live (TTL) field (8 bits) is to prevent packets from being shuttled around indefinitely on a network.
The Protocol field (8 bits) defines the type of data found in the data portion of the packet. Protocol numbers are not to be confused with ports.
Some common protocol numbers are:
1 ICMP Internet Control Message Protocol (RFC 792)
6 TCP Transmission Control Protocol (RFC 793)
17 UDP User Datagram Protocol (RFC 768)
41 IPv6 IPv6 tunneled over IPv4 (RFC 2473)
83 VINES Banyan Vines IP
89 OSPF Open Shortest Path First (RFC 1583)
132 SCTP Streams Control Transmission Protocol
The Header Checksum field (16 bits). The 16-bit one’s complement of the one’s complement sum of all 16 bit words in the header.
The Source Address field (32 bits) contains the IPv4 address of the sender (may be modified by NAT).
The Destination Address field (32 bits) contains the IPv4 address of the recipient (may be modified by NAT in a reply packet).
Options (0 to 40 bytes) Not often used. Rarely if ever seen “in the wild”. These are not relevant here. If you want the details, read the RFCs.

## Slide 160: IPv4 Limitations
Limited number of IP addresses (4 billion)
No provision for authentication
Security issues
No provision for routing
Does not work well with large networks
Notes: 4 billion addresses, but more than 7 billion people with multiple devices

## Slide 161: Common Internet protocols
  TCP/IP (Transmission Control Protocol/Internet Protocol) is a stream protocol.
  Any data transmitted between these two endpoints is guaranteed to arrive, thus it is a so-called lossless protocol.
  It is also called a peer-to-peer protocol.
TCP/IP
  HTTP (HyperText Transfer Protocol) is the protocol used to transmit all data present on the World Wide Web.
  It is the protocol used to transmit HTML, the language that makes all the fancy decorations in your browser. It works upon TCP/IP.
HTTP
  FTP (File Transfer Protocol) is the protocol used to transmit files between computers connected to each other by a TCP/IP network, such as the Internet
FTP
  UDP (User Datagram Protocol) is one of the core members of the Internet protocol suite.
  UDP uses a simple connectionless communication model with a minimum of protocol mechanisms.
UDP
Notes: TCP/IP (Transmission Control Protocol/Internet Protocol) is a stream protocol. This means that a connection is negotiated between a client and a server. Any data transmitted between these two endpoints is guaranteed to arrive, thus it is a so-called lossless protocol. Since the TCP protocol (as it is also referred to in short form) can only connect two endpoints, it is also called a peer-to-peer protocol.
HTTP (HyperText Transfer Protocol) is the protocol used to transmit all data present on the World Wide Web. This includes text, multimedia and graphics. It is the protocol used to transmit HTML, the language that makes all the fancy decorations in your browser. It works upon TCP/IP.
FTP (File Transfer Protocol) is the protocol used to transmit files between computers connected to each other by a TCP/IP network, such as the Internet
UDP (User Datagram Protocol) is one of the core members of the Internet protocol suite. UDP uses a simple connectionless communication model with a minimum of protocol mechanisms

## Slide 162: The TCP/IP Protocol Suite
Ethernet
IP
TCP &UDP
SMTP, FTP, HTTP, POP3, IMAP4, SNMP
A protocol suite is a collection of protocols that are designed to work together
Application
Application
Presentation
Session
Transport
Networking
Datalink
Physical
Datalink and Physical
Transport
Networking
OSI
TCP/IP
Protocols
Notes: Note: The OSI model is an idealised networking model, whereas the TCP/IP model is a practical implementation.
What is important to understand is that the interfaces between the interfaces are well defined so that it is theoretically possible to replace a particular protocol with another one that operates at that level.
For example you should theoretically be able to replace the IP networking protocol with the IPX networking protocol without affecting how the application e.g. POP3 works.
Although this doesn’t always apply the application protocols like SMTP ,POP3 etc will work Okay across different data link protocols like Ethernet,Token ring etc.

## Slide 163: Internetworking
Internetworking is the process or technique of connecting different types of networks by using intermediary devices such as routers or gateway devices in order to exchange packets
Internetworking ensures data communication among networks owned and operated by different entities using a common data communication and the Internet Routing Protocol
An internetworking device is a widely-used term for any hardware within networks that connect different network resources
Key devices that comprise a network are routers, bridges, repeaters and gateways

## Slide 164: IPv4 Addressing
IP addresses are 32-bit binary values: for readability purposes they're usually written as four octets in dotted decimal location
It's not just a serial number though: each address has two parts
The network ID identifies a unique subnet on the wider network, while the host ID identifies a specific host on that subnet.
192.168.
133.178
Network ID
Host ID
Notes: IP addresses are 32-bit binary values: for readability purposes they're usually written as four octets in dotted decimal location. It's not just a serial number though: each address has two parts
The network ID identifies a unique subnet on the wider network, while the host ID identifies a specific host on that subnet.

## Slide 165: IPv4 addresses (Cont.)

## Slide 166
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Intro
Monday
Tuesday
Wednesday
Thursday
Friday

## Slide 167: Classful and classless addressing
Classless interdomain routing (CIDR)
Class | First octet | First bits | # of subnets | # of hosts | Subnet mask | Mask prefix
A | 0.-127. | 0 | 128 | 16,777,216 | 255.0.0.0 | /8
B | 128.-191. | 10 | 16,384 | 65,536 | 255.255.0.0 | /16
C | 192.-223. | 110 | 2,097,152 | 256 | 255.255.255.0 | /24
D | 224.-239. | 1110 | * | * | * | *
E | 240.-254. | 1111 | * | * | * | *

## Slide 168: Problems with class-based IP addressing
The classful routing system included classes A, B, and C:
Class A - Over 16 million host identifiers
Class B - 65,535 host identifiers
Class C - 254 host identifiers
The old method of IP addressing came with inefficiencies that exhausted the availability of IPv4 addresses faster than it needed to
Notes: The problem would commonly occur when an organization required more than 254 host machines and therefore would no longer fall into class C but rather class B.
This means that the organization would use a class B license even though they had far less than 65,535 hosts.
Therefore if an organization only required 2,500 hosts, they would be wasting about 63,000 hosts by holding a class B license which would greatly decrease the availability of IPv4 addresses unnecessarily.

## Slide 169: Classless interdomain routing (CIDR)
An IP addressing scheme that improves the allocation of IP addresses
It replaces the old system based on classes A, B, and C
This scheme also helped greatly extend the life of IPv4 as well as slow the growth of routing tables
Notes: How does CIDR work?
CIDR is based on variable-length subnet masking (VLSM). This allows it to define prefixes of arbitrary lengths making it much more efficient than the old system. CIDR IP addresses are composed of two sets of numbers. The network address is written as a prefix, like you would see a normal IP address (e.g. 192.255.255.255). The second part is the suffix which indicates how many bits are in the entire address (e.g. /12). Putting it together, a CIDR IP address would look like the following:
192.255.255.255/12

## Slide 170: Map of Regional Internet Registries

## Slide 171: Variable-length subnet masking
The simplest way to subnet is to use fixed length subnet masking (FLSM), which divides a network into multiple subnets with the same mask prefix number.
The alternative is variable length subnet masking (VLSM), which allows you to subnet a network in multiple "passes", breaking it into subnets of variable size and thus variable subnet length.

## Slide 172: Variable Length Subnets
Say we have a Network of
Wan1
WAN2
LAN 1 – 75 Hosts
LAN 2 – 50 Hosts
Mask | 128 | 192 | 224 | 240 | 248 | 252 | 254 | 255
Bits | /25 | /26 | /27 | /28 | /29 | /30 | /31 | /32
Hosts | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Subnets | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
Notes: IP Range is 192.168.1.0/24 [Write the 192.168.1.0/24 onto board on the WAN link
We need to split this into 3 subnets
The table shows what subnets we can divide the current /24 into by using the remaining bits

## Slide 173: Special IPv4 addresses
0.0.0.0 is a non-routable address which can either mean the current network, the default route, any address at all, or a specific error condition, depending on context.
255.255.255.255 is the broadcast address to the currently configured subnet.
The entire Class A network 127.0.0.0 is reserved for loopback addresses, which as the name implies simply point right back to the local host.

## Slide 174: Special IPv4 addresses
Three private network ranges are defined for internal LANs.
The 169.254.0.0/16 network is reserved for link-local or automatic Private IP addressing (APIPA) addresses.
  10.0.0.0/8, or the single Class A network with addresses 10.0.0.0 - 10.255.255.255
  172.16.0.0/12, or the 16 contiguous Class B networks with addresses 172.16.0.0 - 172.31.255.255.
  192.168.0.0/16, or the 256 contiguous Class C networks with addresses 192.168.0.0 - 192.168.255.255.

## Slide 175: IPv4 subnetting
The main things to remember are that every IPv4 address is split into network ID and host ID, that each part consists of a contiguous series of bits in the binary address, and that both together are 32-bits
When you subnet an address, that means you borrow bits from the host ID portion, meaning fewer possible hosts, in exchange for making more subnets.

## Slide 176: IPv6 Addressing
Internet Protocol v6 - 128-bit address
340,282,366,920,938,463,463,374,607,431,768,211,456 addresses (340 undecillion)
6.8 billion people could have 5,000,000,000,000,000,000,000,000,000 addresses each

## Slide 177: IPv6 Address Compression
Your DNS will become very important!
Groups of zeros can be abbreviated with a double colon ::
Only one of these abbreviations allowed per address
Leading zeros are optional

## Slide 178: IPv6
IPv6 uses a 128-bit address: this allows 2128 addresses
It allows easier network configuration, more efficient routing and data flow, and even improved security
The primary drawback is that it's a much different protocol from IPv4 and isn't backwards-compatible

## Slide 179: IPv6 addresses
Instead of dotted decimal, they're written as 32 hexadecimal digits, broken into eight groups of four separated by colons
fe80:0000:0000:0000:c249:3765:00c0:9b22

## Slide 180: Ipv6 Rules
Leading zeros in a group don't need to be displayed, so :00c0: can be displayed as :c0: instead.
A group consisting entirely of zeros can be displayed as :0:
Once per address, multiple consecutive groups of zeros can be replaced with a double-colon.
This means :0000:0000:0000: can be written as :: instead.
Using this method, the same address could be written as follows:
fe80::c249:3765:c0:9b22

## Slide 181: IPv6 Addresses (Cont.)
In a typical IPv6 address, the first 64 bits is the network prefix, while the last 64 bits is the device identifier
Global Routing Prefix
Subnet ID
Device Identifier
fe80 : d18 : 0000
: 12c0 :
5d18 : cffd : 0000 : fef3
128 bits = 16 bytes
16 bits
2 bytes
2 octets
=
=
Network
Node
Notes: In a typical IPv6 address, the first 64 bits is the network prefix, while the last 64 bits is the device identifier.
This can be divided into:
a global routing prefix
A subnet ID
And a device identifier

## Slide 182: IPv6 Address Types & Scope
Three
types
Global Unicast Address
Unique Local
Link Local
Scope Internet
Routed on Internet
Scope Internal
Network or VPN internally routable, but NOT routed on Internet
Scope network link
Not Routed internally or externally
Notes: IPv6 addresses have three types:
Global Unicast Address –Scope Internet- routed on Internet
Unique Local — Scope Internal Network or VPN internally routable, but Not routed on Internet
Link Local – Scope network link- Not Routed internally or externally.

## Slide 183: IPv6 Addressing - Global and Public Addresses
  These addresses are known as global Unicast addresses and are the equivalent of the public addresses of IPv4 networks
  The Internet authorities allocate address blocks to ISPs who in turn allocate them to their customers
Global addresses are routable on the internet and start with 2001
Notes: Global and Public Addresses
Global addresses are routable on the internet and start with 2001:
These addresses are known as global Unicast addresses and are the equivalent of the public addresses of IPv4 networks.
The Internet authorities allocate address blocks to ISPs who in turn allocate them to their customers.

## Slide 184: IPV6 Task
Compression
fd00:0040:0000:c298:0000:0000:0000:c200
fd19:0b00:0100:0000:0000:0001:0000:001c
fd00:0000:0005:0700:0083:002c:8200:0000
Expansion
fd00:11:83:0:1022:8a:c4:0
fd00:9100:20::
fd10:10:0:604a::4000:0
Notes: Compress the first IP range
Rules
[First Octect must be wrote fully}
Any octet after the start that starts with a 0 followed by a letter or number can be wrote without the zeros Example
Any contiguous 0000:0000:0000 can be wrote as :: for example FD00:0000:0000:0001 can be FD00::1
Any 0000:0000 after a :: can be wrote as FD00::ABCD:0:1
Use an example of fd00:0000:0000:0041:0000:4300:0004:0000 {answer is fd00::41:0:4300:4:0}
1st Answer = fd00:40:0:c298::c200
2nd Answer = fd19:b00:100::1:0:1c
3rd Answer = fd00:0:5:700:83:2c:8200:0
4th Answer = FD00:0011:0083:0000:1022:008a:00c4:0000
5th Answer = fd00:9100:0020:0000:0000:0000:0000:0000
6th Answer = fd10:0010:0000:604a:0000:0000:4000:0000

## Slide 185: 1.5 Compare and contrast the characteristics of network topologies, types and technologies
Wired topologies
  Logical vs. physical
  Star
  Ring
  Mesh
  Bus
Wireless topologies
  Mesh
  Ad hoc
  Infrastructure
Types
  LAN
  WLAN
  MAN
  WAN
  CAN
  SAN
  PAN
Technologies that facilitate the Internet of Things (IoT)
  Z-Wave
  Ant+
  Bluetooth
  NFC
  IR
  RFID
  802.11

## Slide 186
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Intro
Monday
Tuesday
Wednesday
Thursday
Friday

## Slide 187: Topologies
A term used in the description of the schematic depiction of the arrangement of a network
It is used to describe the various ways in which nodes are connected

## Slide 188: Topologies: Bus
A bus network is an arrangement in a local area network (LAN) in which each node (workstation or other device) is connected to a main cable or link called the bus
Simple and reliable
Transmission of data in only one direction
If one node fails to operate, all the rest can still communicate with each other
For a major disruption to take place, the bus itself must be broken somewhere
Bus networks are easy to expand
Additional nodes can be added anywhere along the bus

## Slide 189: Topologies - Bus
There are several limitations to the bus network topology
The length of the bus is limited by cable loss
A bus network may not work well if the nodes are located at scattered points that do not lie near a common line
  In situations like this, a ring network, mesh network, or star network may prove more flexible and more cost effective
Requires terminators
Limited to 10Mbps

## Slide 190: Topologies - Bus
Advantages of the Bus Topology
  The bus topology as we know it is very cost-effective
  This topology system makes use of the least amount of cable, unlike the others
  This is sufficient for small networks
  A layperson can easily understand this system
  You can also quickly expand on this network

## Slide 191: Topologies - Bus
Disadvantages of the Bus Topology
  Once there is a problem in one part of the cable, the whole network is down
  At the advent of traffic on the network, the entire network will have a slowed-down performance
  Collisions occur in the network resulting in packet loss
  There is a limit to the strength of the cable
  This topology is not as speed effective as the ring topology
  It is difficult to isolate faults in the network

## Slide 192: Topology - Bus
https://www.bbc.co.uk/bitesize/guides/z7mxh39/revision/6

## Slide 193: Topologies: Star
Star topology (or ‘star network’) is the most widely used network for LANs
First popularized by ARCnet, before being adopted by Ethernet
Each node (such as a computer or printer) within the company or team is connected to one central network device (which could be a hub, a switch, or a computer) via a cable
When the nodes (or computers) want to communicate with each other, they pass the message on to the central server hub, which then forwards that message back on to the different nodes

## Slide 194: Topologies: Star
Advantages of a Star topology
  If one node or connection breaks, the rest of the network remains unaffected
  Other computers and their connections can continue working with zero downtime
  It’s highly scalable: new computers/machines can be added or removed without disturbing the whole network
  Star networks can accommodate lots of different machines, which means it’s possible to create a large network
  Star networks are safer in the event of a cyber attack
Notes: Star networks are safer in the event of a cyber attack. Let’s say you run a bank with several branches. If one branch or office comes under attack, the server will be notified and prevent a second. One branch goes down, but the others continue running in complete safety

## Slide 195: Topologies: Star
Disadvantages of a Star topology
  Each cable is individually connected to the central node, which means you’re going to need A LOT of cables
  The hub (central node) is a single point of failure, which means that if it stops, it brings the whole lot down
  In reality, there are only so many machines you can connect to a central server before you start running out of cable length and ports
Notes: Each cable is individually connected to the central node, which means you’re going to need A LOT of cables
And that doesn’t come cheap. Although it’s worth noting that the upfront cost of cables is a fraction of the cost of downtime in the event of a total system failure. Most network designers think this benefit far outweighs the cable cost.
The hub is a single point of failure, which means that if it stops, it brings the whole lot down.
In reality, there are only so many machines you can connect to a central server before you start running out of cable length and ports. One way to get around this is to extend the star topology into multiple stars with a new central server in the middle. In this situation, messages from each system are transferred to its star, which then transfers it to the core server, then back out to the star and then to the destination system.

## Slide 196: Topologies: Ring
Computers are connected to each other in a circular format
Every device in the network will have two neighbours and no more or no less
Ring topologies were commonly used in the past but you would be hard pressed to find an enterprise still using them today
The first node is connected to the last node to link the loop together
As a consequence of being laid out in this format packets need to travel through all nodes on the way to their destination
Within this topology, one node is chosen to configure the network and monitor other devices
Ring topologies are half-duplex but can also be made full-duplex
To make ring topologies full-duplex you would need to have two connections between network nodes to form a Dual Ring Topology

## Slide 197: Topologies: Ring
Disadvantages of a ring topology:
  If any of the nodes fail, the ring is broken and data cannot be transmitted
  It is difficult to troubleshoot a ring network topology
  Because all nodes are wired together, the network must be temporarily stopped to add additional nodes

## Slide 198: Topologies: Ring
Advantages of a ring topology:
  Data passes around the network in one direction, there are no network collisions
  Adding additional nodes has very little impact on bandwidth

## Slide 199: Topologies: Ring
Single – half-duplex
Dual – full-duplex

## Slide 200: Topologies - Ring

## Slide 201: Topologies: Mesh
Each computer and network device is interconnected with one another, allowing for most transmissions to be distributed even if one of the connections go down
It is a topology commonly used for wireless networks
Each node has a dedicated point-to-point link to every other node
A fully connected mesh network having ‘n’ number of nodes has a total of n(n-1)/2 number of links
Example: 6 nodes = (6(6-1))/2 = 15 links

## Slide 202: Topologies - Mesh
Full Mesh
  Every node has a circuit connecting it to every other node in the network
  Yields greatest redundancy, so if one node fails, network traffic can be redirected to any of the other nodes
  Usually reserved for backbone networks since it is very expensive

## Slide 203: Mesh

## Slide 204: Topologies - Mesh
Partial Mesh
  Some nodes are organized in a full mesh scheme but others are only connected to 1 or 2 in the network
  Common in peripheral networks connected to a full meshed backbone
  Less expensive to implement
  Yields less redundancy

## Slide 205: Partial Mesh
Notes: Nodes 1 and 2 are connected to every other node

## Slide 206: Topologies: Ad Hoc or Hybrid
No pre-existing infrastructure
Devices communication amongst themselves
Can be a mixture of topologies
Multiple physical topologies are combined to form one large network
Each topology has its own strengths and weakness
Objective: total strength improves the network performance

## Slide 207: Topologies: Infrastructure
All devices communicate through an access point
The most common wireless communication mode

## Slide 208: Topologies: Wireless Mesh
Advantages
  Scalability
  Robustness
  Redundancy
Notes: . Scalability
One of the advantages of a mesh topology is that (in theory) you don’t need to add routers to the network, as each node can act as a router. If you’re working on a mesh network for the lighting in your office building, and you want to add a light in a particular room, you should be able to add the light and have it automatically connect to the network. There isn’t a lot of extra management that needs to happen, which makes the network scalable.
2. Robustness
Another benefit of a mesh network topology is that if one of the nodes goes down, it doesn’t necessarily bring the entire network down. The network can heal itself around a bad node if other nodes can complete the mesh. Additionally, if you need to get more range out of a mesh system, you can add another node and the messages can hop through the mesh back to the gateway—which is why some believe mesh networks are more robust.
Because all nodes in a mesh are receiving and translating information, there is some redundancy in a mesh topology; however, you can also gain speed with the excess bandwidth. If one route happens to be slow, a mesh network could potentially find a better route and optimize itself.

## Slide 209: Topologies: Wireless Mesh
Ad hoc devices work together to form a mesh “cloud”
Self form and self heal

## Slide 210: Topologies: Wireless Mesh
Disadvantages
  Complexity
  Network Planning
  Latency
  Power Consumption
Notes: Disadvantages Of A Mesh Topology
1. Complexity
Each node needs to both send messages as well as act as a router, which causes the complexity of each node to go up pretty significantly. Let’s say you’re making a small, low-power device—like a room occupancy sensor—and you are looking to get better range out of your system. The nodes have to now keep track of messages from five or 10 of their ‘neighbors,” which exponentially increases the amount of data that node has to deal with in order to pass along a message. Thus, if you add additional sensors to the mesh just to benefit the range, you’re naturally making the system more complex.
2. Network Planning
As we mentioned previously, mesh networks are often considered highly scalable, and adding a node to the network typically isn’t very involved. But planning the network as a whole is a different story. Let’s say you have poor latency in one area of your building (which we’ll discuss below), and you need a particular light to turn on faster than it currently turns on. With a mesh network, you’d need to add a dedicated node that only forwards messages. But this complicates your network planning, because you now have to deploy a piece of equipment just to get your messages properly routed in a reasonable amount of time.
3. Latency
As mentioned, latency—the time it takes a message to get from a node to the gateway—can impact your mesh network planning. Interestingly, you may improve some latency by using a mesh network with a larger scale system with more bandwidth, memory, and power. But latency becomes an issue in smaller low power, wide-area networks (LPWANs) because it doesn’t have the processing capability to handle the messaging. Thus, if you have a WiFi mesh, messages will likely be translated much quicker than a ZigBee mesh. This is something to consider based on the protocol you’ll be using and the latency your application requires.
4. Power Consumption
Because each node in a mesh has to act as an endpoint and a router, it has to draw more power to operate. Thus, if you have battery-powered, low-power nodes, a mesh may be difficult to deploy without a lot of network planning.
Let’s say you have battery-powered nodes in windows and doors for your smart security system. The customer keeps the control panel in the basement, but all of the sensors are on the first and second floor. So while a second-floor window may be low power, because it only transmits messages, the sensors on the first floor will have to handle messages from the second floor windows and doors. In other words, you’re compounding the amount of data each node has to handle in a mesh, and so batteries on some nodes are likely to die faster.

## Slide 211: Physical and Logical Topology
Physical topology defines how the systems are physically connected
Logical Topology - How devices are connected to the network through the actual cables that transmit data
The logical topology defines how the systems communicate across the physical topologies

## Slide 212: NETWORK TOPOLOGY (LOGICAL TOPOLOGY)

## Slide 213
Each computer connects
to the central hub
Inside, the ports of the hub are wired in a circle. Data packets travels in a ring – not as a star!
Physical – Logical Topology

## Slide 214: Infrastructure and design
We define the structure of our networks based on the reach and functionality of the data flows
Here you’ll learn about WAN, MAN, LAN, WLAN, PAN, SCADA, and Medianet infrastructures.

## Slide 215: WAN
Wide Area Network
A Wide Area Network (WAN) is where the workstations are 'further apart' from each other compared to a LAN
For example, the computers may be spread out over a town, a country or the world (like the Internet is).
WANs are usually a number of LANs that are connected up over some distance
The connections are frequently made using the normal telephone cables but they might involve fibre optic connections, wireless, microwave or satellite, for example

## Slide 216: LAN
A Local Area Network (LAN) is a network where the workstations are 'close' together
It isn't strictly defined in terms of an exact distance but it is usually thought of as computers in the same room, or building or even in a number of buildings which are next to each other, such as a school or hospital
The different parts of the network might be connected together using wireless signals or they may be physically connected together using cables such as a type known as CAT 5 or using a fibre optic cable.

## Slide 217: LAN
With computers and computer equipment connected together in a LAN, users can do a number of things:
  They can log on using a login name and password - this stops unauthorised users from getting access to the network.
  They can use any computer on the LAN, even if their most convenient one isn't working.
  They can easily share files and resources with other users. You only need one printer for all the users, for example.
  They can easily communicate with other users in their organisation by sending them email or by using an internal Internet known as an Intranet. Intranets are like the Internet but they are only accessible by people in the organisation. Using the Intranet, you can send messages, set up bulletin boards, web pages

## Slide 218: Differences between LANs and WANs
LANs are spread over a smaller area whereas WANs are spread over a larger area
WANs are usually made up of LANs connected together
LANs are usually much faster than WANs
LANs can usually send much bigger volumes of data in a second (known as 'bandwidth') than a WAN
Users generally share hardware on a LAN
On a WAN, however, the focus is all on communicating and sharing data

## Slide 219: MAN
A metropolitan area network (MAN) is a computer network that interconnects users with computer resources in a geographic region of the size of a metropolitan area

## Slide 220: WLAN
A wireless LAN (WLAN) is a wireless computer network that links two or more devices using wireless communication to form a local area network (LAN) within a limited area such as a home, school, computer laboratory, campus, or office building
This gives users the ability to move around within the area and remain connected to the network
Through a gateway, a WLAN can also provide a connection to the wider Internet
Most modern WLANs are based on IEEE 802.11 standards and are marketed under the Wi-Fi brand name
Wireless LANs have become popular for use in the home, due to their ease of installation and use
They are also popular in commercial properties that offer wireless access to their employees and customers

## Slide 221: PAN
A PAN is a Personal Area Network
This is a network that revolves around one person or a small group of people
For example, it might involve just a laptop, a phone and perhaps some wearable technology
PANs can be wired but often, they are wireless networks
The most common wireless technology used to create a PAN is Bluetooth but other wireless technologies can be used, such as infra-red or NFC
The typical radius of a PAN is only about 10 metres so it is very much a network for use in a small area

## Slide 222: SCADA
SCADA is an acronym for supervisory control and data acquisition, a computer system for gathering and analysing real time data
SCADA systems are used to monitor and control a plant or equipment in industries such as telecommunications, water and waste control, energy, oil and gas refining and transportation.

## Slide 223: SCADA

## Slide 224: MediaNet
A medianet is a network optimized for rich media - not only voice and video, but the mixing together of videos and documents, webpages, text, and many other forms of media
The applications must be able to query the network for services and information in order to offer users a better experience

## Slide 225: 1.6 Given a scenario, implement the appropriate wireless technologies and configurations
802.11 standards
  a
  b
  g
  n
  ac
Cellular
  GSM
  TDMA
  CDMA
Frequencies
  2.4GHz
  5.0GHz
Speed and distance requirements
Channel bandwidth
Channel bonding
MIMO/MU-MIMO
Unidirectional/omnidirectional
Site surveys

## Slide 226: Wireless
Uses radio to connect network nodes
  Avoids costly cabling
  Works at the physical layer (1)
Bluetooth, NFC, Wi-Fi or Cellular (GSM)
Bluetooth
  Low power, short range
  Mice, keyboards, smartphone, headsets
  Built into OS
NFC (Near field communication)
  4cm range
  Contactless payment (smartphone)
  Data sharing(smartphone)

## Slide 227: Wi-Fi
 | 802.11 | 802.11a | 802.11b | 802.11g | 802.11n | 802.11n IEEE Specification | 802.11ac Wave 1 | 802.11ac Wave 2 | 802.11ac IEEE Specification | 802.11ax
Band | 2.4GHz | 5.8GHz | 2.4GHz | 2.4GHz | 2.4GHz and 5GHz | 2.4GHz and 5GHz | 5GHz | 5GHz | 5GHz | 2.4GHz and 5GHz
Max Speed | 1.2Mbps | 54Mbps | 11Mbps | 54Mbps | 450Mbps | 600Mbps | 1.3Gbps | 2.34GHz – 3.47GHz | 6.9GHz | 10Gbps
MIMO | Single User | Single User | Single User | Single User | Single User | Single User | Single User | Multi User | Multi User | Multi User

## Slide 228: 1.7 Summarize cloud concepts and their purposes
Types of services
  SaaS
  PaaS
  IaaS
Cloud delivery models
  Private
  Public
  Hybrid
Connectivity methods
Security implications/considerations
Relationship between local and cloud resources

## Slide 229: Types of Services
  SAAS
  PAAS
  IAAS

## Slide 230: Cloud Infrastructure as a Service (IaaS)
Provides processing, storage and networks
The consumer is able to deploy and run arbitrary software, which can include operating systems and applications
The consumer does not manage or control the underlying cloud infrastructure, but has control over
  operating systems
  storage
  deployed applications
  selected networking components (e.g., host firewalls)
Examples are:
  Microsoft Azure
  Amazon Web Services
  Google Cloud

## Slide 231: Cloud Infrastructure as a Service (IaaS)

## Slide 232: Cloud Platform as a Service (PaaS)
The consumer deploys onto the cloud infrastructure consumer-created or acquired applications created using programming languages and tools supported by the provider
The consumer does not manage or control the underlying cloud infrastructure but has control over the deployed applications
Examples are:
  server space for web pages such as Rackspace or GoDaddy
  Google App engine

## Slide 233: Cloud Platform as a Service (PaaS)

## Slide 234: Cloud Software as a Service (Saas)
The ability to use the provider’s applications running on a cloud infrastructure
The applications are accessible from various client devices through a thin client interface, such as a Web browser
The consumer does not manage or control the underlying cloud infrastructure including network, servers, operating systems, storage, or even individual application capabilities
Examples are: Google Docs, Office365, Gmail, Dropbox, Slack

## Slide 235: Cloud Software as a Service (Saas)

## Slide 236: Cloud Delivery Models
Public
Private
Community
Hybrid

## Slide 237: Public Cloud
The cloud infrastructure is provisioned for open use by the general public
It may be owned, managed, and operated by a business, academic, or government organization, or some combination of them
It exists on the premises of the cloud provider
Under most circumstances, a public cloud is owned by the cloud provider, and it uses a pay-as-you-go model
A good example of a public cloud is webmail or online document sharing/collaboration

## Slide 238: Private Cloud
The cloud infrastructure is provisioned for exclusive use by a single organization comprising multiple consumers (e.g., business units). It may be owned, managed, and operated by the organization, a third party, or some combination of them, and it may exist on or off premises
Under most circumstances, a private cloud is owned by the organization, and it acts as both the provider and the consumer
It has a security-related advantage in not needing to put its data on the Internet

## Slide 239: Hybrid Cloud
The cloud infrastructure is a composition of two or more distinct cloud infrastructures (private, community, or public) that remain unique entities, but are bound together by standardized or proprietary technology that enables data and application portability (e.g., cloud bursting for load balancing between clouds)
A hybrid can be any combination of other delivery models
Not only are public and private listed in the definition, but also community

## Slide 240: Community Cloud
CompTIA no longer includes the community cloud delivery model on the Network+ exam (but does require you to know it for its cloud-focused certifications)
For real-world purposes, you should know that the key to distinguishing between a community cloud and other types of cloud delivery is that it serves a similar group
There must be joint interests and limited enrolment

## Slide 241: Connectivity Methods
Most cloud providers offer a number of methods that clients can employ to connect to them
It is important, before making an investment in infrastructure, to check with your provider and see what methods it recommends and supports

## Slide 242: Connectivity Methods
One of the most common is to use an IPsec, hardware VPN connection between your network(s) and the cloud providers
This method offers the capability to have a managed VPN endpoint that includes automated multidata centre redundancy and failover
A dedicated direct connection is another, simpler, method
You can combine the dedicated network connection(s) with the hardware VPN to create a combination that offers an IPsec-encrypted private connection while also reducing network costs

## Slide 243: IPSec and VPN
IPSec Internet Protocol Security
  Encrypts IP packets
  VPNs use IPSec to establish and run encrypted connections
  Adds headers and trailers to the packet data payload (50-60 bytes), may require MTU adjustments
  Authenticates each packet
  Uses UDP to get through firewalls
  In tunnel mode the original IP addresses are encrypted and new IP headers added. The tunnel exists between the source and destination routers
  In transport mode the original IP headers are in the clear
  IPSec uses port 500

## Slide 244: Security Implications/Considerations
Security is one of the most important issues to discuss with your cloud provider
Cloud computing holds great promise when it comes to scalability, cost savings, rapid deployment, and empowerment
When so much control is removed risks are involved
Each risk should be considered carefully to identify ways to help mitigate it
The responsibilities of both the organisation and the cloud provider vary depending on the service model chosen
Ultimately the organisation is accountable for the security and privacy of the outsourced service
Notes: Security is one of the most important issues to discuss with your cloud provider.
Cloud computing holds great promise when it comes to scalability, cost savings, rapid deployment, and empowerment.
As with any technology where so much is removed from your control, though, risks are involved.
Each risk should be considered carefully to identify ways to help mitigate it.
Naturally, the responsibilities of both the organization and the cloud provider vary depending on the service model chosen, but ultimately the organization is accountable for the security and privacy of the outsourced service.

## Slide 245: Relationship Between Local and Cloud Resources
Cloud offers the ability to store more and more data on it and to let a provider worry about scaling issues instead of local administrators
From an economic perspective, this can be a blessing
From an administrative point, though, it can present some issues
To minimise problems, be sure that files are kept current, and synchronisation between local and remote files is always running

## Slide 246: 1.8 Explain the functions of network services
DNS service
  Record types
  A, AAAA
  TXT (SPF, DKIM)
  SRV
  MX
  CNAME
  NS
  PTR
Internal vs. external DNS
Third-party/cloud-hosted DNS
Hierarchy
Forward vs. reverse zone
DHCP service
  MAC reservations
  Pools
  IP exclusions
  Scope options
  Lease time
  TTL
  DHCP relay/IP helper
NTP
IPAM

## Slide 247: DHCP
A DHCP server dynamically assigns an IP address
Dynamic Host Configuration Protocol (DHCP) is a network management protocol
A DHCP server enables computers to request IP addresses and networking parameters automatically from the Internet service provider (ISP)
In the absence of a DHCP server, a computer or other device on the network needs to be manually assigned an IP address, or to assign itself an APIPA address
Notes: Dynamic Host Configuration Protocol (DHCP) is a network management protocol used on Internet Protocol (IP) networks, whereby a DHCP server dynamically assigns an IP address and other network configuration parameters to each device on the network, so they can communicate with other IP networks.
A DHCP server enables computers to request IP addresses and networking parameters automatically from the Internet service provider (ISP), reducing the need for a network administrator or a user to manually assign IP addresses to all network devices.[1] In the absence of a DHCP server, a computer or other device on the network needs to be manually assigned an IP address, or to assign itself an APIPA address, the latter of which will not enable it to communicate outside its local subnet.

## Slide 248: DHCP
The DHCP server assigns addresses using leases, which are temporary but renewable assignments
Addresses can be assigned dynamically, or by reservation
Assigned addresses are leased for a fixed amount of time, after which they must be renewed
Lease time can be configured on the server
The DHCP server can assign additional network settings, called DHCP options.
When a DHCP client connects to the network, it looks for a DHCP server using a broadcast packet
If a DHCP server is not on the client's local segment, routers can be configured as DHCP relay agents

## Slide 249: The DHCPv4 Leasing Process
Client
DHCP Server
DHCPDISCOVER
DHCPOFFER
DHCPACKNOWLEDGE
DHCPREQUEST
Time
Notes: Each message may be either a broadcast or a unicast, depending on the DHCP client capabilities.

## Slide 250: DHCP process
Step 1:
Discover - Client to DHCP Server
Step 2:
Offer - DHCP Server to client
Step 3:
Request - Client to DHCP Server
Step 4:
Acknowledgment - DHCP Server to client
Find all of the available DHCP Servers
Send some IP address options to the client
  DHCP server sends an acknowledgment to the client
  Client chooses an offer and makes a formal request

## Slide 251: The DHCPv6 leasing process
DHCPv6 uses a DHCP Unique Identifier (DUID) for address allocations and client/server identification during the leasing process
DHCPv6 allows two configuration methods, stateless and stateful

## Slide 252: APIPA
APIPA is short for Automatic Private IP Addressing
A feature of Windows operating systems, meant for non-routed small business environments, usually less than 25 clients
With APIPA, DHCP clients can automatically self-configure an IP address and subnet mask
Used when a DHCP server isn't available
IP address range (from 169.254.0.0 - 169.254.255.255)
Reserved by the Internet Assigned Numbers Authority (IANA) for that purpose
Notes: APIPA is short for Automatic Private IP Addressing, a feature of Windows operating systems, meant for non-routed small business environments, usually less than 25 clients
With APIPA, DHCP clients can automatically self-configure an IP address and subnet mask when a DHCP server isn't available.
The computer selects an IP address from a range of addresses (from 169.254.0.0 - 169.254.255.255) reserved by the Internet Assigned Numbers Authority (IANA) for that purpose

## Slide 253: APIPA
If a system that does not support APIPA cannot get an address from a DHCP server, it typically assigns itself an IP address of 0.0.0.0.
Keep this in mind when troubleshooting IP addressing problems on non-APIPA platforms

## Slide 256: Configuring DHCP
DHCP configuration is relatively straightforward
Server exclusions can be set up

## Slide 257: Scope properties
IP address range
  And excluded addresses
Subnet mask
Lease durations
Other scope options
DNS server, default gateway, WINS server

## Slide 258: DHCP Pools
Grouping of IP addresses
Each subnet has its own scope
192.168.1.0/24, 192.168.2.0/24, 192.168.3.0/24, etc.
A scope is generally a single contiguous pool of IP addresses
DHCP exceptions can be made inside of the scope

## Slide 259
A range of addresses to be reserved for allocation

## Slide 261: IPAM systems
IP address management (IPAM) software that integrates DNS and DHCP and allows you to centrally manage both services across your network.
  Keeping an inventory of IP address pools and subnets, both for DHCP and static addresses.
  Keeping an inventory of available host and domain names.
  Tracking current DHCP and DNS assignment.
  Keeping DHCP and DNS services aware of each other's status. For example, if a named host has its IP address changed, IPAM can make sure the host name points to the new IP address.

## Slide 262
01
02
05
03
04
06
Understanding & Troubleshooting Networking
Intro
Monday
Tuesday
Wednesday
Thursday
Friday